## Slide 1
3GPP TSG-RAN #63 RP-140418
Fukuoka, Japan, 3-6 March, 2014
Document for: Discussion
Agenda Item: 14.1.1
Motivation for new WI proposal: Scalable Bandwidth UMTS
By Filtering
China Unicom

## Slide 2: Deployment Scenarios and Use Cases
Standalone Scalable UMTS
  Band VIII: 3.6MHz GSM+ 2.4MHz S-UMTS
  Transitional period of refarming GSM system
  Deploy specific use cases such as small cell and MTC
Carrier aggregation of Scalable UMTS with UMTS
  Band VIII: 5MHz UMTS+ 1.25MHz S-UMTS
  For GSM refarming requirement and increase the feasibility of UMTS system
  Use case: hotspot capacity requirement
S-UMTS
UMTS
5 MHz
1.25 MHz
Band VIII 6MHz

## Slide 3: Motivation
Filtering solution has been studied since RAN1#74bis meeting
Scalable bandwidth UMTS by filtering is intended to completed at RAN#62
Good progress has been achieved at RAN1#76 and package CR to TR25.701 compiling the agreed changes to a single CR has been approved
It is proposed to start a WI targeting Rel-12

## Slide 4: Objective (1/2)
Define the support for Scalable Bandwidth UMTS by Filtering for the HSDPA carrier aggregation operation mode
  Based on the chip zeroing filtering solution
Define the support for Scalable Bandwidth UMTS by Filtering for the standalone narrow-band operation, focusing on 2.5MHz bandwidth (supporting both voice and data services)
  After selecting one suitable solution among basic filtering (no chip zeroing) and chip zeroing filtering

## Slide 5: Objective (2/2)
Define the support of Scalable Bandwidth UMTS by Filtering for Bands I (2.1 GHz), V (850 MHz) and VIII (900 MHz). Other bands may be considered later, based on interest.
Introduce the required changes in RAN1, RAN2 and RAN3 specifications, as well as core requirements in RAN4 specifications.