## Slide 1: UL Data Compression in UTRA - Motivations
3GPP TSG RAN Meeting #65 Edinburgh, GB, 9 - 12 Sep 2014
RP-141139

## Slide 2: Motivation
Faster Uplink Data, Better User Experience
  With same bandwidth more application data can be sent
  => Better perceived speed of the connection
Data compression also benefits UE battery consumption
  Reduced transmission time (in high power UMTS radio states)
Less Uplink Data, Less Interference
  => It is possible to increase data capacity using compression
  The feature was studied during Rel-12, with good outcome/conclusions (see TR 25.700, section 5.2)

## Slide 3: Compressing Uplink Traffic
For typical webpages, web-browser sends 50-100 HTTP GET/POST Requests. Many apps also send HTTP requests
Significant redundancy exists within and across HTTP requests
Observed compression level across websites
Total n. of bytes after compression
Total number of bytes
Compression Factor
=

## Slide 4: Benefit - User Experience (1/2)
Up to ~70% Page Load Time Reduction with UL Data Compression
Chart: Page Load Time Reduction (Web-browsing mode)
| no limit | 350kbps | 250kbps | 180kbps | 100kbps
NYT | 2.2 | 15 | 32 | 55 | 73
CNN | 5.7 | 11 | 18 | 39 | 63
WSJ | 4 | 11 | 23 | 34 | 43
Amazon | 1.7544 | 6.4516 | 8.1967 | 9.375 | 29.0698

## Slide 5: Benefit - User Experience (2/2)
Up to ~45% App Load Time Reduction with UL Data Compression
Chart: Page Load Time Reduction (App mode *)
| no limit | 350kbps | 250kbps | 180kbps | 100kbps
BBC | 0 | 4 | 32 | 43 | 44
CNN | 0 | 0 | 19 | 45 | 47
(*) Pages in app mode are cleaner compared to browsing mode, e.g. mostly text with less pics/ads, resulting in fewer HTTP requests.

## Slide 6: Benefit - Improved Battery Life
Up to ~65% Battery Consumption Reduction with UL Data Compression
Chart: Web-browsing Battery Life Improvement
| 0 | 5 | 10 | 15 | 18
NYT | 3.1 | 3.9 | 5.6 | 52.2 | 57.5
CNN | 0.4 | 14.9 | 29.4 | 50.4 | 64.4
WSJ | 10.2 | 10.8 | 10.6 | 45.4 | 56.2
> 10 % of time in metro/urban area
40 % of time in metro/urban area

## Slide 7: Benefit - Legacy Users
UL Data Compression frees up system resources for legacy UE’s
 | Penetration of UL Data Compression UE’s |  |  | 
Web-browsing as fraction of total traffic | 25% | 50% | 75% | 100%
1/3 | 9.5 % | 19 % | 28.6 % | 38.2 %
1/2 | 19.1 % | 38.3 % | 57.4 % | 76.6 %
Throughput gain (%) for legacy UE’s*
* Results are obtained by simulations: 57 cell wraparound, ISD = 1km 3GPP channel mix, E-DCH w/ 2ms TTI, No 16 QAM, Target BLER = 10% after 1st transmission, Max. # of transmissions = 4, ROT Target = 6dB, Number of legacy UE’s/cell = 4, Varying # of Web-browsing UE’s.

## Slide 8: UL Data Compression - Overview
Can apply to TCP/IP headers and payload
UE compresses data – when useful; RNC decompresses it
Limited impacts
  No PHY layer impacts
  Transparent to NodeB
  No impact to applications
  No impact to HTTP servers
  No impact to device Operating Systems

## Slide 9: UL Data Compression in 3GPP
Main WI Objectives:
  Standardize the necessary compression parameters and associated signaling, over the air and within UTRAN, to support Configuration, (De-)Activation and Capability indication
  UL data compression should apply to TCP/IP header and/or Payload
  No need to specify a detailed compression algorithm
    Some min. performance for the compressor efficiency could be considered (e.g. as done for RoHC)
RAN2 is the primary/main WG
  RAN4 may be involved on compression perf. aspects
Work Item Aspects