## Slide 1: HSPA Dual-Band UL carrier aggregation - Motivations
3GPP TSG RAN Meeting #65 Edinburgh, GB, 9 - 12 Sep 2014
RP-141141

## Slide 2: Motivation
DB-DC/4C-HSDPA can aggregate DL across two bands
  UL carriers are configured only on one of the two bands
  UL carriers on the other band are not efficiently exploited
DC-HSUPA is possible, but may not always be suitable
  10MHz of contiguous spectrum may not be available (e.g. in some 900MHz markets)
DB-DC-HSUPA is a natural evolution/extension of DC-HSUPA & DB-DC/4C-HSDPA, to optimize spectrum utilization and UL data performance

## Slide 3: Deployment Scenario and Band Combinations
Scenario: Co-located (aligned) antenna patterns on both bands
High frequency coverage
Low frequency coverage
Node B
Node B
Node B
UL/DL Band A | UL/DL Band B
I | VIII
I | V
II | V
NOTE: one UL carrier configured on each UL band
Bands Legend:
I = 2100 MHz
II = 1900 MHz
V = 850 MHz
VIII = 900 MHz
Candidate Band Combinations

## Slide 4: Work Item Aspects
RAN4 is the primary WG. Some RF aspects to consider:
  UE maximum output power requirements, e.g. per PA/band/UE
    Note: a separate PA per band is assumed.
  UE Tx requirements for unbalanced Tx power
  UE self-desensitization caused by intermodulation products of aggregating two UL inter-band carriers
  UL Harmonics based on different band combinations
RAN2/3 should introduce the functionality in relevant AS/UTRAN protocols and specifications
Such feature should be defined as release-independent
  As for other multi-carrier configurations (TS 25.327)