## Slide 1: Advanced Receivers for UMTS DCH - Motivations
3GPP TSG RAN Meeting #65 Edinburgh, GB, 9 - 12 Sep 2014
RP-141143

## Slide 2: Motivation & Goals
Advanced receivers are defined only for HSDPA
For DCH/Voice, system sometimes operates at a higher DL DPCH Ec/Ior than required (using power control)
  Trying to achieve better coverage, with known capacity trade-offs
Goals:
  Reduce DL DPCH Ec/Ior required for DCH traffic by improving UE demodulation performance
  Define enh. performance requirements for DCH Adv. Rx

## Slide 3: New Advanced Receiver Types for DCH
Introduce enhanced perf. requirements for DCH (RAN4)
  Dual Rx Antenna Capability
    Type 1-dch: UEs which utilise RAKE receiver with Rx diversity for DCH
  Interference Cancellation Capability + Single Rx Antenna
    Type 2i-dch: UEs with interference-aware chip equaliser and single Rx for DCH
  Interference Cancellation Capability + Dual Rx Antenna
    Type 3i-dch: UEs with interference-aware chip equaliser and Rx diversity for DCH
Benefit both user experience and system capacity
  Link level: improve the DL power link budget, allowing a better RF coverage and/or call reliability & retainability
  System level: DL power savings increase capacity/Tput for all UEs
  Initial Link/System simulation results show significant gains
    …see next slides (& Annex for sim. assumptions)

## Slide 4: Link-level Performance (single UE) for AMR12.2K
Type 0: Receiver Type with perf. requirements based on single Rx antenna
DL DPCH Ec/Ior Gains compared to Type 0
Chart: AMR12.2k
| PA3 G=0 | PA3 G=6 | PB3 G=0 | PB3 G=6 | VA30 G=0 | VA30 G=6 | VA120 G=0 | VA120 G=6 | UAR4 AVG | UAR5 AVG | UAR6 AVG | UAR7 AVG
Type 1-cs | 6.25 | 5.16 | 3.61 | 3.99 | 3.4 | 3.06 | 3.08 | 3.11 | 2.348 | 2.312 | 2.512 | 2.4
Type 2i-cs | 0.65 | 0.82 | 0.83 | 2.23 | 0.44 | 1.52 | 0.45 | 1.85 | 1.082 | 1.856 | 1.954 | 1.394
Type 3i-cs | 6.7 | 6.3 | 4.53 | 5.99 | 4.08 | 4.91 | 3.74 | 4.81 | 3.918 | 4.512 | 4.658 | 4.176
Summary of gains (dB range) | Type 1-dch | Type 2i-dch | Type 3i-dch
 | 2.3dB <-> 6.2dB | 0.4dB <-> 2.2dB | 3.7dB <-> 6.7dB
Type 1-dch
Type 2-dch
Type 3-dch

## Slide 5: Link-level Performance (single UE) for AMR5.9K
DL DPCH Ec/Ior Gains compared to Type 0
Chart: AMR5.9k
| PA3 G=0 | PA3 G=6 | PB3 G=0 | PB3 G=6 | VA30 G=0 | VA30 G=6 | VA120 G=0 | VA120 G=6 | UAR4 AVG | UAR5 AVG | UAR6 AVG | UAR7 AVG
Type 1-cs | 6.53 | 4.82 | 3.54 | 3.05 | 3.64 | 3.13 | 3.34 | 3.13 | 2.312 | 2.206 | 3.002 | 2.25
Type 2i-cs | 0.59 | 0.5 | 0.74 | 1.69 | 0.56 | 1.61 | 0.5 | 1.85 | 1.166 | 1.914 | 2.6 | 1.368
Type 3i-cs | 7.11 | 5.98 | 4.53 | 5.19 | 4.37 | 5.08 | 4 | 5.03 | 4.032 | 4.932 | 5.592 | 4.134
Summary of gains (dB range) | Type 1-dch | Type 2i-dch | Type 3i-dch
 | 2.2dB <-> 6.5dB | 0.5dB <-> 2.6dB | 4dB <-> 7.1dB
Type 0: Receiver Type with perf. requirements based on single Rx antenna
Type 1-dch
Type 2-dch
Type 3-dch

## Slide 6: System Performance (PA3) – BE UEs Tput Gain
Type-1-dch receiver at Best Effort(BE) UE under mixed voice and data scenario
Number of UEs/cell: BE UEs = 4; Voice UEs: 0, 8, 16, 24, 32 ,40, 48; UEs dropped uniformly across the system. Other Simulation Assumptions are provided in Annex

## Slide 7: System Performance (VA30) – BE UEs Tput Gain
Type-1-dch receiver at Best Effort(BE) UE under mixed voice and data scenario
Number of UEs/cell: BE UEs = 4; Voice UEs: 0, 8, 16, 24, 32 ,40, 48; UEs dropped uniformly across the system. Other Simulation Assumptions are provided in Annex

## Slide 8: Annex Simulation Results – Assumptions

## Slide 9: Simulation Results - Channel Conditions
Single Cell Scenarios
Multi-cell scenarios
 |  | Cell Geometries [dB] |  |  |  | 
Case | # of cells | Ior1/Ioc | Ior2/Ioc | Ior3/Ioc | # of OCNS | OCNS SF
UAR4 | 3 | 3.8 | -0.3 | -3.5 | [1 1 1] | [4 4 4]
UAR5 | 3 | 5.77 | 2.67 | 2.67 | [1 1 1] | [4 4 4]
UAR6 | 3 | 4.77 | 4.77 | -1.23 | [1 1 1] | [4 4 4]
UAR7 | 3 | 4.47 | 1.47 | -4.03 | [1 1 1] | [4 4 4]
Channel | Geometry [dB]
PA3 | 0, 6
PB3 | 0, 6
VA30 | 0, 6
VA120 | 0, 6

## Slide 10: System Level Evaluation - Assumptions (1/2)
Parameters | Comments
Number of UEs/cell | BE: 4 Voice: 0, 8, 16, 24, 32 ,40, 48 UEs dropped uniformly across the system
Channel Model | 100% PA3 (ITU), 100% VA30 (ITU) Fading across all pairs of antennas is completely uncorrelated.
CPICH Ec/Ior | -10 dB
Total Overhead power including C-PICH | 20%
UE Antenna Gain | 0 dBi
UE noise figure | 9 dB
UE Receiver | Type 3i for BE UE Voice UE: 1Rx vs 2Rx Rake
Thermal noise density | -174 dBm/Hz
Maximum Sector Transmit Power | 43 dBm
Soft Handover Parameters | R1a (reporting range constant) = 6 dB

## Slide 11: System Level Evaluation - Assumptions (2/2)
Parameters | Comments
Cell Layout | Hexagonal grid, 19 Node B, 3 sectors per Node B with wrap-around
Inter-site distance | 1000 m
Carrier Frequency | 2000 MHz
Path Loss | L=128.1 + 37.6log10(R), R in kilometers
Penetration loss | 10 dB
Log Normal Fading | Standard Deviation : 8dB Inter-Node B Correlation:0.5 Intra-Node B Correlation :1.0
Max BS Antenna Gain | 14 dBi
Antenna pattern | = 70 degrees, Am = 20 dB