## Slide 1
3GPP TSG RAN#65
RP-141228: RAN offload solutions using LTE- WLAN IP Flow Level Aggregation

## Slide 2: Technology enablers
WLAN access can provide means for increased bandwidth coverage to the RAN;
TCP traffic still counts for the largest amount of traffic that is shared over the links. Recent (2014) public available traces from CAIDA (http://www.caida.org/data/passive/trace_stats/ ) still show a ratio of UDP:TCP traffic ratio of up to 1:5 (in number of packets) or up to 1:10 (in number of bytes) ;
The work in UPCON has reached the conclusion that the solutions 1.5.5 Off-path based and 1.6.1: Policy-based congestion mitigation are to be added into normative specifications;
Both UE initiated as well as network initiated NBIFOM are part of the Release 13 work to be done, and it may be used for congestion mitigation scenarios by creating the means to allow IP flows being offloaded to WLAN;
Several operators have expressed interest for a hybrid solution using LTE access in order to provide coverage and WLAN access to address the increased bandwidth needs.

## Slide 3: Technology enablers – MP-TCP
MP-TCP [RFC6824] offers transparent wireless resource pooling for a single "IP flow" for multi-homing UEs with least network complications, as it effectively implements automatic RAT selection/handover/pooling through TCP's adaptive end-to-end rating mechanism [RFC6356].
As a limitation, end-to-end MP-TCP solution deprives network's control over service/RAT preference, which is considered to be essential for better operation and service provision in 3GPP networks.
Network deployed MP-TCP proxy comes as a compromise, which would certainly benefit MP-TCP enabled UEs by providing protocol adaptation, and at the same time maintain as the wireless network operator's policy enforcement point for their preferred network selection/usage strategies. (draft-deng-mptcp-mobile-network-proxy)

## Slide 4: TECHNOLOGY ENABLERS - MP-TCP
Preliminary experimental demo results indicate that MP-TCP provides link aggregation close to 98%.

## Slide 5: Technology enablers – wlan access
To provide traffic steering decisions that yield the best match to the QoS and/or throughput requirements of the system, WLAN Radio measurements are not sufficient as an estimate of the quality of the WLAN access.
IEEE 802.11 suggests the use of a single parameter, such as estimated available throughput, which combines RNSI/RCPI, channel bandwidth, operating band, number of spatial streams, BSS load, and WAN metrics. This parameter would be determined inside of the WLAN modem and then delivered to the upper layers for a decision.

## Slide 6: Way forward in 3gpp release 13
3GPP should prioritize work for the low hanging fruits by prioritizing solutions that provide the maximum impact with minimum disruption on the terminal architecture;
In SA, MP-TCP proxy deployments together with NBIFOM as well as the UPCON offpath solution represent viable solutions for a seamless aggregation solution of the TCP traffic over both cellular and WLAN;
In SA, UPCON offpath solution augmented with network initiated NBIFOM may be used for congestion mitigation using WLAN offload;
In RAN, the operator requirements can also be fulfilled using Solution 1A of SCE DuCo (as a starting point). Our initial estimate of this solution indicates that it has a minimum impact on the terminal, while it provides the operator required nobs for a high level of QoS and desired throughput. The resource management between the accesses shall be done taking into account the IEEE response LS.

## Slide 7: Thank You!