## Slide 1: Way forward on new UE categories in Rel-12 and 13
NTT DOCOMO, INC.
3GPP TSG-RAN#67
Shanghai, China, 9 - 12 March 2015
Agenda: 14
RP-150207

## Slide 2: Way forward
Introduce a new UE category for DL 750 Mbps from Rel-12.
  The corresponding CR is prepared for RAN#68.
Introduce new UE categories for 1 Gbps or beyond from Rel-13
  The target rate will be continued to discuss and decided until RAN#69 (so that the corresponding CR can be prepared for RAN#70).

## Slide 3: Rationale for 750 Mbps category
Market demand for high frequency bands
  E.g., 3DL CA with low and high frequency bands.
    20 MHz with 2 layer MIMO (low) and 40 MHz with 4 layer MIMO (high).
    B1/3+B42+B42 is being specified in RAN4.
Support of 2 layer MIMO up to 5 CCs.
  The current specification supports the 2 layer MIMO configuration up to 4 CCs (300/450/600 Mbps).
  As 2 layer MIMO is a typical configuration applicable to all frequency bands, support for 5CCs (i.e., 750 Mbps) is deemed as necessary.