## Slide 1
LG Electronics
Motivation of
Feasibility Study on
LTE-based V2X Services
3GPP TSG RAN WG Meeting #68 RP-150777
Malmö, Sweden, June 15 - 18, 2015
Agenda item: 13.1.1
Document for: Discussion

## Slide 2: Wide interest on V2X
Various V2X related Organizations (Automotive Industries & Governments)
  CEN, ETSI, ISO, IEEE, SAE, CALM, CAMP, C2C-CC, CVRIA and etc (including each country’s ITS bodies).
Lots of Interests in LTE V2X Technologies for Connected or Smart Car
Various V2X R&D Projects, Assessments and (Pre-)deployment Programs

## Slide 3: Current status of V2X in LTE
Strong interest in V2X study was identified in RAN#66 as captured in RAN report [1].
Considering the interest in RAN and urgency of RAN V2X, RAN#66 sent an LS [2] to SA1 in order to trigger SA1 study on requirements as early as possible.
SA1#69 agreed a new Rel-14 study on ‘LTE support for V2X services’ [3] to investigate use cases and potential requirements.
  The start of V2X specification activity was announced to external organisations [4].
SA1 sent a response LS [5] which includes outcome of their study on the use cases and requirements.

## Slide 4: Summary of SA1 study status
SA1 study item is scheduled to be completed in SA1#72 (11/2015).
  The current progress is 50% (as of 04/2015).
  WI schedule was discussed and it was proposed to agree on WID in SA1#71 (08/2015) [6].
The study outcome in [7] contains
  Three V2X services types
    V2V (vehicle-to-vehicle): Communication between vehicles.
    V2I (vehicle-to-infrastructure): Communication between a vehicle and a roadside unit (RSU) which is implemented in an eNB or a stationary UE.
    V2P (vehicle-to-pedestrian): Communication between a vehicle and a device carried by an individual (pedestrian, cyclist, driver or passenger).
  18 use cases and corresponding requirements
    All the three types are covered in these use cases.
    Both safety and non-safety applications are included.
RAN can start the first step of V2X study based on the information provided by SA1.

## Slide 5: V2V and V2I use case
V2V and V2I provide delivery of V2X messages such as CAM/DENM between vehicles via direct interface and RSU respectively.
  Note that inter-vehicle message delivery can be realized not only by V2V but also by V2I [7].
Example of V2V and V2I use cases (Vehicle Collision Warning)

## Slide 6: V2P use case
V2P provide delivery of V2X messages between a vehicle and a pedestrian (a device carried by an individual).
  Note that V2P can cover not only a pedestrian but also a cyclist, a driver or a passenger in the SA1 study [7].
Example of V2P use case (Pedestrian Collision Warning)

## Slide 7: Challenges and possibilities of LTE-based V2X
ProSe can be one of important building blocks for LTE V2X services.
  For example, to support LTE V2X outside network coverage (use case in 5.13 in [7]).
However, careful study is necessary on what the current ProSe can support for LTE V2X.
  One reason is that the design target is different from what was considered in Rel-12/13 ProSe study.
 | ProSe discovery | ProSe communication | V2X
Target range | Long, medium, short | Long | Medium, short (focusing on safety services)
Latency/reliability requirement | Best effort | Strict | Strict
Number of users | Large | Small | Large
Message size | Small | Small (focusing on VoIP) | Variable size

## Slide 8: Challenges and possibilities of LTE-based V2X
Parameter comparison between ProSe communication and V2X
 | ProSe communication for VoIP[8] | V2X for forward collision warning (use case in 5.1 [7])
Target range | 700 m1) | 50 ~ 320 m
Number of TX UEs per cell | 3 with inter-site distance of 1732 m | Can grow to 100 or more with inter-site distance of 500 m in urban scenarios
Message size | 41 bytes | Typically 50 ~ 300 bytes, maximum 1200 bytes
Message period | 20 ms with 75% activity | 100 ms at the maximum frequency
Latency requirement | 200 ms | 100 ms
Traffic intensity | 36.9 kbps per cell = 42.6 kbps per km2 | 200 kbps per cell2) = 2770 kbps per km2
1) Assuming -107 dBm receive power with 23 dBm UE TX power at 700 MHz NLOS channel
2) Assuming 50 byte message at every 100 ms and 50 TX UEs per cell

## Slide 9: Challenges and possibilities of LTE-based V2X
Preliminary evaluation results
  When 100% UL resources are used for vehicle-to-vehicle direct transmissions.
  Performance metric: Ratio of reliably connected vehicles within the target range from a vehicle.
It may be challenging to fulfill the V2X requirement with straightforward enhancements to Rel-12/13 ProSe.
Number of vehicles per cell | Average inter-vehicle distance1)
32 | 125.2m
64 | 65.43 m
128 | 33.63 m
1) Average of the distance to the closest vehicle locating on the same lane.

## Slide 10: Challenges and possibilities of LTE-based V2X
Performance enhancement by the assistance from network
  eNB overhears vehicle transmissions and forwards them.
  Vehicles attempt to receive each message twice, directly from the transmitter vehicle and via network forwarding from eNB.
Assistance from the network can be one possibility to facilitate LTE V2X services.
Using 100% UL and 28% DL resources
Using 50% UL and 28% DL resources
Using 100% UL and no DL resources
Using 100% UL and no DL resources

## Slide 11: Needs for Rel-13 V2X Study in RAN
Overall study is necessary for LTE V2X.
  To do the gap analysis, i.e., to see whether / to which extent the current LTE can fulfill the V2X service requirements.
  To indentify technical options to enable / facilitate V2X services, which may require substantial specification changes.
    All the three links (uplink, downlink, and sidelink) need to be studied together to cover the SA1 use cases as well as to find out the set of universal solutions.
RAN1 has not performed a study focusing on vehicular communications so far.
  No evaluation methodology in terms of deployment scenarios and channel models for vehicular communications, proper traffic model and performance metric, and so on.
  Early start of this feasibility study in Rel-13 will be beneficial for timely completion of the related Rel-14 specification works with high quality.

## Slide 12: Proposal for Rel-13 RAN study on V2X
We propose that RAN should study V2X in the following steps [9]:
  Evaluation methodology for V2X
    Deployment scenarios and channel models suitable for vehicular communications
    Modeling of vehicle mobility and its impact on the physical layer operations and performance
    Traffic models and performance metrics
  Gap analysis between the SA1 requirement and the performance of the existing LTE systems
  Identification and evaluation of technical options for enhancements in LTE uplink, downlink, and sidelink

## Slide 13: Work Plan for RAN study in REL-13
Time plan proposal is provided in [10].

## Slide 14: References
[1] RP-150002, Report of 3GPP TSG RAN meeting #66.
[2] RP-142312, LS to SA1 on LTE based Vehicular Communication, TSG-RAN.
[3] S1-150284(=SP-150051), Agreed SID for Study on LTE support for V2X services, LG Electronics.
[4] SP-150166, LS on information regarding V2X study in 3GPP, TSG-SA.
[5] RP-150557(=S1-151629), Reply LS to RP-142312 on LTE based Vehicular Communication, SA1.
[6] S1-151093, Proposed plan for V2X (Stage 1), LG Electronics.
[7] 3GPP TR 22.885 v0.2.0: Study on LTE support for V2X services. S1-151330.
[8] 3GPP TR 36.843 v12.0.1: Study on LTE Device to Device Proximity Services;
Radio Aspects.
[9] RP-150778, New SI proposal: Feasibility Study on LTE-based V2X Services, LG Electronics, CATT.
[10] RP-150779, Time plan for the new SI proposal on LTE-based V2X, LG Electronics, CATT.
[11] ETSI TR 102 861 v.1.1.1 Intelligent transport systems; STDMA recommended parameters and settings for cooperative ITS; Access layer part.

## Slide 15: Appendix
Cell deployment | Macro only
Carrier frequency | 2 GHz
System bandwidth | 10 MHz
Inter-site distance | 500 m
Number of cells | 7 sites (21 cells)
Road deployment | 150m*150m urban grid model in [11] is adjusted to fit in the wrap around cell deployments. 2 lanes in each direction (4 lanes in each street).
Vehicle UE drop | Uniform on the road. 32, 64, 128 UEs per cell.
Number of antennas | 2 TX and 2 RX at eNB, 1 TX and 2 RX at UE
Antenna height | 25 m at eNB, 2 m at UE
TX power | 46 dBm at eNB, 23 dBm at UE
Channel model | Outdoor-to-outdoor model in [8] with the exception that NLOS probability of UE-UE link is 1 when there is building between two vehicles.
Vehicle UE speed | 60 km/h
Simulation assumptions

## Slide 16: Appendix
Message generation | 50 byte message is generated in every 100 ms in each UE.
Vehicle-to-vehicle transmission | Random resource selection within resource pool in UL. 8 RBs are used with no repetition for each 50 byte message. PUSCH-based channel structure is assumed.
Vehicle-to-eNB transmission | eNB overhears vehicle-to-vehicle transmissions and forwards successfully received messages.
eNB-to-vehicle transmission | SFN transmission from each 7-cell cluster using DL. Messages received in the cell at the cluster center are transmitted from the center cell as well as 6 neighboring cells. Rank 1 PDSCH using port 7 with 2 symbol PDCCH is assumed.
CP length | Normal CP in all transmissions.
Synchronization | Ideal in time and frequency
Reliability criterion | BLER less than 10%
Target range | 100 m

## Slide 17: Appendix
Illustration of cell and vehicle deployments