## Slide 1: Small data coverage enhancements for umts
RP-150847 - Motivation for New proposed WI

## Slide 2: Background
During the Study Item phase several physical channels were subject to coverage evaluations in order to identify potential bottle necks.
From the investigations performed it was concluded that the PRACH preamble, the PRACH message, EUL, and PCH are the channels more limited in coverage among the ones that were evaluated.
Since that conclusion was made, and due to the different nature of the channels, the TSG RAN WG1 has focused most of their efforts and investigations on finding potential solutions for improving the coverage of those channels along with L1 signalling optimizations on the E-DPCCH.

## Slide 3: Proposed RAN Work Item
Coverage enhancements: Specify a technical solution for each of the physical channels that during the SI phase were identified as bottlenecks.
  PRACH preamble
    A solution facilitating the PRACH Preamble Repetition shall be standardized.
  PRACH message
    A solution facilitating the PRACH Message Repetition shall be standardized.

## Slide 4: Proposed RAN Work Item
  PCH
    A solution facilitating PCH coverage enhancements shall be standardized based on either
      Smaller PCH TBS
      Dynamic Power Boosting
    or both if due to its orthogonal nature are seen as a complementary solutions for enhancing further the coverage of the PCH.
  EUL
    A solution facilitating the EUL coverage enhancements shall be standardized based on either:
      EUL consecutive TTI repetitions
      EUL TDM operation (w/o repetitions)
    and L1 E-DPCCH optimizations if they are seen beneficial as complementary solutions for enhancing further the coverage of the EUL.

## Slide 5: benefits
Coverage range extension for the channels identified as bottle necks.
Better coverage balancing between the channels.
Increased service availability for UEs in a coverage limited situation.
The improvements are beneficial not only for machine devices or small data transmissions but for the UL and DL transmissions in general.