## Slide 1: Motivation for New WI: Small Data Power Saving Enhancements for UMTS
Ericsson
3GPP TSG RAN Meeting#68
Malmo, Sweden, Jun. 15 – 18, 2015
RP-150851
Document for: Discussion/Decision
Agenda Item: 13.1.2

## Slide 2: background
Power consumption is important for small data devices
Delay tolerant devices may sleep for a long time to enable long battery life time
Power Saving Mode (PSM) introduced in REL-12 introduces such power savings in Idle mode
DRX extensions in both Idle and Connected mode can provide additional benefits for small data transmissions

## Slide 3: Justification (1/2)
DRX extensions in Idle mode:
  Similar benefits as discussed for extended DRX in LTE (RP-150181)
  Idle-to-connected mode signalling is avoided to check for DL data
DRX extensions in Connected mode (CELL_PCH/URA_PCH):
  In PCH state identical measurement requirements and UE based mobility (cell re-selection) as in Idle mode
  Seamless transition from PCH state to CELL_FACH can avoid signalling and delay compared to DRX extension in Idle mode

## Slide 4: Justification (2/2)
Quick return into power saving modes:
  There can be a significant delay to re-configure a UE into "power savings" after data transmissions (reducing battery life time):
  Without knowing that UE is configured with PSM, RNC may switch the UE to CELL_PCH/URA_PCH instead of idle:
  Similar improvements as for PSM can apply for the DRX enhancements

## Slide 5: Proposed HSPA RAN2 work item
DRX enhancements in Idle mode and Connected mode (i.e. CELL_PCH and URA_PCH):
  DRX extensions that are applicable for both beyond and within the SFN limit of 40.96 sec
Quick return into power savings:
  Quick return into PSM mode after data transmission
  Quick return into DRX extensions (within and beyond SFN limit) after data transmission

## Slide 6: context
Take into account solutions described in TR 25.705 “Study on small data transmission enhancements for UMTS”