## Slide 1: Way forward on MIMO/CSI capability for intra-band contiguous CA (R2-152921, RP-150980)
NTT DOCOMO, INC., Intel
RP-151023
TSG RAN meeting #68
15-18 June 2015, Malmö, Sweden

## Slide 2: Identified issue
Additional capability signaling was agreed to allow the UE to indicate MIMO/CSI capabilities individually per carrier for intra-band contiguous CA.
  The legacy signaling is still used to indicate their capabilities supported on all carriers.
However, an additional specification impact was found to enable an individual MIMO layer per carrier as indicated by the additional signaling.
  Rank Indicator bit width needs to be determined taking into account the additional MIMO/CSI capabilities.

## Slide 3: Expected specification impacts
TS 36.212
  The mechanism to determine the RI bit width (section 5.2.2.6)
TS 36.331
  Additional signaling for the UE to determine the RI bit width (if needed)

## Slide 4: Proposed way forward
Postpone to approve the CRs (R2-152921 and RP-150980).
Have an official RAN2 email discussion until RAN2#91 to discuss the identified issue.
  Intended outcomes are agreeable 306/331 CRs and proposed changes to 36.212.
  Intel will lead the email discussion.
Send an LS to RAN1 at the beginning of RAN2#91
  So that RAN1 can prepare the 36.212 CR.
All the required CRs (36.212/306/331) are brought to RAN#69 for approval.