## Slide 1: Consideration on MDT Further Enhancements
CMCC
RP-151182
3GPP TSG RAN Meeting #69
Phoenix, USA, Sep. 14 - 16, 2015
Agenda Item: 14.1.2
Document for: Discussion and Decision

## Slide 2: General
The SI “Further Enhancements of Minimization of Drive Tests for E-UTRAN” (feMDT) is completed at RAN2#91
A new WI should be started to specify the corresponding concluded solutions (marked in red in the following two slides)

## Slide 3: Conclusions of feMDT study(1/2)
On solutions for QoS verification: it is considered as beneficial to obtain the latency, packet loss and traffic drop metrics of MMTEL voice and video traffic.
  Regarding latency metrics collection, UL PDCP queuing delay measurement should be performed per QCI per UE and should reflect the packet delay observed at UE’s PDCP layer only (from packet arrival at PDCP upper SAP until the packet starts to be delivered to RLC).
  Regarding packet loss metrics collection, data loss measurement for UL and DL (except for UL dropping of PDCP SDUs) can be done based on existing L2 measurements. For UL dropping of PDCP SDUs the UE should log number of PDCP SDUs that are discarded and reports statistics thereof to the eNB.
  Regarding traffic drop metric collection, UE should include presence of a QCI 1 bearer at the time of RLF in the RLF report. The UE should also indicate failure of subsequent re-establishment and NAS recovery.
  Regarding user distribution, the VoLTE user distribution among different geographical areas during different time can be derived through eNB implementation and Rel-11 MDT functionality.

## Slide 4: Conclusions of feMDT study(2/2)
On solutions for enhanced coverage optimization:
  It is considered as beneficial when UEs in RRC_IDLE supporting the IDC mechanism should remove measurements from the Logged MDT report that were affected by IDC interference.
  On network side solutions can be considered where either the eNB indicates to the TCE whether measurements have been collected while eICIC was configured or the eNB decides to not report those results to the TCE.

## Slide 5: Objectives of feMDT WI Enhanced QoS Verification Use Case
Specify MDT measurements and procedures to support better understanding of the QoS and its limiting factors for MMTEL voice and video traffic, including:
  UL PDCP queuing delay measurement, which should be performed per QCI per UE and should reflect the packet delay observed at UE’s PDCP layer only (from packet arrival at PDCP upper SAP until the packet starts to be delivered to RLC).
  Data loss measurement for UL and DL (except for UL dropping of PDCP SDUs), which should be done based on existing L2 measurements. For UL dropping of PDCP SDUs the UE should log number of PDCP SDUs that are discarded and reports statistics thereof to the eNB.
  Traffic drop metric collection. UE should include presence of a QCI 1 bearer at the time of RLF in the RLF report. The UE should also indicate failure of subsequent re-establishment and NAS recovery.

## Slide 6: Objectives of feMDT WI Enhanced Coverage Optimization Use Case
Specify corresponding procedures to support the following solutions, including:
  UEs in RRC_IDLE supporting the IDC mechanism should remove measurements from the Logged MDT report that were affected by IDC interference.
  eNB indicates to the TCE whether measurements have been collected while eICIC was configured or eNB decides to not report those results to the TCE.

## Slide 7: Thank you