## Slide 1: RP-151578 Motivation for New WI (RP-151579): NB-LTE for Low Complexity Radio Access Network for Cellular Internet of Things Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, AT&T, Bittium Wireless, CHTTL, Ericsson LM, Gemalto N.V., HTC, Intel Corporation, InterDigital Corporation, ITL, ITRI, KPN, LG Electronics, LG Uplus, LightSquared, Mediatek Inc., Motorola Mobility, Nokia Networks, Nordic Semiconductor ASA, NextNav, NTT, NTT Docomo, Samsung, Sequans, Sharp Corporation, Sierra Wireless SA, SK Telecom, Sony, SouthernLINC Wireless, Sprint Corporation, Telenor, Telstra, T-Mobile US, Verizon, ZTE Corporation

## Slide 2: Background: GERAN SI
SI in GERAN on “Cellular System Support for Ultra Low Complexity and Low Throughput Internet of Things”
Study included design of a new access system for low complexity and low throughput radio access technology to address the requirements of cellular internet of things
Objectives:
  improved indoor coverage
  support for massive number of low throughput devices
  low delay sensitivity
  ultra-low device cost
  low device power consumption
  (optimised) network architecture

## Slide 3: Narrowband LTE for CIoT
Studied in the GERAN SI and included in TR 45.820
  Further details and evaluation provided in RP-151389 and RP-151387
Exploits maximal re-use of LTE technology, including Rel-13 eMTC
Has some major advantages, including:
  Faster development of specifications
  Greater implementation re-use
  Reduced technology fragmentation
  Greater deployment flexibility for spectrum refarming and coexistence
  Scalability with increasing MTC traffic
  Further improvement of Rel-13 eMTC by common enhancement of network interface

## Slide 4: Operation Modes
NB-LTE can support 3 different modes of operation:
‘Stand-alone operation’ utilizing for example the bands currently being used by GERAN systems
‘Guard band operation’ utilizing the unused resource blocks at the edge of an LTE channel
‘In-carrier operation’ utilizing resource blocks within a normal LTE carrier
In order to avoid unnecessary design variations, the specification work should provide a common design for all the above modes of operation.
  Only NB-LTE can achieve this common design.

## Slide 5: Design principles
200 kHz UE RF bandwidth for both downlink and uplink
OFDMA DL with 15 kHz sub-carrier spacing, using at least BPSK/QPSK modulation
SC-FDMA UL, including single-tone transmission as a special case of SC-FDMA, assuming 2.5 kHz sub-carrier spacing, PAPR reduction techniques and (phase rotated) BPSK/QPSK modulation
Signal design and physical layer processing re-using those defined in E-UTRA to the greatest extent possible
  commonality to the greatest extent possible for ‘stand-alone’, ‘guard band’ and ‘in-carrier’ operation
MAC, RLC, PDCP and RRC procedures comprising a subset of existing LTE RRC and a reuse with minimal changes of existing LTE MAC, RLC and PDCP procedures, maximising reuse of E-UTRA protocols
Enhancements to S1 interface to CN to support the work SA2 is conducting on the systems aspects such as signalling reduction for small data transmissions.

## Slide 6: Timeframe
Due to the maximal reuse of existing LTE and eMTC technology, the core specification work can be completed within Rel-13
  No impact to existing LTE Rel-13 work items due to use of parallel session as recommended by PCG

## Slide 7: Thank you!