## Slide 1: Motivation for New WI Cell-specific Operation in CA [COCA]

## Slide 2: Legacy CA operation and MAC function
UE-specific CA operation
  No differentiation between aggregated cells.
    All aggregated cells are assumed to have same or similar characteristics.
Due to no differentiation between aggregated cells, MAC functions are designed as…
  No mapping between Bearer and Cell
  No differentiation between UL grants from multiple cells
  No support of cell-specific implicit deactivation of SCell
  UE specific DRX configuration/operation
BACKGROUND:

## Slide 3: MOTIVATION & JUSTIFICATION
Trend of Mobile Application
More diverse data traffic and applications
Voice
Social Network
Web Browsing
Video
File Sharing
Online Game
Delay sensitive,
periodic data
Delay critical
Delay tolerant,
Low data rate
Delay tolerant
Delay sensitive,
High data rate
Delay tolerant,
Burst data at event

## Slide 4: MOTIVATION & JUSTIFICATION
Increased number of aggregated cells invalidates the assumption that all aggregated cells have the same or similar characteristics.
  Among aggregated cells, a certain cell may provide, e.g., lower delay, higher coverage, than other cells.
CA enhancement
R12
R12
R13
R13
R13
R12
R12
R12
  5 Carriers up to Rel-12
  32 Carriers from Rel-13
Introduction of CA
  5 Carriers
  1 TAG
Rel-10
CA with multiple TAGs
  5 Carriers
  4 TAGs
Rel-11
Introduction of DC
  2 eNBs
  5 Carriers
  4 TAGs per CG
Rel-12
WI on CA enhancement
  32 Carriers
  DC with 32 CCs
Rel-13

## Slide 5: MOTIVATION & JUSTIFICATION
CA is the most essential feature even in LTE-Advanced Pro and 5G.
  To increase the throughput by utilizing fragmented spectrum.
However, CA needs to be enhanced to support cell-specific operation.
  In order to serve diverse applications on large number of aggregated cells more efficiently.
    Because aggregated cells may have different characteristics.

## Slide 6: MOTIVATION & JUSTIFICATION
Especially, it is necessary to serve a specific application on a specific cell.
  It can be realized by differentiating UL grants from different cells in Logical Channel Prioritization procedure.
    For example, UL grant from a cell with lower delay is used for VoIP while UL grants from other cells are used for web browsing/file sharing.
Music
Web browsing
Voice Call
Email
Video Call
Messenger

## Slide 7: MOTIVATION & JUSTIFICATION
If a specific cell serves only certain applications (e.g. VoIP) …
  The cell may need to be configured with SPS.
  The cell may need to be added in activated state.
  The cell may need to be configured with application-specific deactivation timer value.
  The cell may need to be configured with application-specific DRX configuration.

## Slide 8: OBJECTIVES
Logical channel prioritization procedure
  Differentiating UL grants received from multiple cells
  Transmitting UL data of a specific radio bearer on a specific cell
PDCP/RLC
PDCP/RLC
PDCP/RLC
PDCP/RLC
Cell 1
Cell 4
Cell 2
Cell 3
MAC

## Slide 9: OBJECTIVES
Semi-Persistent Scheduling procedure
  Introducing SPS configuration other than SpCell
  Configuring multiple SPS patterns, one per each serving cell
Activation/Deactivation procedure
  Allowing activated state at SCell addition
  Introducing per-cell implicit deactivation timer value
Discontinuous Reception procedure
  Configuring multiple DRX patterns, one per each serving cell or frequency band