## Slide 1: Motivation for New SI Enhanced COnnectivity for companion device (ECO)

## Slide 2: Why is a wearable device special?
Smart watches should support various services including voice/streaming with full mobility, almost like smart phones.
Customers expect much longer battery lifetime than smart phones, possibly almost like legacy watches.
Rel-12 PSM and Rel-13 eDRX are generally good for UE power saving. However, those features cannot fully support real-time services such as voice call and streaming service.
 | Smart Phone | Smart Watch | Smart Meter
Mobility | Full support | Full support | Limited support
Data Rate | High | medium | Very low
Delay | Sensitive service support | Sensitive service support | Insensitive service only
Battery lifetime | Relatively short (e.g. one or two days) | As long as possible | Extremely long

## Slide 3: Wearable and secondary UE
Customers will typically wear smart watches as their secondary devices while holding smart phones as their primary devices.
A smart watch including USIM can stand alone from time to time e.g. while a user is doing outdoor activity.
“A wearable UE can leverage the master phone in proximity to enhance connectivity with power efficiency.”
We belong to the same user.
In proximity
Standalone
device
Secondary
device
Not in proximity

## Slide 4: Connectivity aspects in SMARTER
SA1 is working on enhanced connectivity e.g. for wearable device in the context of connectivity aspects in SMARTER.
In SA1 scenario, a device can be connected to the network through a relay UE.
A short range communication RAT might be Bluetooth, WLAN or a 3GPP RAT.
A device can switch between a direct connection and a relayed connection to the network

## Slide 5: Key aspects for enhanced connectivity
SA1 defines key aspects of connectivity aspects. Most of them are essential in RAN to support smart watches:
  Secure communications and QoS consideration between the devices using short range communications
  Supporting the desired end user services, including real-time voice and data
  Minimizing power consumption on devices
  Supporting multiple devices behind a relay UE
  Service continuity for devices that switch between a relayed and direct connection to the network and for devices that switch from one relay connection to another relay connection
  Supporting roaming access to the network, whether the relayed or relaying device is roaming
Companion study on RAN aspects must start in Rel-14 to provide enhanced connectivity in Rel-15 considering market needs for attractive wearable devices.

## Slide 6: Study areas for enhanced connectivity (1/2)
Support SA1 requirements on connectivity aspects for both LTE and 5G
  The study is initially based on LTE in SI phase but should consider SA1 progress.
  The study should move forwards for 5G e.g. in the end of SI phase or in WI phase.
Investigate the enhanced connection of companion UE to the network via master UE [RAN2, RAN3]
  Support the enhanced connection even while companion UE is switching off AS operation
Investigate service continuity between enhanced connection and Uu connection under operators’ control for support of real-time service. [RAN2, RAN3]
  Companion UE may switch between enhanced connection and Uu connection e.g. considering QoS and/or proximity with master UE.
  Support service continuity with short interruption in switch e.g. for real time traffic.
Bluetooth, WLAN or new sidelink
NW
Master UE
Companion UE
Enhanced Connection
via master UE
Connection
switching
under NW control
NW
Connection
on Uu

## Slide 7: Study areas for enhanced connectivity (2/2)
Support maintenance of the enhanced connection for companion UE in mobility which is moving together with master UE [RAN2, RAN3]
Support the enhanced connection based on non-3GPP RAT such as Bluetooth and WLAN as well as Rel-12/13 3GPP sidelink. [RAN2]
  Consider support of the enhanced connection on Rel-12/13 sidelink without optimization
Investigate new design of short range sidelink transmissions on licensed/unlicensed band for the enhanced connection [RAN1, RAN2]
  Support unicast transmissions in sidelink for power efficiency, higher reliability and higher throughput
The study is not limited to IoT devices/services.
  Support normal UE capabilities for LTE, e.g. Cat 4 or higher, as well as IoT devices
  Consider various applications/services in wearable devices, like in smart phones.

## Slide 8: Proposed Study Plan
The study begins with RAN scenarios and requirements on enhanced connectivity mainly for smart watches. Initial result of the study can be used as an input to 5G RAN SI.
Q1/2016
  RAN scenarios and requirements considering SA1 progress
Q2/2016
  RAN scenarios and requirements considering SA1 progress
  Architecture solutions for proxy connection [RAN2]
Q3/2016
  Architecture solutions for proxy connection [RAN2, RAN3]
  Service continuity/mobility solutions [RAN2]
Q4/2016
  Service continuity/mobility solutions [RAN2, RAN3]
  New sidelink design in physical layer [RAN1]
Q1/2017
  Service continuity/mobility solutions [RAN2, RAN3]
  New sidelink design in physical layer [RAN1]
  New sidelink design in layer 2 [RAN2]