## Slide 1
New WI proposal: Motivation for S1 interface based Dual Connectivity Extension for LTE
Source: China Telecom, ZTE
3GPP TSG RAN Meeting #70
Sitges, Spain, December 7 - 10, 2015

## Slide 2: Background
DC is an effective solution for improving per-user and system throughput when macro and small cells are connected via non-ideal backhaul.
In R12/13 DC specification, the X2 interface is mandatory support between MeNB and SeNB for both 1A and 3C UP options.
  SeNB addition/Modification/Release related signaling for both 1A and 3C options have been specified via X2-C interface
  User data flow management for 3C option have been specified via X2-U interface
  the latency and throughput of X2 interface significantly influence the per-user and system performance.
1A UP Option
3C UP Option

## Slide 3: Identified Requirement
Providing coverage and capacity cost effectively in hotspot (e.g. hotels, malls, office buildings, and etc) is a clear need for operators. And small cell has been regarded as an effectively solution for catering to this need. Furthermore, a mass of small cells with high frequency(e.g. 3.5G) will be introduced in the indoor scenarios. Arranging backhaul between those nodes and Macro nodes is a major challenge
X2 interface may not exists between two nodes
  "no X2" attribute has been defined in OAM
  Some factors may also lead to no X2 connection,e.g
    IOT between vendors
    MeNB and SeNB deployed with different kinds of backhaul, then the latency and QoS still can not be guaranteed. One example is SeNB is deployed with fixed broadband access network while MeNB is deployed with IP-RAN
Requirement: How to support the flexible deployment in varied scenarios for DC is a major challenge for operators.

## Slide 4: Example use case
MME
MeNB
SeNB
Weak X2 or non at all or
Inter-vendor IoT doesn’t work

## Slide 5: Consideration on the Enhancement
Problem of R12/13 DC
  only support X2 based DC
  DC can not work in “No X2 scenario "or” the latency and QOS of X2 can not be guaranteed”
Enhancement for DC
  Introducing S1 based DC for "No X2 scenario”
  S1-based DC can be regarded as a complementary solution for X2-based DC.
Introducing S1-based solution for 1A option will extend the application scenarios for DC

## Slide 6: Proposed WI Objectives
The WID aims to evaluate and specify the S1 interface based dual connectivity extension in R14.The RAN impacts on the S1 based signalling support for the dual connectivity operation.
Support for the dual connectivity operation based on S1 interface with 1A Option.
  Support SeNB Addition via S1
  Support SeNB Modification via S1
  Support SeNB Release via S1
Support mobility scenarios of S1 interface based dual connectivity
  SeNB Change
  MeNB to eNB
  eNB to MeNB change
  Inter-MeNB handover without SeNB change
Other enhancements, e.g., SIPTO/LIPA support, CSG support in S1 DC.

## Slide 7
Thanks for your attention