## Slide 1: Way Forward on Indoor Positioning
Qualcomm, Ericsson, Nokia Networks, TruePosition, Sprint
3GPP RAN #70
December 2015
RP-152229

## Slide 2: Status @ RAN #70
Our understanding of the status is as follows
  Wifi, BT, Barometric support: complete
  Terrestrial Beaconing / MBS: not complete
    RAN4 component not addressed
      From the WID: “For TBS, co-existence, co-location and co-siting requirements will be addressed [RAN4].
  Terrestrial Beaconing / PRS Beacon: not complete
    No progress in RAN2 due to lack of agreements & TUs in RAN1
  LTE RAT dependent enh. (OTDOA/E-CID): not complete
    No progress in RAN2 due to lack of agreements in RAN1 & RAN4

## Slide 3: Some background on the feature
Goal was to study indoor positioning techniques & a specific goal was to provide uncompensated barometric pressure to the network (via PSAP) & to use WiFi/BT measurements (via a central database eg NEAD) to derive a dispatchable UE location
  This is implied by the FCC Report and Order for Indoor E911 location in the US
  NEAD = National Emergency Address Database

## Slide 4: Proposed way forward
Incorporate WiFi, BT, Barometric in Rel-13
  Both LTE & UMTS
  Requires revision of agreed CRs for:
    36.305 (R2-157059), 36.355 (R2-157125)
    25.305 (R2-156942), 25.331 (R2-156943), 25.413 (R3-152856), 25.453 (R3-152920)
  Addresses the vertical component which was identified as the missing feature from the beginning & supports dispatchable UE location
Move all other components to Rel-14 since they are not complete
  They can be incorporated when the work is complete