## Slide 1: Report of offline discussion on NB-IoT
Huawei, HiSilicon
3GPP TSG RAN Meeting #70 RP-152281
Sitges, Spain, December 7-10, 2015
Agenda Item: 11.7.17

## Slide 2: LS to RAN1
  There is only one NB-IoT UE category
  At least the first UL message after NB-PRACH for initial access to the network can be via single-tone UL
  Recommending a working assumption that both of the following are supported by the specifications:
    3.75 kHz subcarrier spacing for the first transmission after the first UL random access transmission
    15 kHz subcarrier spacing for the first transmission after the first UL random access transmission
    Details of network configurability is left to WGs (including the possibility of configuring both in the same cell)
  RAN has made no decision on capability/interoperability testing signaling