## Slide 1: Motivation of Enhanced ACDC for Connected Mode in LTE
March 7th 2016
3GPP TSG RAN-71 Göteborg, Sweden, March 7th -10th , 2016
CATT

## Slide 2: Background
Operators’ Challenges
  Diversified user requirements on comparatively limited network resources
  Efficient management of radio resources based on the differentiated treatment of user traffic
  To guarantee the support of essential services of communication in special situations (like: disaster)
  To reduce negative impacts by unattended traffic [1]
3GPP Work: Rel-13 ACDC
  Application specific Congestion control for Data Communication (ACDC) is an access control mechanism for the operator to allow/prevent new access attempts from particular, operator-identified applications in the UE
  Only targeted for UE in idle mode

## Slide 3: Motivation
Issues of Rel-13 ACDC:
  UE Misbehavior: The ACDC category is only based on UE declaration
  “Free Ride” [2]: A UE setups RRC connection with a high level ACDC category, the traffic of low level ACDC category can just reuse the existing RRC connection while bypass ACDC mechanism, which is UNFAIR to all other idle mode UEs.
  The remaining Rel-13 issues above significantly reduced the effectiveness of ACDC’s implementations.
Rel-13 ACDC Mechanism needs to be further enhanced to be more effective to address the increasing challenges faced by operators!

## Slide 4: Objectives
Analyze and develop candidate solutions to support enhanced ACDC for LTE UE in connected mode:
  Mechanism at UE side to control the data access on an ACDC category basis;
  Mechanism at eNB side to control the user traffic and connection with or without UE assistance and on an ACDC category basis;
  Standardize any protocol and signaling changes for E-UTRAN to support the abovementioned mechanisms to allow operator to have application specific control for UEs in connected mode.
The WI should be based on existing Rel-13 idle mode ACDC assumptions and agreements.

## Slide 5: Conclusion
We propose that RAN approve a new REL-14 WID on Enhanced ACDC for Connected Mode in March 2016 for E-UTRAN.
We request 1 TU (starting with 0.5) in LTE session for each RAN2 meeting from April to December 2016.

## Slide 6: Reference
R2-153301 Restricting Unattended/Background Data Traffic; Verizon, Acatel-Lucent, Ericsson, Qualcomm; discussion;
R2-153112 Coexistence and free-ride issues of ACDC; China Mobile Com. Corporation; discussion