## Slide 1: Discussion on further mobility enhancements with RRC diversity
China Telecom
RP-160248
3GPP TSG RAN Meeting #71
Göteborg, Sweden, March 7 - 10, 2016
Document for: discussion
Agenda Item: 10.1.2

## Slide 2: Discussion
Mobile data traffic volume will continuously grow up. Network densification referred as Ultra-Dense Network (UDN) , is the key solution to meet the requirements of ultra-high traffic volume density.
Mobility performance is one of the most important aspects for wireless communications.
  In UDN, mobile users may experience more frequent handover due to smaller cell coverage.
  In UDN, mobile users may experience higher handover failure due to bad channel condition of RRC signaling.
    Based on the current Dual-connectivity framework, the transmission of control plane signalling is still restricted in MeNB
A mechanism to improve mobility and signalling robustness is necessary.

## Slide 3: Simulation Scenarios
Scenario 1：RRC diversity (RRC connection reconfiguration) between source eNB and target eNB
Scenario 2：RRC diversity (RRC connection reconfiguration) between MeNB and SeNB based on Dual Connectivity

## Slide 4: Simulation assumptions
 | Macro cell | Pico cell
BS Tx power | 46dBm | 30dBm
Distance-dependent path loss | TR 36.814 Macro-cell model 1 | TR 36.814 Pico cell model 1
Channel model | ITU Channel model | 
Penetration Loss | 20dB | 20dB
Cell layout | 100% | 100%
BS Antenna gain including Cable loss | 15dB | 5dB
MS Antenna gain | 0 dBi | 0 dBi
Shadowing standard deviation | 8 dB | 10 dB
Correlation distance of Shadowing | 25 m | 25 m
Shadow correlation | 0.5 between cells/ 1 between sectors | 0.5 between cells
Antenna pattern | The same 3D pattern as is specified in TR 36.814, Table A.2.1.1-2 | Omni, as is specified in TR 36.814, Table A.2.1.1.2-3
Antenna configuration | BS 1Tx, UE 2Rx | BS 1Tx, UE 2Rx
Items | value
Layer 1 sample interval | 10ms
Layer 1 filtering time | 200ms
Layer3 Filter Parameter K | 1
Qout / Qin | -8 dB / -6dB
T310 | 1s
N310/N311 | 1/1
A3 Time To Trigger (TTT) | 160 ms
A3 Prep + Exec | 90 ms
A3 Offset | 2 dB
A2, A4 and A6 Time To Trigger (TTT) | 160 ms
A2, A4 and A6 Prep + Exec | 90 ms
A2 Threshold | -16 dB RSRQ
A4 Threshold | -16 dB RSRQ
A6 Offset | 1 dB

## Slide 5: Simulation results – Scenario1
 | Macro cell | Pico cell
carrier frequency/bandwides | 2.0Ghz/ 10Mhz | 3.5Ghz/ 10Mhz
layout | 19Cell，3sector per cell，1cluster per sector | 4 or 10 picos per cluster
ISD | 500m | 
Minimum distance(2D distance) | Small cell-small cell: 20m | 
 | Macro –small cell cluster center: 105m | 
Chart: 
| 60km/h 4 picos per cluster | 60km/h 10 picos per cluster
conventional | 4.0804 | 4.6595
RRC diversity | 0.2593 | 0.46382
Chart: HO failure rate (%)
| 30km/h 4 picos per cluster | 30km/h 10 picos per cluster
conventional | 2.6679 | 3.1157
RRC diversity | 0.16089 | 0.26996

## Slide 6: Simulation results – Scenario2
 | Macro cell | Pico cell
carrier frequency/bandwidth | 2.0Ghz/ 10Mhz | 3.5Ghz/ 10Mhz
layout | 19Cell，3sector per cell，1cluster per sector | 4 picos per cluster
ISD | 200m | 
Minimum distance(2D distance) | Small cell-small cell: 20m | 
 | Macro –small cell cluster center: 40m | 
Chart: HO failure rate (%)
| 30km/h 4 picos per cluster
conventional | 7.0999
RRC diversity | 3.0423
Chart: HO failure rate (%)
| 60km/h 4 picos per cluster
conventional | 9.6805
RRC diversity | 5.6675

## Slide 7: Conclusion
RRC diversity can improve mobility and signalling robustness and thus reduce the handover failure rate significantly.
It is proposed to further study RRC diversity for mobility enhancements in Rel-14.