## Slide 1
Motivation for new SI Proposal
Study on HSPA and LTE Joint Operation
China Unicom
3GPP TSG RAN Meeting #71 RP-160311
Gothenburg, Sweden, Mar 7 - 10, 2016
Document for: Discussion
Agenda Item: 10.1.3

## Slide 2: Background
With the increasing of LTE subscribers, it is critical for UMTS operators to consider how to achieve satisfied utilization of UMTS resources.
  Spectrum refarming needs in long term since the data traffic still increases in the HSPA networks (operators reduce the data tariff)
  For voice supporting, CSFB still be the common mechanism for LTE devices. Operators needs UMTS networks for voice services.
Voice over CS will be existed for long time paralleling with voice over LTE
  VoLTE could be challenge for operators as it needs IMS deployment and bring new problems of cell planning, network optimization
  CS voice has advantage in coverage since UMTS has been deployed and optimized for long time
  CS voice solutions are still under evolutions to provide even better voice service, e.g. EVS etc.

## Slide 3: Motivation
UMTS and LTE interworking mechanisms specified are not sufficient
  Users could only camp on and access to either LTE or HSPA, and users could be scheduled from one RAT to another RAT for inter-RAT load balance.
  The user experience is restricted by the available radio resource and the channel quality in single RAT.
Tight-integration of HSPA and LTE could be a way for satisfied voice supporting and high data rate
  The continuous wide coverage of HSPA network can provide satisfactory voice services
  LTE has attractive abilities for high data rate PS services

## Slide 4: Objective and Scope
Study possible solutions to support CS in 3G and PS in 4G, evaluate the impacts on network architecture and interface, e.g.
  Assumption: UE always camps on LTE and voice service is on 3G.
  Study the possible solutions, on top of current mechanism, as the following cases
    An idle UE in LTE initiating MT/MO voice call, both network and UE side behaviors
    A connected UE in LTE initiating MT/MO voice call, both network and UE side behaviors
    A connected UE in 3G with CS service, UE tries to establish PS service
  Study the possible solution and impacts on architecture, signaling flow enhancement, etc.
    With the working assumption that impacts should be as less as possible, e.g. 4G specs.

## Slide 5: Time budget proposal
RAN #71 Q2/2016 RAN #72 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf | R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf
84bis | 84bis | 93bis | 93bis | 93bis | 91bis | 78bis | 78bis | 78bis | 78bis | 85 | 85 | 94 | 94 | 94 | 92 | 79 | 79 | 79 | 79
 |  |  | 0.5 | 0.5 | 1 |  |  |  |  |  |  |  | 0.5 |  | 1 |  |  |  | 
RAN #72 Q3/2016 RAN #73 |  |  |  |  |  |  |  |  |  | 
R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf | 
86 | 86 | 95 | 95 | 95 | 93 | 80 | 80 | 80 | 80 | 
 |  |  |  | 0.5 | 1 |  |  |  |  | 
L: LTE, U: UMTS, J: Joint, RD: RRM/demodulation