## Slide 1: Way forward on Requirements TR
3GPP TSG-RAN Meeting #71 RP-160644
Göteborg, Sweden, March 7 - 10, 2016
AI 9.2.2
Document for discussion/approval
Nokia Networks, Alcatel-Lucent, Ericsson, NTT DOCOMO

## Slide 2: Deployment scenarios (1/2)
Indoor Hotspot, Dense Urban, Rural, Urban Macro, High Speed as discussed in Wednesday evening session with the following addition:
  Urban Macro user distribution for eMBB:
    20% outdoor in car 30 km/h
    80% indoor 3 km/h
Long range communications (LRC) (System-level or link-level simulation and/or Link-budget calculation for up to 100 km, RAN1 to decide)
  System/link-level simulation for up to 100 km (RAN1 to decide)
  Link-budget calculations as an extension of other coverage-limited scenarios for ranges beyond 100km
High speed (HS) (Link-level simulation)
  BS-to-relay or BS-to-UE in train
  Mobility KPI up to 500km/h is evaluated

## Slide 3: Deployment scenarios (2/2)
URLLC, e.g. eHealth (Link-level simulation)
  Reliability KPI for different sets of packet sizes and reliability/latency levels is evaluated
mMTC deployment scenario
  Separate discussion ongoing
V2X
  Separate discussion ongoing

## Slide 4: KPIs
  User experienced data rate
    Evaluated to show the limits against set targets (not strict requirements)
    FTP traffic model simulation
  Area traffic capacity
    Evaluated to show the limits against set targets (not strict requirements)
    FTP traffic model simulation
  TRP S.E.
    ~3x as an initial target could be revisited later, full buffer simulation
  5% S.E.
    ~3x as an initial target could be revisited later, full buffer simulation
  UP & CP latency
    As agreed in a separate discussion
  Coverage & extreme coverage
    As agreed in a separate discussion
  UE battery life
    Separate discussion ongoing
  Energy efficiency
    Separate discussion ongoing

## Slide 5: Evaluation methodology
The following scenarios are evaluated with system-level simulations:
  Indoor hotspot (InH)
  Dense urban (UMx)
  Urban macro (UMa)
  Rural macro (RMa) w/ ISD1=1732m
  [Long range communications (LRC) (range = 100km)] TBD by RAN1