## Slide 1: Motivation for New SI: NB-IoT RF requirement for coexistence with CDMA
China Telecom, Sprint, SK Telecom, Qualcomm, Huawei, HiSilicon
3GPP TSG RAN Meeting #72
Busan, Korea, 13th – 16th June, 2016
Agenda Item 10.1.4
RP-160770

## Slide 2: Justification
R13 NB-IoT RF requirement was specified based on the NB-IoT coexistence with legacy GSM/UMTS/LTE systems.
Currently, CDMA coexistence with NB-IoT has not be considered in NB-IoT RF requirements evaluation. This will make it difficult for CDMA operators to deploy NB-IoT , and also inter-operator coexistence might be problematic.

## Slide 3: Justification
CDMA system is widely used in many countries such as China, Japan, Korea, US etc. In different regions, the frequencies below 2GHz are mainly used, while 800MHz is the most important frequency band for CDMA network to provide wide coverage.
CDMA2000 Deployments (includes CDMA2000 1X & EV-DO) |  |  |  |  |  | 
 | Asia - Pacific | North America | Caribbean - Latin America | Europe - Russia | Africa - Middle East | Worldwide
Operators | 73 | 63 | 48 | 59 | 71 | 314
Countries/Territories | 32 | 2 | 24 | 14 | 46 | 118
CDMA2000 Devices by Operating Frequency |  |  |  |  |  |  |  |  | 
 | 450 MHz | 800 MHz | 800/1900 MHz | 1700 MHz | 1900 MHz | 2100 MHz | 800/2100 MHz | 800/1900/ 2100 MHz (AWS) | 800/1900/700/ 1700/2100 MHz (AWS)
1X | 124 | 1065 | 478 | 167 | 96 | 1 | 1 | 7 | 14
1xEV-DO Rel. 0 | 21 | 261 | 210 | 92 | 2 | 0 | 12 | 0 | 8
1xEV-DO Rev. A | 45 | 201 | 394 | 8 | 17 | 7 | 39 | 2 | 25
EV-DO Rev. B | 7 | 2 | 4 | 1 | 0 | 1 | 18 | 0 | 2
1X Advanced | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 3
Totals | 197 | 1,529 | 1,091 | 268 | 115 | 9 | 70 | 9 | 52

## Slide 4: Justification
In RAN4#78bis meeting, a WF on handling of CDMA and NB-IoT coexistence study was approved in R4-162833, and the agreements below were reached:
  CDMA and NB-IoT coexistence should be studied.
  Considering the tight schedule of R13 NB-IoT, it is recommended such coexistence study be conducted and evaluated in potential R14 WI/SI.

## Slide 5: Objective
Identify operating bands for interference evaluation on NB-IoT coexistence with CDMA, such as bands around 800M (B5, B26 etc.)
For the NB-IoT stand-alone operation mode, evaluate coexistence requirement between NB-IoT and CDMA, and further evaluate whether R13 NB-IoT RF requirements could be reused or not.
Identify necessary additional RF requirements to ensure NB-IoT for co-existence with CDMA.

## Slide 6: Reference
[1]. R4-162833, Way forward on handling of CDMA and NB-IoT coexistence study, China Telecom, SK Telecom, Sprint, Qualcomm, HuaWei, Intel, ZTE, Samsung, 3GPP TSG-RAN WG4 Meeting #78bis,San Jose Del Cabo, 11 – 15 Apr, 2016