## Slide 1: Motivation of New Work Item Proposal: Enhancement of NB-IoT
Agenda item: 10.1.1
Source: MediaTek Inc
Document for: Discussion
3GPP TSG RAN Meeting #72
Busan, Korea, 13th – 16th June, 2016
RP-161021

## Slide 2: Introduction
LPWA (Low Power Wide Area) IoT market has potential for massive growth
  Diverse applications with diverse requirements in terms of e.g. mobility, data rates: smart metering, fleet management, asset tracking, smart agriculture etc.
Rel-13 NB-IoT provide long battery life and up to 164dB MCL
  Low complexity device
  10 years battery life
  20dB coverage improvement
  Low mobility, low throughput, infrequent small data transmission
Further improvements for NB-IoT needed in Rel-14
  Higher data rates and higher efficiency
  Point-to-multipoint DL transmission for Data distribution.
  Mobility improvement
  Positioning
Unlock new markets
Improve efficiency
Create more value

## Slide 3: Peak Data Rate
Rel-13 NB-IoT peak data rate is limited due to 1 HARQ process and relaxed timing.
  UL: ~ 64kbps
  DL: ~ 28kbps
Rel-14 NB-IoT peak data rate aims at 150kbps/100kbps for uplink and downlink
  Larger TBS: 2000/1000 bits for uplink/downlink  avoid segmentation
  16QAM and redundancy version support for downlink improve DL data rate
  Up to 4 HARQ process for both uplink and downlink  improve peak data rate
1 UL HARQ process: min 16ms to diver max (1000 + 24) bits
8ms
3ms
1 DL HARQ process: min 25/26ms to diver max (680 + 24) bits
3ms
12ms
4ms
4 HARQ process: ~150kbps for UL

## Slide 4: Mobility
Improved connection robustness
  Connected mode mobility
    For MTC systems, devices are expected to use significant DRX in connected mode, also when main part of the time the UEs are in Idle mode.
    We assume that MTC systems shall always be well tuned for low overhead.
    We assume that the need for very high performing mobility, e.g. interruption times < 100ms, is not required for MTC systems
    Thus, in order to allow long DRX in connected mode and not be dependent on timely delivery of measurement report, and to have a low overhead mobility procedure not dependent on signaling in the source cell, we suggest that the method shall be based on Cell Reselection with Cell update in the target cell, where the UE context is fetched from the source cell.
    However, the case that cell reselection happens during an ongoing transmission of a transport block should be avoided, and it could be possible to avoid this by slightly postponing a cell reselection. Also, similar to LTE, forwarding of data from source to target should be supported to avoid higher layer retransmissions. Without Uu signaling in the source cell, the forwarding of data will need to be triggered from the target cell, e.g. by the fetch of the UE context.
    Thus, Means shall be supported to have low loss likelihood at cell change.
  Support for USS reconfiguration
    In Rel-13 there is no trigger for USS/NPDCCH reconfiguration, meaning that all change of coverage level will be done triggered by radio link failure which gives unnecessary overhead and outage. For UEs using the CIOT CP optimizations NAS recovery need to be triggered.
    To have better performance for mobile UEs, it is suggested that it should be possible to reconfigure USS/NPDCCH without Radio Link Failure, i.e. a trigger condition such as a measurement report or CSI information for the serving cell is needed and the possiblity to reconfigure USS/NPDCCH
    We assume this enhancement can be made available to UEs using either CIOT UP optimization or CIOT CP optimization.

## Slide 5: Efficiency
Enhancements to multi-carrier NB-IoT operation
  Non-anchor carrier is a good way to avoid L1 overhead of synchronization signals, MIB and SIB transmissions, which is very significant in a NB-IoT system.
  In Rel-13, the UE is redirected to a non-anchor carrier by RRC in a quite late stage. For small amounts of data, where most of the transmissions are overhead, the possibility for load-sharing between a anchor and a non-anchor carrier is limited, as almost 50% of the transmissions have already taken place on the anchor carrier at the point in time when the UE is redirected to the non-anchor carrier.
  The most straight-forward approach for efficient load sharing between anchor and non-anchor carriers is to have a solution where all transmissions can take place on the non-anchor carrier.
  Thus our proposal is
    RACH on non-anchor carrier
    UE based non-anchor carrier selection, where we assume that this can be a simple random draw function where a UE randomly selects among non-anchor carriers.
More efficient data transmission and better support for heterogeneous traffic model.
  Uplink HARQ with NPHICH, with a NPHICH design to allow uplink early termination or uplink non-adaptive HARQ. This will enhance the efficiency in most cases.
  User data transmission in MSG 3/4 with NPRACH enhancement with optimization of scheduling request/NPDCCH-order-initiated transmissions during connected. We assume that Size of the buffered data for the Scheduling can be supported in Layer 1 by NPRACH enhancement. This will enhance the efficiency for sessions with more data transmissions than the report-response model used for Rel-13.
  PHR report after MSG 3 and CSI reporting are needed for sessions with more data transmissions than the report-response model used for Rel-13.

## Slide 6: Multi-Cast Downlink Transmission
Support for multi-cast downlink transmission
  For the support of distribution of software and of configuration files etc it is suggested to support point to multipoint multicast transmission for the DL.
  We assume that multi-cell transmission would not help much, as most “bad-coverage” spots in a NB-IoT network are assumed to be deep indoor rather than path-loss-limited-between-cells.
  Thus, the NB-IoT multi-cast transmission should use SC-PTM MBMS as baseline.

## Slide 7: Positioning
RAT based positioning categories:
  Category: Simple positioning, with methods that from complexity point of view could be assumed could be supported by all UEs and all networks
  Category: Advanced positioning, with methods that due to complexity would typically be assumed to be supported by some UEs and/or some networks.
  We think ECID methods (except AoA) belong to the first category while OTDOA, UTDOA belong to the second category.
On positioning accuracy:
  No RAT-based positioning technology is expected to be very accurate in bad coverage/deep indoor.
  OTDOA / UTDOA may have good accuracy, depending on physical layer design, LMU density etc, but will for NB-IoT typical deployments (low frequency etc) anyway not be expected to support very fine granularity, e.g. it is not likely to support discrimination between two neighbor parking meters, not likely to support discrimination between items in different aisles/shelves in a warehouse.
  ECID / pattern matching have varying accuracy, but can be expected to be useful e.g. to determine at which terminal a certain packet is (for logistics packet tracking), between which terminals the packet is, if en-route, and also discriminate between streets etc in urban radio deployments.
Our proposal is to Support ECID positioning
  Support for eNB measurements on NPRACH
    It is assumed that PDCCH order is used to trigger NPRACH for positioning.
  Support for UE report of Neighbor cell RSRP measurements.

## Slide 8: Appendix

## Slide 9: Early Termination or Non-adoptive HARQ
Opt 1: One transmission targeting to 10% or lower BLER
Opt 2: Retransmission triggered by NPDCCH
Opt 3: 1 bit ACK and NACK or NACK only
Opt 4: 1 bit ACK only(Early Termination)
NPUSCH
NPUSCH
NPDCCH
NPUSCH
NPUSCH
NPUSCH
NPDCCH
NPDCCH
NPDCCH
NACK
NPUSCH
NPUSCH
NPUSCH
ACK
Resource can be used
for other DL traffic
NPDCCH
Scheduled a large # of rep
Opt 2-3 vs Opt 1:
Less NPUSCH transmission time
  30%~40% power consumption
  and UL resource saving
Opt 3-4 vs Opt 2:
Less DL resource
  60%~96% DL resource saving
Conclusion:
NPHICH design to allow uplink early
termination or uplink non-adaptive
HARQ shall be introduced for Rel-14.
Rel-13

## Slide 10: Early Termination or Non-adoptive HARQ
 |  | Time (ms) |  |  | Power saving | UL resource Saving | DL resource Saving | BLER
 |  | Tx | Rx | stand by |  |  |  | 
MCL = 164dB | One transmission | 288 | 0 | 0 |  | Reference |  | 0.128
 | Retransmission trigger by NPDCCH | 206.2608 | 18.56 | 0 | 28.38% | 28.38% | Reference | 0.0622
 | ACK and NACK | 192.696 | 2 | 2.13 | 33.09% | 33.09% | 89.22% | 0.0551
 | ACK only | 193.0368 | 1.4484 | 2.1416 | 32.97% | 32.97% | 92.35% | 0.0622
 | NACK only | 206.2608 | 0.58 | 4 | 28.37% | 28.38% | 96.88% | 0.0622
MCL = 148.8dB | One transmission | 64 | 0 | 0 | - | Reference | - | 0.108
 | Retransmission trigger by NPDCCH | 36.3671 | 0.2656 | 0 | 43.18% | 46.65% | Reference | 0.051168
 | ACK and NACK | 34.14605 | 0.08 | 2.2032 | 46.63% | 46.46% | 69.88% | 0.043824
 | ACK only | 34.26355 | 0.059927 | 2.213824 | 46.44% | 43.18% | 77.88% | 0.051168
 | NACK only | 36.3671 | 0.021248 | 4 | 43.14% | 43.18% | 92.00% | 0.051168
Chart: TBS=328 MCL=164dB I_TBS =3
| 2 | 3 | 4 | 5 | 6 | 7
3.75 | 0.654 | 0.45 | 0.29 | 0.19 | 0.128 | 0.079
Early termination enable
Chart: TBS=328 MCL=148.8dB I_TBS=10
| 1 | 2 | 3 | 4
15 | 0.826 | 0.2656 | 0.165 | 0.108
Early termination enable
Either saving on
UL resource
/power consumption
Or DL resource
Both UEs in extreme coverage and extended coverage can benefit from it.
Less number of UEs in poor coverage occupy most of the resource (~50% based on model in TR 45.820)