## Slide 1: 3GPP TSG RAN Meeting #72 Busan, South Korea, June 2016
Motivation for further enhancement of IoT for LTE

## Slide 2: Justification
In Rel-13, two work items, i.e. eMTC and NB-IoT, were one of the first industry efforts to address the requirements of cellular internet of things.
As the number of devices increase drastically, it is important to ensure that large amounts of IoT devices and IoT traffic can be handled efficiently in the networks and that new service requirements can be satisfied:
  Requirements for device location
  Requirements for efficient firmware upgrades
  Requirements to accommodate massive number of IoT devices while maintaining adequate system efficiency

## Slide 3: Objectives
Positioning support
Multi-cast enhancements
Multi-Carrier enhancements
Mobility enhancements

## Slide 4: Positioning
Study and specify new reference signal to support positioning for in-band, guard band, and standalone deployment scenarios and for coverage enhancement scenario. [RAN1, RAN4]
Study and specify enhancements on control plane overhead reduction and UE power consumption reduction. UEs in both RRC-connected/idle mode should be considered [RAN2]

## Slide 5: Multi-cast enhancements
Study and specify means to enable both MBSFN and SC-PTM reception in both normal and enhanced coverage [RAN1, RAN2]:
  Reuse the Rel-13coverage enhancement technology as much as possible.
  Develop new scheme for MBSFN and SC-PTM, if needed.
Specify means to optimize UE power consumption for both MBSFN and SC-PTM [RAN2]
  Enhanced MBMS service data scheduling
  Optimize UE power consumption in monitoring MCCH
Specify means for reliable support of multicast traffic types, e.g. for software update [RAN1, RAN2]

## Slide 6: Multi-carrier enhancements
Specify enhancements for multiple carriers in a single cell [RAN1, RAN2]：
  Multiple configured NB-IoT carriers for NPRACH transmission
  Paging transmissions on non-anchor carrier(s) for load balancing
  Cross carrier dynamic scheduling for unicast transmissions
Specify enhancements for multiple cells configured with multiple carriers [RAN1, RAN2]：
  Optimization of load balancing solutions for NB-IoT devices in RRC-IDLE/connected

## Slide 7: Mobility enhancements
  Evaluate the synchronization performance of mobility scenarios, e.g. the accuracy of TA. Based on the evaluation results, specify necessary enhancement [RAN1]

## Slide 8: Thank you