## Slide 1
Motivation for new WID on latency reduction by processing time reduction
Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG RAN Meeting #72
Busan, Korea, June 13 - 16, 2016
Agenda Item: 10.1.1
RP-161045

## Slide 2: Background
The Study Item on Latency Reduction Techniques considered shorter TTI lengths along with reduced processing times.
  Significant improvement in User Perceived Throughput (UPT) has been observed.
  Shorter TTIs call for a significant re-design of L1, including DL and UL control and data channels (PDSCH, PDCCH & PUSCH, PUCCH) and corresponding demodulation reference signals
On the other hand, processing times can also be reduced while keeping the TTI length unchanged.
Furthermore, the gains for shorter TTI diminish if processing times are not reduced accordingly, as shown in our R1-165928 contribution (using the processing time reductions captured in the SI TR)

## Slide 3: Performance with a file size of 100kB
With similar processing time assumptions, 1ms TTI, 7-symbol TTI & 2-symbol TTI perform similarly

## Slide 4: Performance with a file size of 500kB
With similar processing time assumptions, 1ms TTI, 7-symbol TTI & 2-symbol TTI perform similarly

## Slide 5: Observations
Reducing the TTI length alone will not bring the envisioned latency reduction benefits for LTE radio
Reduced latency can also be achieved with the legacy 1ms TTI and channel design by reducing the packet processing times
  This will enable early implementation and roll-out without the need to rely on new channel design for PDSCH, PDCCH, PUSCH, PUCCH and the corresponding demodulation reference signals
Note: When TTI length is shortened, the allowed processing times should be reduced linearly to achieve optimal gains.

## Slide 6: Proposed WID
Objective:
  Specify reduced processing times for UL grant to UL data and for DL data to HARQ feedback for legacy 1ms TTI operation

## Slide 8: Overview of simulated cases
 | 14 symbol TTI |  | 7 symbol sTTI |  | 2 symbol sTTI | 
 | TCP ssthresh = 45 * MSS, SR waiting time =1ms for 14 OS, 1ms for 7 OS, 0.5ms for 2OS |  |  |  |  | 
 | UL access delay | RTT | UL access delay | RTT | UL access delay | RTT
[n+2] | 5 TTI | 4 TTI | - | - | - | -
[n+3] | 7 TTI | 6 TTI | - | - | - | -
[n+4] | 9 TTI | 8 TTI | 10 sTTI | 8 sTTI | 12 sTTI | 8 sTTI
[n+8] | - | - | 18 sTTI | 16 sTTI | 20 sTTI | 16 sTTI

## Slide 9: Simulation Assumptions
Parameter | Assumption
System bandwidth | 20 MHz
Duplex mode | FDD
Carrier frequency | 2GHz
Cell layout | Hexagonal grid, 7 sites, 21 cells per site, with wrap-around
Number of UEs per macro sector | 10 (80% indoor, 20% outdoor)
Inter-site distance | 500m
UE speed | 3 km/h, quasi-static model
Antenna configuration | 2x2, cross-polarized
Receiver DL | LMMSE-IRC
eNB TX power | 46 dBm
eNB antenna height | 25 m
Antenna pattern | 3D
UE Tx power | 23 dBm
UE antenna height | 1.5 m
Channel model | 3D-UMa
Pathloss model | UMa, with 3D distance between eNB and UE
Shadowing | UMa, with 3D distance between eNB and UE
Penetration loss | Outdoor UEs: 0 dB, Indoor UEs: 20 dB+0.5din
CSI feedback period | 5 ms
Feedback mode | 3-1
CSI report delay | 6 ms
Channel and interference estimation | Ideal
UL access delay | 16/14/12/10/8 sTTIs + SR period waiting time
HARQ RTT | 16/14/12/10/8 sTTIs
SR period waiting time | 1ms for 7/14 OS sTTI/TTI while 0.5 ms for 2OS
DRX | Disabled
Transport type | TCP
TCP ACKs | Error-free
Initial TCP Window | 3 x 1500 Bytes (MSS), RFC 5681, section 3.1
Initial Ssthresh | 45 x 1500 Bytes (MSS)
Ssthresh | Dynamic according to RFC 5681, sections 3.1 and 3.2
FTP file size | FTP 3 0.5 MB/0.1MB
User Packet arrival rate λ | FTP model 3 with packet arrival according to Poisson process: [0.25, 0.5, 0.75] and [1.25, 2.5, 3.75] for 500KB and 100KB, respectively.
Scheduler | TD: PF, FD: PF
Maximum number of scheduled users per TTI | 10 (max)
L1 overhead | CRS with dynamic number of CCEs according to Num. of scheduled UEs
Core network delay | 2 ms
TTI Length | 14OS, 7OS, 2OS
MCS | QPSK, 16 QAM, 64 QAM
Network synchronization | Synchronous
Control overhead | Dynamic per sTTI SINR dependent, UL grants and DL assignment