## Slide 1: Motivation for WID on LTE MTC and NB-IoT enhancements
RP-161152
3GPP RAN #72 Busan, Korea, June 2016
Agenda item: 10.1.1

## Slide 2: General motivation
Rel-13: eMTC and NB-IoT introduced features to support:
  Low cost/complexity
  Reduced power consumption
  Enhanced coverage
Rel-14: Extend eMTC and NB-IoT by
  enhancing the existing operation
  enabling eMTC/NB-IoT features in other types of UEs

## Slide 3: Summary of objectives
New features:
  Positioning: Essential for asset tracking and wearables
  Multi-cast transmission: Essential for effective delivery of software update of MTC UEs.
General enhancements:
  Physical layer enhancements to increase coverage, spectral efficiency, and power efficiency.
  Mobility enhancements for NB-IoT
Enabling eMTC/NB-IoT features in other types of UEs
  Reduced power consumption by bandlimited operating mode
  Enhanced coverage

## Slide 4: Positioning support
Many IoT applications require mobility and positioning services
  Essential for asset tracking, emergency scenarios
Downlink based positioning, similar to legacy LTE
  OTDOA based
  RSRP/RSRQ based
  UE Rx-Tx time difference based
Main design goals:
  Keep commonality with legacy LTE when possible
  Reduced bandwidth operation
  Enhanced coverage

## Slide 5: Multi-cast downlink transmission
With long battery life and low cost, deployed UEs may target ~10 years of life
  Over-the-air software update is essential to introduce new functionalities
Unicast transmission is not efficient to deliver information to a massive number of UEs
Multi-cast transmission provides support for effective transmission to multiple UEs
Need to introduce enhancements to MBSFN/SC-PTM to support:
  Coverage enhancements
  Narrowband operation

## Slide 6: Physical layer enhancements for eMTC
Proposals to increase coverage, capacity and power efficiency
Synchronization signal improvements:
  The coverage of PSS/SSS/PBCH may be the limiting factor in some scenarios
  Enhancing the synchronization sequence provides increased coverage and reduced power consumption
Multiplexing of multiple UEs in 1 PRB for uplink transmission:
  Power limited UEs do not benefit from increased resource allocation
  Multiplexing multiple UEs in 1 PRB increases the system capacity while maintaining each UE data rate
Enable early determination of presence of control channel transmission for power savings:
  UEs in good coverage are able to early decode control channels, but may not be able to determine that no transmission is present
    Need to know additional information about precoding, power, etc. (power for EPDCCH/DMRS may be different from CRS power)
  Especially useful for monitoring of MPDCCH for paging
  Introduce mechanisms to enable early detection in Rel-14

## Slide 7: Physical layer and mobility enhancements for NB-IoT
Proposals to increase power and spectral efficiency, and enable mobility
Mobility enhancements:
  Rel-13 NB-IoT has reduced mobility support (only idle mode mobility)
  For transmission of longer packets in mobile scenarios, support of handover is essential
  Introduce necessary mechanisms to provide measurements and connected mode mobility procedures
CSI feedback:
  Due to the lack of CSI feedback in Rel-13, rate adaptation algorithms cannot follow fast channel variations
  Introduce simplified feedback mechanisms to increase data rates and reliability in mobile scenarios
PAPR reduction techniques:
  Rel-13 NB-IoT supports low PAPR modulation, but only for very low data rates (single tone)
  Supporting low PAPR modulation schemes for multi-tone assignments will enable higher PA efficiency or simpler PA architecture while maintaining higher data rates

## Slide 8: Enhancements for high category UEs
eMTC features for higher category UEs:
  Extended coverage mode: Enables low rate services in bad coverage conditions
  Low power mode: Enables low power consumption when UE does not require high data rates
Some of these mechanisms are enabled in Rel-13, but enhancements are needed to
  enable seamless transition between modes
  enable initiation of bandlimited operation by a UE for low power consumption