## Slide 1: Motivation for CR on eDRX Paging Hyper-Frame and PTW_Start Calculation
Agenda item: 14.2.6
Source: Intel Corporation, NTT DOCOMO, INC., Samsung, Sequans
Document for: Discussion
3GPP TSG RAN Meeting #72 RP-161157
Busan, Korea, 13th – 16th June 2016

## Slide 2: Background
RAN2 agreed to update eDRX Paging Hyper-Frame (PH) calculation aiming to address the issues identified in [R2-164514].
In post meeting email discussion “[94#15][LTE/eDRX] eDRX Paging Hyper-Frame Calculation”, the CR [R2-164574] to 36.304 was agreed proposing to change the PH calculation to use UE_ID_H instead UE_ID:
  The H-SFN satisfying the H-SFN mod TeDRX,H = (UE_ID_H mod TeDRX,H) where
    TeDRX,H is eDRX cycle of UE in Hyper-Frames
    UE_ID_H = floor(IMSI/16384) mod 1024
RAN2 also discussed potential changes to the start of the paging time window (PTW_start), however could not conclude on this within the deadline.
This document shows the concerns associated with current PTW_start calculation, and the benefits associated with two options that received most support during the email discussion.

## Slide 3: Rel-13 eDRX PTW_start discussion (1/5)
Current PTW_start calculation (baseline)
  PTW_start SFN = 256 * ieDRX, where ieDRX = floor(UE_ID/TeDRX,H) mod 4
 | Baseline
Max. # of UEs monitoring same SFN | 126
Total # of unused SFN | 824 (80.46%)
Total # of UEs scheduled for PO in this H-SFN | 12602
Current PTW_start (baseline)
Current PTW_start calculation leads to
  higher number of subframes where no UE checks for paging, and
  higher number of UEs monitoring paging on the same subframes
  Uneven Paging load distribution,
  Available SFN for paging is not utilized to its full potential
Notes: BL = Bandwidth reduced Low complexity
MT = Mobile Terminated calls

## Slide 4: Rel-13 eDRX PTW_start discussion (2/5)
    PH calculation uses “UE_ID_H = floor(IMSI/16384) mod 1024” (as per [94#15])
Current PTW_start calculation (baseline)
  PTW_start SFN = 256 * ieDRX, where ieDRX = floor(UE_ID/TeDRX,H) mod 4
Proposed solutions to PTW_start calculation that received most support:
  Option 1: uses the UE_ID_H for the PTW_start calculation
    PTW_start SFN = 256 * ieDRX_H, where ieDRX_H = floor(UE_ID_H/TeDRX,H) mod 4
  Option 2: use 2 MSBs from UE_ID for PTW_start calculation and different equation is used depending the UE_ID length agreed for eMTC vs LTE/NB-IoT:
    Case A: For UE monitoring PDCCH or NPDCCH:
      PTW_start SFN = 256 * ieDRX, where ieDRX = floor(UE_ID/256) mod 4 and,
      UE_ID = IMSI mod 1024
    Case B: For UE monitoring MPDCCH:
      PTW_start SFN = 256 * ieDRX, where ieDRX = floor(UE_ID/4096) mod 4 and,
      UE_ID = IMSI mod 16384
Notes: BL = Bandwidth reduced Low complexity
MT = Mobile Terminated calls

## Slide 5: Rel-13 eDRX PTW_start discussion (3/5)
Opttion1- PTW_start using UE_ID_H
 | Option 1 | Option 2 case A/B
Max. # of UEs monitoring same SFN | 40 | 41
Total # of unused SFN | 224 (21.87%) | 224 (21.87%)
Total # of UEs scheduled for PO in this H-SFN | 12556 | 12580
Option 2 case A - PTW_start using UE_ID = IMSI mod 1024
  Option1 and Option 2 improves the paging load distribution reducing the # of unused SFN for paging DRX parameter of nB = T, DRX cycle = 128
Option 2 case B - PTW_start using UE_ID = IMSI mod 16384
DRX cycle (T) = 128 and nB =T (with UE_ID_H = floor (IMSI/16384) mod 1024)

## Slide 6: Rel-13 eDRX PTW_start discussion (4/5)
DRX cycle (T) = 256 and nB =4T (with UE_ID_H = floor (IMSI/16384) mod 1024)
  The impact of changing nB from T to 4T is observed when comparing on terms of sub-frames (PO) – the paging load on SFN (PF) level is the same.
    E.g., assuming 25 UEs scheduled at a PF; for nB=T, all 25 UEs monitor PO = 9 where as for nB = 4T, 25 UEs are spread over PO = 0, 4, 5 and 9 for paging monitoring.
  For Option 2 Case A, only 1 subframe will be used for each PTW_start while for a total of 4 available subframes for nB=4T, DRX cycle = 256
 | Baseline | Option 1 | Option 2 Case A | Option 2 Case B
Max. # of UEs monitoring same sub-frame (PO) | 26 | 11 | 26 | 11
Total # of unused sub-frames (PO) | 9440 (92.18%) | 7187 (70.18%) | 9440 (92.18%) | 7189 (70.2%)
Total # of UEs scheduled for PO in one H-SFN | 12497 | 12685 | 12394 | 12528
  Option2 may not fix the distribution problem for all DRX parameter

## Slide 7: Rel-13 eDRX PTW_start discussion (5/5)
The differences of Option 1 and Option 2 are summarize as follows:
Comparison Item | Option 1 | Option 2 (Case A, B)
Applicability for all paging DRX parameter | YES | NO
Simplicity | SIMPLE (one equation) | LESS SIMPLE (different equation for non-eMTC and for eMTC
Proposal: To agree to adopt Option 1 of PTW_Start equation
    PTW_start SFN = 256 * ieDRX_H, where ieDRX_H = floor(UE_ID_H/TeDRX,H) mod 4

## Slide 8: Rel-13 eDRX PH discussion for NB-IoT
The eDRX cycle is up to 256 H-SFN for LTE/eMTC (i.e. 43.69min) and up to 1024 H-SFN for NB-IoT (i.e. 2.91hours), therefore the agreed definition for UE_ID_H to “(IMSI/16384) mod 1024” needs to be updated at least for NB-IoT
  Alternatives proposed to addressed this issue:
    Alt. 1:
      if P-RNTI is monitored on PDCCH or MPDCCH,
        UE_ID_H = floor (IMSI/16384) mod 1024
      if P-RNTI is monitored on NPDCCH
        UE_ID_H = floor (IMSI/16384) mod 4096
    Alt. 2: (common for all UEs)
      UE_ID_H: floor (IMSI/16384) mod 4096
  The paging distribution properties are maintained when using the new “UE_ID_H = (IMSI/16384) mod 4096” (results in Annex)
  Proposal: To agree to adopt Alt.1 or Alt.2 of UE_ID_H definition
Note that these enhanced PH, PTW_start equations work on the assumption that the related IMSI bits provides the necessary random property.

## Slide 9: Appendix

## Slide 10: Rel-13 eDRX PTW_start discussion (1/2)
The paging distribution properties are maintained when changing the PH calculation with new “UE_ID_H = floor (IMSI/16384) mod 4096” - instead of “(IMSI/16384) mod 1024”.
DRX cycle T = 128, nB = T (with UE_ID_H = floor (IMSI/16384) mod 4096)
 | Baseline | Option 1 | Option 2 (Case A, B)
Max. # of UEs monitoring same SFN | 121 | 41 | 42
Total # of unused SFN | 824 (80.46%) | 224 (21.87%) | 224 (21.87%)
Total # of UEs scheduled for PO in one H-SFN | 12452 | 12549 | 12486

## Slide 11: Rel-13 eDRX PTW_start discussion (2/2)
DRX cycle T = 256, nB = 4T (with UE_ID_H = floor (IMSI/16384) mod 4096)
 | UE_ID_H = floor (IMSI/16384) mod 4096 |  |  | 
 | Baseline | Option 1 | Option 2 Case A | Option 2 Case B
Max. # of UEs monitoring same sub-frame (PO) | 23 | 11 | 24 | 11
Total # of unused sub-frames | 9431 (92.09%) | 7183 (70.14%) | 9440 (92.18%) | 7163 (69.95%)
Total # of UEs scheduled for PO in one H-SFN | 12415 | 12507 | 12530 | 12400
  The paging distribution properties are maintained when using the new “UE_ID_H = (IMSI/16384) mod 4096”

## Slide 12: Simulation parameters