## Slide 1: DL multicast enhancements for V2X
Huawei, Intel, Orange, Telecom Italia, Deutsche Telekom, China Mobile, China Telecom, Oppo, HiSilicon
3GPP TSG RAN Meeting #72 RP-161256
Busan, South Korea, June 13- 17, 2016
Document for: Decision
Agenda Item: 10.1.1

## Slide 2: Background (1)
  Conclusion of V2X Study Item (TR 36.885) on DL multicast enhancements:
The RAN WGs identified solutions to improve the latency, capacity, and reliability performance of LTE Uu interface and observed that UL enhancements to the SPS protocol and DL enhancement to multicast/broadcast are beneficial from performance perspective. It is recommended to support the following solutions identified in this TR for Uu-based V2X:
  Transmission using a single CP shorter than extended CP, with normal CP as the baseline, with necessary additional study
  HARQ feedback and retransmissions for SC-PTM and MBSFN, with necessary additional study

## Slide 3: Background (2)
  Conclusion of Rel-13 SC-PTM Study Item (TR 36.890): SC-PTM transmission without UL feedback performs significantly better than MBSFN transmission in the following 3 cases:
    when the network is not synchronized;
    when users receiving a service are all in 1, 2 or 3 cells;
    when the MBSFN area is pre-defined and contains a number of cells with no user receiving the service.
  V2X is local area broadcast/multicast (e.g. area only contains 2-3 cells), this is because one vehicle is only required to delivery its V2X messages to other vehicles within the distance of 300m (Highway) or 150m(Urban), as per SA1 requirement. So, SC-PTM is a better choice for V2X compared to MBSFN in terms of DL capacity.

## Slide 4: Proposal
Proposal: In V2X WI, support of UL feedback (i.e. HARQ and CSI feedback) and retransmissions for SC-PTM transmission.
  In V2X WI, it is beneficial to support UL feedback (i.e. HARQ and CSI feedback) for SC-PTM:
    To increase the reliability based on ACK/NACK feedback, especially for vehicles in cell edge.
    To increase the spectrum efficiency, since the eNB can select more aggressive MCS based on the UL feedback.