## Slide 1: Way forward on remaining open issues in TR38.913
3GPP TSG-RAN Meeting #72 RP-161308 Busan, Korea, June 13 - 16, 2016
AI 9.2.2
Document for discussion/approval
NTT DOCOMO, CMCC

## Slide 2: Motivation
The email discussions kicked-off after RAN#71 resolved the majority of the open issues in 38.913.
However, there are still a few remaining open issues to be addressed.
This contribution provides a way forward on the remaining open issues in 38.913

## Slide 3: (1) 4. Introduction
Open issue:
The following two square brackets are remaining.
[Brief descriptions of deployment scenarios for next generation access technologies to be developed in this TR]
[Brief descriptions of requirements for next generation access technologies to be developed in this TR]
Proposed action:
Remove the text in the square brackets from the TR.
Add the following text instead:
“A set of requirements have been defined, so that the fulfilment of these will make the New Radio support the usage scenarios eMBB, mMTC, and URLLC. To ensure a wide operating range, a set of deployment scenarios has also been identified, ranging from indoor to rural.”

## Slide 4: (2) 7.6. Latency for infrequent small packets
Open issue:
No requirement captured for this KPI.
Proposed action:
- Remove this KPI if no requirement is introduced until RAN#73.

## Slide 5: (3) 7.17 Connection density
Open issue:
QoS definition is missing for this KPI.
Proposed action:
- Add QoS definition to the definition as follows if there is not proposal on the definition:
“Connection density refers to total number of devices fulfilling a target QoS per unit area (per km2), where the target QoS is to deliver within 10s an amount of data of 200 bytes per day with 99% success probability.”

## Slide 6: (4) Mapping between deployment scenarios and usage scenarios for each KPI
Open issue:
The most of tables on mapping between deployment scenarios and usage scenarios for each KPI are empty in Chapter 7.
Proposed action:
Remove empty tables and only leaves tables with numbers.
Strike through empty cells for tables with numbers for only a subset of deployment scenarios or usage scenarios.

## Slide 7: (5) Evaluation methodologies for TR38.913 KPIs
Open issue:
The evaluation methodology for each KPI is not clarified in the TR.
Proposed action:
Propose to add a new section at the end of chapter 7 as shown in the next slide to include the mapping table based on RAN#71-11 and RAN#71-03/RAN#71-06 discussion outcomes.

## Slide 8
Section | KPI | Evaluation methodology | Relevant deployment scenario
7.1 | Peak data rate | Analytical evaluation | N/A
7.2 | Peak spectral efficiency | Analytical evaluation | N/A
7.3 | Bandwidth | Inspection | N/A
7.4 | Control plane latency | Analytical evaluation | N/A
7.5 | Use plane latency | Analytical evaluation | N/A
7.6 | Latency for infrequent small packets | Analytical evaluation | N/A
7.7 | Mobility interruption time | Analytical evaluation | N/A
7.8 | Inter-system mobility | Inspection | N/A
7.9 | Reliability | Link level evaluation | N/A
7.10 | Coverage and extreme coverage | Link budget / link level analysis | Extreme long distance coverage in low density areas
7.11 | UE battery life | Analytical evaluation | N/A
7.12 | UE energy efficiency | Inspection | N/A
7.13 | Cell/TRP spectral efficiency | A joint system level evaluation | Indoor Hotspot, Dense Urban, Rural, Urban Macro, High speed
7.14 | Area traffic capacity |  | 
7.15 | User experienced data rate |  | 
7.16 | 5th percentile user spectrum efficiency |  | 
7.17 | Connection density | [Analytical evaluation and system level simulation] | [Urban coverage for massive connection (Urban environment)]
7.18 | Mobility | Link level evaluation with deployment scenario specific operating point | [Rural] [High Speed]
7.19 | Network energy efficiency | Inspection and system level evaluation | For inspection: NA For system level evaluation: at least in 2 deployment scenarios: one coverage limited environment (ex: Rural) AND one capacity limited environment (ex: Dense Urban)
7.20 Evaluation methodology
This section describes the evaluation methodology and relevant deployment scenario
of each KPI in the TR. This is summarized in Table 7.20.1.
Table 7.20-1: Evaluation methodology and relevant deployment scenario for each KPI
  References: RP-160961, RP-160962, RP-160963, RP-160964, RP-160965, RP-160966, RP-160967, RP-160968, RP-160969, RP-160970, RP-160884, RP-160885, RP-160805

## Slide 9: (6) Editorial issue
Do update Table 6.1.2-1 in the TR by removing the square bracket in Table 6.1.2-1 on the number of users per TRP.
This was already resolved in RP-160672 at the RAN#71 meeting.
This is an editorial issue.

## Slide 10: (7) Editor’s notes
Open issue:
There are still some Editor's notes in Section 3.1, 4, 6.1.4, 6.1.8, 6.1.9, 7.3, 7.6, 7.8, 7.9, 7.17, 7.19, 10.1.2.
Definition of terminology TRP in section 3.1
Proposed action:
Propose to solve the issues of Editor's notes by RAN #73.
Email discussions after RAN #72 should be kicked off.