## Slide 1: Motivation for Study on Multimedia Enhancements for LTE
Agenda item: 10.1.2
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN Meeting #74 RP-162045

## Slide 2: Content
Motivation
Objectives of the study
Appendix

## Slide 3: Motivation 1
Issue with conversational video calls
  Degradation of perceived conversational video (real-time streaming) quality is observed e.g. video jumps, freezes and higher latency under UL radio congestion in different cases.
  The problem may also occur for HTTP based streaming. In this case the critical data would be the IP packets which carry the video frames which are encapsulated in html5 data.
  Existing solutions such as bitrate adaptation based on End-to-End bandwidth estimation or FEC (Forward Error Correction) are not sufficient for a good perceived video quality or may lead to an even more congested network.
  Note: This issue was confirmed by RAN2 in RAN2#95bis when it was initially discussed in the context of the RAN3-led Context Aware Service Delivery SI

## Slide 4: Issue with conversational video calls (1/5)
Case 1: critical UL video data may be lost due to PDCP discard timer
  Video decoder is less robust against packet loss than VoLTE as the quality of decoded frames (or picture) depends on the preceding frames. For example:
    If an I-frame (critical video data) is not fully received, it is typically perceived as small video freeze or jump up to few seconds.
      I-frame (Intra Coded Picture): key frame not relative to any other frame in the sequence
        Critical Video data
      P-frame (Predictive Coded Picture): compressed frame relative to previously decoded frames
        Non-critical Video data
    Some RTCP feedbacks (FIR, PLI, NACK) can also be considered as critical data.

## Slide 5: Issue with conversational video calls (2/5)
Case 2: critical UL video data may be lost due small UL grant allocation
  Under UL radio congestion (e.g. in highly loaded cells or bad UL radio conditions), average transmission time of longer video frames (typically I-frame) exceeds PDCP discard timer.
    The video bitrate and ratio of I-frame/P-frame are not constant, therefore the size of video frames may vary significantly.
Case 3: critical UL video data cannot be differentiated because any video data (critical or not) is sent on same bearer.
  eNB cannot differentiate UEs with non-critical vs other ones with critical video data so that the UE with critical video data could get enough UL grant(s) before the PDCP timer expires.

## Slide 6: Issue with conversational video calls (3/5)
Exemplary use case: IR.94 video call in lossless Loopback mode (i.e. a received UL packet is always sent in DL) to analyze the impact under UL congested situation (by limiting the available RBs granted to the UE).
Channel allocation | Available UL radio bitrate | Achieved average UL video bitrate | Comments
Full UL capacity (i.e. non UL congestion) | 3112 kbps (RB=30, TBSI=6, QPSK, 389 byte/MAC_grant) | ~367 kbps | Video bitrate reaches negotiated CBP1.2 bitrate (384kbps) and is not constrained by available radio bitrate
UL congestion | 392 kbps (RB=4, TBSI=6, QPSK, 49 byte/MAC_grant) | ~280 kbps | Video bitrate is constrained by available radio bitrate
392 kbps
3112 kbps
Uplink
3112 kbps
Downlink
CMW loopback
Congest
“Foreman” video sequence

## Slide 7: Issue with conversational video calls (4/5)
Exemplary measurement: impact of the PDCP discard timer on video bitrates and critical data (I-frames)
    When congestion is detected on higher layers, UE performs bitrate adaption (e.g. by TMMBR) based on video End-to-End bandwidth estimation (green curve shown in figure). However this upper layer adaptation mechanism might not be sufficient for a good perceived video quality, specially under UL radio congestion conditions.
      For example, video jumps/freezes might happen, as shown in the figure by the pink dashed bubbles; these correspond to frames that are not decoded or played out because some I-frames were not fully received due to PDCP discards on some of their RTP packets.
PDCP discards
Impacting I-frame
Yellow areas mean PDCP discards happened, some frames were not decoded and decoded video bitrate dropped
Congestion 3112 → 392 kbps
De-congestion
392kbps→ 3112 kbps
Video freezes
Time (hh:mm:ss)
Bitrate
(kbps)
Legend
Encoder set to 1 I-frame sent / 2 seconds
I-frame received with no PDCP discard
I-frame with PDCP discard (either received with retransmission or not fully received)
Estimated E2E bandwidth (kbps)
Decoded bitrate (kbps)
Encoded bitrate (kbps)
Channel bandwidth (kbps)
Notes: TMMBR - Temporary Maximum Media Stream Bit Rate. In case of UL congestion, this mechanism may not be sufficient.

## Slide 8: Issue with conversational video calls (5/5)
Exemplary measurement: impact of the PDCP discard timer on critical data (I-frame)
Older RTP video packets get discarded by PDCP and are not transmitted: higher probability a (big) I-frame gets impacted since more packets will sit in UL PDCP queue waiting to be transmitted
Video fluidity (video jumps, lower frame per sec) degraded due to I-frames not received (red bubbles) and sometimes also surrounding P-frames
(no bubble shown in graph for clarity)
18 I-frame received w/o re-tx → No PDCP discard (green bubbles)
Total 24 I-frame during congestion period (1min) 7 I-frame received w >= 1 re-tx → PDCP discard, and Re-tx success (red bubbles)
1 I-frame not completely received → PDCP discard, and Re-tx discard again (red bubble)
Legend
Encoder set to 1 I-frame sent / 2 seconds
I-frame received with no PDCP discard
I-frame with PDCP discard (either received with retransmission or not fully received)
Encoded video frame size (KByte)
Time (hh:mm:ss)
Video
Frame
size
(KByte)
Congestion starts
Congestion ends
PDCP discards
Impacting I-frame
Notes: CBP1.2: It corresponds to the Constrained Bitrate Profile negotiated during IMS IR94 session. It corresponds to “Low resolution” codec including 384kbps bitrate, 353x288 CIF resolution, 15 frame/second

## Slide 9: Motivation 2
Issue with uncompressed header in RoHC
  In order to ensure high-quality voice services over E-UTRAN, the UE and network are required to support RoHC acc. to GSMA IR.92 (IMS Profile for Voice and SMS).
    At minimum, the UE and network must support RTP/UDP/IP profile (0x0001) for RTP packets and UDP/IP profile (0x0002) for RCTP packets.
    The UE and network must support these profiles for both IPv4 and IPv6.
  Header compression has a significant impact on the performance of VoLTE. However, during an ongoing VoLTE session there are cases where the RoHC compressor may send uncompressed header. In this case the coverage of UL voice data transmission will be impacted.
  Existing mechanisms are not sufficient to improve the VoLTE performance when UL voice data carrying uncompressed header need to be transmitted.

## Slide 10: Issue with uncompressed header in RoHC (1/2)
RoHC compresses the RTP, UDP, IP header in case of IPv4 from 60 Bytes to 3 Bytes
But the headers may be sent uncompressed even when RoHC is enabled
  At the beginning of a session, as part of initial context establishment, the full header is sent (i.e., transmission without protocol header compression).
  In case of VoLTE packet failures at PHY (after HARQ; no ARQ at RLC or application layer for VoLTE), the receiver may send RoHC feedback to notify a bad synchronisation of the RoHC context. The header compressor at the TX side transmits the full header information as part of the “Refresh and re-initialization” of the RoHC context.
  In case of periodic refresh of the RoHC context, for instance when RoHC mode is uni-directional.

## Slide 11: Issue with uncompressed header in RoHC (2/2)
  Timing budget constraint (40ms) and assuming only initial transmission without HARQ retransmissions
  FD-FDD: # of repetitions ≤ time budget
  HD-FDD: # of DL repetitions + # of UL repetitions + 1 ≤ time budget
  Maximal coverage
  Key observation
    There can be a coverage difference as large as 6dB when comparing use of compressed vs. uncompressed headers
Example of timing relationship for HD-FDD, where PDSCH and PUSCH are SPS scheduled, and PUCCH has no repetition, which punctures PUSCH.
BLER=2% |  | 40ms with header compression |  |  |  |  | 40ms without header compression |  |  |  | 
Frame type | PDSCH Rx antenna | DL RLs | DL MCL | UL RLs | UL MCL | Overall MCL | DL RLs | DL MCL | UL RLs | UL MCL | Overall MCL
FD-FDD | 1 | 16 | 144.96 | 32 | 142.08 | 142.08 | 16 | 139.06 | 32 | 136.37 | 136.37
FD-FDD | 2 | 16 | 150.46 | 32 | 142.08 | 142.08 | 16 | 145.26 | 32 | 136.37 | 136.37
HD-FDD | 1 | 4 | 139.46 | 32 | 142.08 | 139.46 | 4 | 133.56 | 32 | 136.37 | 133.56
HD-FDD | 2 | 4 | 145.46 | 32 | 142.08 | 142.08 | 4 | 140.06 | 32 | 136.37 | 136.37
Maximal Coverage at BLER=2% for AMR-WB 6.6kbps/EVS 7.2kbps with
transmission time interval of 40ms and with/without header compression

## Slide 12: Objectives of the study
To investigate potential enhancements in RAN
  To solve the problem of critical data discard in PDCP related to UL video transmission in order to improve the perceived video quality by the UE
  To improve the VoLTE performance when UL voice data carrying uncompressed header need to be transmitted

## Slide 13: Objectives of the study
Investigations could be performed in the following areas
  On critical data discard in PDCP for video (RAN2)
    Methods for the UE access stratum to be aware that a PDCP SDU relates to upper layer critical data.
    Methods for the eNB to be made aware that the UE has upper layer critical data within its buffers so that the eNB can take the information into account in UL scheduling decisions. Appropriate network configuration/control of the mechanisms may also need to be considered.
  On voice data transmission with uncompressed header (RAN2)
    Methods for a UE to detect and inform the network about “key frame”, i.e. UL voice data carrying uncompressed header.
    Methods to separate the transmission of UL voice data carrying uncompressed header and compressed header.
    Methods to decouple the user payload transmission and the uncompressed header transmission.

## Slide 14: Objectives of the study
RAN time budget allocation
  A 3-meeting cycle over 2 quarters with max 1 TU for each RAN2 meeting is proposed

## Slide 15: Appendix

## Slide 16: Issues with conversational video calls
Further details on the potentially observed issues:
  Very short video freezes: some I-frames are not fully transmitted by the modem because of PDCP discard. On the receiver side, video decoding is stopped until the video sender retransmits the missing I-frames
  Small video jumps: due to retransmission of the missing video data by the video sender, the end-to-end latency increases suddenly and the video jitter buffer throws away a few frames because they are too old to be played out
  Longer video freezes: the video data which have been discarded by PDCP are not retransmitted by the video sender (because the I-frame to be retransmitted is too old) or are retransmitted by the video sender but discarded again in PDCP layer. The video freezes until the next I-frame

## Slide 17: Simulation assumptions for VoLTE
Parameters | Values
Carrier frequency | 2.0 GHz
Frame type | FDD
System bandwidth | 10MHz
Channel mode | EPA-5Hz
Antenna setup | 2Tx-1Rx and 2Tx-2Rx for PDSCH, 1Tx-2Rx for PUSCH
Occupied BW | 6 PRBs for PDSCH, 3 or 6 PRBs for PUSCH
Repetition level | 1, 2, 4, 8, 16, 32 for PUSCH, 1, 2, 4, 8, 16 for PDSCH
Performance target | 2% BLER
Channel estimation | Cross-subframe channel estimation using 2D-MMSE
Codec type | AMR-WB 6.6 kbps/EVS 7.2kbps

## Slide 18: TBS calculations for VoLTE
  For codecs AMR-WB 6.6kbps and EVS 7.2kbps, the payload and corresponding TBS with transmission time interval of 40ms and with/without header compression (“RoHC-enabled”) are:
40ms, RTP level aggregation, PDSCH with 6 RBs |  |  |  |  |  |  |  |  |  | 
Header compression? | Payload | RTP header | PDCP | RLC | MAC | BRS+PHR | Payload + Headers | TBS | Number of coded bits | R
Yes | 18*2 | 3*2 | 2*2 | 2 | 1 | 0 | 392 | 408 | 1440 | 0.3000
No | 18*2 | 60*2 | 2*2 | 2 | 1 | 0 | 1304 | 1352 | 2880 | 0.4778
40ms, RTP level aggregation, PUSCH with 3 or 6 RBs |  |  |  |  |  |  |  |  |  | 
Header compression? | Payload | RTP header | PDCP | RLC | MAC | BRS+PHR | Payload + Headers | TBS | Number of coded bits | R
Yes | 18*2 | 3*2 | 2*2 | 2 | 1 | 6 | 440 | 456 (3PRBs) | 864 | 0.5370
No | 18*2 | 60*2 | 2*2 | 2 | 1 | 6 | 1352 | 1352 (6PRBs) | 3456 | 0.3981

## Slide 19: VoLTE packet format and size
  A VoLTE packet is composed of 20ms speech burst in case of no aggregation
  Speech frame + Header given in the table
Payload
IPv6 (40 B), UDP (8B), RTP (12B)
Frame Type Index | Frame content | Bytes
0 | AMR-NB 4.75Kbit/s | 13
0 | AMR-WB 6.60 kbit/s | 18
1 | AMR-WB 8.85 kbit/s | 23
2 | AMR-WB 12.65 kbit/s | 33
3 | AMR-WB 14.25 kbit/s | 37
4 | AMR-WB 15.85 kbit/s | 41
5 | AMR-WB 18.25 kbit/s | 47
6 | AMR-WB 19.85 kbit/s | 51
7 | AMR-WB 23.05 kbit/s | 59
8 | AMR-WB 23.85 kbit/s | 61
MAC(1B), RLC(2B), PDCP (2B)*
* Additional 6B for Buffer Status Report (BSR) and Power HeadRoom (PHR) applicable for UL