## Slide 1: Motivation for new WI on UMTS and LTE inter-RAT mobility enhancements
Huawei, HiSilicon
3GPP TSG RAN Meeting #74
Vienna, Austria, December 5 – 8, 2016
Document for: Discussion
Agenda Item: 10.1.3
RP-162182

## Slide 2: UMTS and LTE inter-RAT mobility - overview
UMTS coverage
LTE coverage
Cell reselection
Redirection
PS handover
SRVCC
Inter-RAT mobility solutions
(based on coverage/service/…)
Others……
UE
RNC
SGSN
LTE
Camps on UMTS (idle or connected mode)
Redirection (to LTE)
Perform redirection
Access LTE
Exchange information and update paging routing
Problem description:
After RNC redirects the UE to LTE, SGSN is not aware of this action, so SGSN may send PS paging to the UE, but the UE will not respond as it is performing redirection (e.g. cell-reselection). If LTE initiates redirection, there may be similar problem.

## Slide 3: WI objectives
The objective of this work item is as below:
Specify enhanced mechanisms on co-ordination between RAN and core network in order to mitigate the missing call issue during the inter-RAT mobility operation between UMTS and LTE.

## Slide 4: WI time budget
RAN | R1 | R2 | R3 | R4RF | R4RD | R6 | RAN | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | R6 | RAN
74 Dec.16 | 88 | 97 | 95 | 82 | 82 | 3 | 75 March17 REL-14 freeze | 88bis | 97bis | 95bis | 82bis | 82bis | 89 | 98 | 96 | 83 | 83 | 4 | 76 June17
 |  |  | 1 |  |  |  |  |  |  | 1 |  |  |  |  | 1 |  |  |  |