## Slide 1: Discussion on evolution of 3GPP V2X in Rel-15 and beyond
LG Electronics
3GPP TSG RAN Meeting #74 RP-162194
Vienna, Austria, December 5 - 8, 2016
Agenda item: 9.1

## Slide 2: Outline
Status review on 3GPP V2X
Outcome of SA1 SI on eV2X
Preparation of RAN WG work
Proposed work plan

## Slide 3: Status review on 3GPP V2X
Rel-14 V2X WIs are on track.
  Scheduled to be completed in RAN#75.
Rel-15 SA1 eV2X SI can be completed now.
  25 use cases grouped into 4 use case groups [REF1]
Progress in NR eV2X in RAN
  Some aspects of evaluation methodology are captured in TR 38.913.
  WG discussion on NR eV2X is put on hold until RAN#75.
  Requirement on the relationship between NR V2X and LTE V2X is agreed.
Rel-13
Rel-14
Rel-15
`15
(RAN) SL-based V2V WI
(‘16.1~’16.9)
(SA1) eV2X SI
(‘16.6~’16.12)
5G
LTE-A Pro
Rel-16
PC5-based V2V completed
SA1 study on eV2X can be completed.
(RAN) LTE V2X WI
(‘16.6~’17.3)
Other aspects of LTE-based V2X
5G
LTE Evolution
New RAT
RAN can prepare eV2X work for Rel-15 and beyond.

## Slide 4: SA1 use case group: Platooning
KPI*
  Latency: mostly 10 ~ 25 ms
  Reliability: 90 ~ 99.99%
  Data rate: 12 kbps ~ [65] Mbps
  Range: [5] ~ [10] sec * max relative speed
    Low relative speed is expected between vehicles joining the same platoon, which means relatively short communication range.
Examples of necessary functionalities
  Group management
  High reliability sidelink
    E.g., by HARQ feedback, TX diversity, enhanced resource allocation, …
From http://www.sarte-project.eu
* It should be noted that the set of KPI values required for each use case is not always the combination of the most challenging ones. The exact set is determined depending on the application characteristics (e.g., whether data compression is used or not), the autonomous driving level, etc.

## Slide 5: SA1 use case group: Advanced driving
KPI
  Latency: [3] ~ [100] ms
  Reliability: [99.99] ~ [99.999]%
  Data rate: 65 kbps ~ [50] Mbps (including DL: [0.5] UL: [50] Mbps)
  Range: [5] ~ [10] sec * max relative speed
Examples of necessary functionalities
  Low latency and high reliability in sidelink and uplink/downlink
    E.g., short TTI, connectionless TX/RX, MBMS, …
(1)
(2)

## Slide 6: SA1 use case group: Extended sensors
KPI
  Latency: 3 ~ 100 ms
  Reliability: 90 ~ 99.999%
  Data rate: 25 ~ 1000 Mbps
  Range: 50 ~ 1000 meters
Examples of necessary functionalities
  Very high rate sidelink
    E.g., using spectrum above 6 GHz
  UE-to-UE relaying for coverage extension
  Uplink/downlink to enlarge the range of large-size messages
    E.g., HARQ for MBMS
From 3GPP TR 22.886

## Slide 7: SA1 use case group: Remote driving
KPI
  Latency: 5~[20] ms
  Reliability: [99.999]%
  Data rate: UL 25 Mbps, DL 1 Mbps
Examples of necessary functionalities
  Enhanced mobility management for interruption-free uplink/downlink

## Slide 8: Preparation of RAN WG work
Diverse use cases and KPI sets in SA1 outcome
  Selection of suitable technology may be dependent of the use case.
    RAT (LTE or NR)
    Interface (uplink, downlink, or sidelink)
    Spectrum (below 6 GHz or above 6 GHz, operator-licensed or ITS-dedicated)
Furthermore, RAN agreed the following relationship between NR V2X and LTE V2X.
  “It is not intended for NR V2X to replace the services offered by LTE V2X. Instead, the NR V2X shall complement LTE V2X for advanced V2X services and support interworking with LTE V2X.”
  => Clear and careful guidance is essential from the beginning of the specification work.
A study is necessary to identify the most suitable operation scenario for each use case group.
  To ensure the complementary relationship between NR V2X and LTE V2X
  To identify the focus of the study and development of each technology

## Slide 9: Preparation of RAN WG work
LG’s view
  Rel-14 LTE V2X should be used for the basic services in Rel-15 and beyond.
  Two alternatives:
    Alt 1: NR V2X standards include an operation mode which enables “communication” with Rel-14 V2X UEs.
    Alt 2: If Alt 1 is not possible, the operation of NR V2X is clearly separated from the operation of Rel-14 LTE V2X.
      One example is not to consider NR V2X in a spectrum where LTE V2X is possible (such as 5.9 GHz band).
Some platooning use cases with low KPI may be supported with small enhancement to Rel-14 LTE V2X.
  E.g., [CPR.7.2.2-005] 300~400 bytes at the rate of 30 messages per second with 90% reliability within the group.
    Rel-14 LTE V2X already supports 20 ms latency. Group management may be needed additionally.
Most of the other use cases may require substantial change from Rel-14 LTE V2X.
  Needs to be covered by NR eV2X.

## Slide 10: Proposed work plan
Start a RAN-level study to identify 5G V2X scenarios in RAN#74.
  Goal is to associate each use case group with suitable RAT and spectrum.
  Target to complete in RAN#75.
  Exemplary SID is provided in [REF2].
Start a NR eV2X SI in RAN#75
  Based on the scenarios identified suitable for NR
  The study may continue during the whole NR phase 1, targeting WI in NR phase 2.
    Expected to cover all of uplink, downlink and sidelink both in below and above 6 GHz spectrum.
  Exemplary SID is provided in [REF3].
Start a LTE V2X enhancement WI in RAN#75 if some scenarios are identified suitable for LTE.
  The outcome of this WI can be provided to the related industry as the first version of 5G V2X.
  Minimized specification effort is desirable.
Proposed work plan is summarized in [REF4].

## Slide 11: References
[REF1] S1-163441, “FS_eV2X Consolidation of Requirements,” SA1 eV2X Drafting Session.
[REF2] RP-162122, “New SI proposal: Operation scenario of 5G V2X,” Qualcomm, LG Electronics Inc.
[REF3] RP-162195, “Discussion on new SI proposal: NR support for enhanced V2X,” LG Electronics Inc., Qualcomm.
[REF4] RP-162196, “Proposal for eV2X work plan,” LG Electronics, Qualcomm.