## Slide 1
Discussion on prioritization for flexible duplex of paired spectrum
ZTE, ZTE Microelectronics
3GPP TSG-RAN Meeting #74 RP-162223
Vienna, Austria, December 5 - 8, 2016
Agenda item: 9.2.2
Document for: Discussion

## Slide 2: Background
At RAN#73, the prioritization of items within the New Radio Access Technology SI was discussed. As agreed at RAN#73 in [1], for the items listed below, no dedicated meeting time in the WGs will be allocated until March 2017.
List of items:
  Waveforms above 40GHz
  mMTC
  [Flexible duplex of paired spectrum]
  Interworking with non-3GPP systems
  …

## Slide 3: Background
At RAN1#87, the following agreements were reached [2],
Agreements:
  Referring to TR 38.913, the terminology of “duplexing flexibility” in NR means at least one of the following mechanisms to manage resources flexibly for uplink and downlink for both paired and unpaired spectrum.
    1) UL and DL usage is flexibly changed in time domain in unpaired spectrum.
    2) UL and DL usage is flexibly changed in time domain in UL band in paired spectrum
    3) UL and DL usage is flexibly changed in time domain in DL band in paired spectrum
  Note: the definition of the above terminology is not intended to have impact on prioritizing discussion on any of the above mechanisms

## Slide 4: Motivation
  Operators should comply with regional regulatory requirements when deciding how to use their paired spectrum resources.
  The regulatory aspects for flexible duplex have been discussed and no sufficient consensus were reached.
    RAN REL-13 SI Study on regulatory aspects for flexible duplex for E-UTRAN:completed with TR 36.882 (RP-151568) and the conclusion "At least in one country and in some bands, utilizing UL spectrum for transmission from the network to UEs is possible.”[3]
  The coexistence with FDD-LTE in co-channel or adjacent carrier should be considered firstly.
  According to the discussion in RAN#73 meeting, tdoc RP-161914 [1] is approved to consider the forward compatibility issue of NR. The item of “Flexible duplex of paired spectrum” was included in the list of forward compatibility. However, the square brackets […] of [Flexible duplex of paired spectrum] lead to different understanding and cause some confusions when the duplexing was discussed in RAN1#87.

## Slide 5: Proposal
To remove the square brackets […] of [Flexible duplex of paired spectrum] in relation to RP-161904 and provide clear guidance to working groups. The updated list of items as follows,
List of items:
  Waveforms above 40GHz
  mMTC
  [Flexible duplex of paired spectrum]
  Interworking with non-3GPP systems
  …

## Slide 6: Reference
[1] 3GPP TSG RAN#73, RP-161904 Outcome from prioritization discussion for New Radio Access Technology SI, RAN1 Chairman, RAN2 Chairman, RAN3 Chairman, RAN4 chairman, New Orleans, USA, September 19-22, 2016.
[2] 3GPP TSG RAN WG1 Meeting #87, Chairman's Notes RAN1_87_final, Reno, USA 14th – 18th November 2016.
[3] 3GPP TSG RAN#69, Report of 3GPP TSG RAN meeting #69, Phoenix, USA, September 14–16, 2015

## Slide 7: Thank you