## Slide 1: Motivation for SI: Study on LTE Vehicular Positioning Technologies
3GPP TSG RAN Meeting #74 RP-162252
Vienna, Austria, 5 - 8 Dec. 2016

## Slide 2: LTE Vehicular Communication Background on LTE-V2X Enhancements
Work on R.14 LTE-V2X communication is progressing towards completion - Feb’17
LTE-V2X defines enhancements for two complementary air-interfaces: PC5 and Uu
  LTE sidelink V2X enhancements (LTE PC5)
    eNB controlled mode: SL SPS scheduling + reporting of location information
    UE autonomous mode: SL sensing & resource selection + geo-zoning
    Enhancements of L1 structure for robust performance at high speeds
    GNSS synchronization (GNSS as sync reference for time/frequency)
  LTE downlink and uplink V2X enhancements (LTE Uu)
    Uplink SPS enhancements to efficiently handle quasi-periodic V2X traffic
Vehicle location information is used for LTE-V2X radio-resource management
  Autonomous radio resource selection or scheduling based on geo-location information of vehicle provides improved communication performance

## Slide 3: LTE-V2X and Geo-location Demand for Accurate and Reliable Vehicle Location
Automotive industry transformation
  Automotive industry transforms towards support of higher automation levels (autonomous driving)
  V2X applications require accurate and reliable geo-location for robust operation
  Demand for tighter integration of vehicular geo-location and communication technologies
    Road safety / intelligent transportation and traffic management / navigation / platooning / assisted & autonomous driving services
3GPP SA1 “Study on enhancement of 3GPP support for 5G V2X services (Rel.15)”
  High precision positioning techniques should be supported
  V2X positioning requirements - technically challenging targets
    “3GPP system shall support relative lateral position accuracy of 0.1 m”
    “3GPP system shall support relative longitudinal position accuracy of less than 0.5 m for UEs supporting V2X application in proximity”

## Slide 4: V2X Positioning GPS Trial Measurements
Experimental GPS measurements
  Vehicle with GPS receivers mounted inside a car (consumer grade)
  GPS accuracy experiment is conducted on predefined route
    Scenario 1: Suburban Freeway (mostly Freeway)
    Scenario 2: Urban Dense (+ skyscraper urban canyon)
  Synchronized measurements from different GPS sources
    Absolute GPS measurement: vehicle absolute coordinate error
    Relative GPS measurement: distance error between two vehicles
  True coordinates are estimated using MEMS IMU
    MEMS IMU has accurate GNSS and utilizes data from multiple sensors
  Vehicle speeds varies in the range from 20-100km/h

## Slide 5: V2X Positioning GPS Requirements and Trial Measurement Results
  Observation
  State of the art GPS receivers may not provide sufficient accuracy for V2X positioning in all scenarios
3GPP GNSS requirements (TS 36.171)
Field Test Trial GPS measurement from different recording sets
System | Success rate | 2-D position error | Max response time
GPS | 95 % | 30 m | 20 s
System | Success rate | 2-D position error | Max response time
GNSS | 95 % | 15 m | 20 s
3GPP GNSS requirements
3GPP GPS requirements

## Slide 6: V2X Positioning LTE-V2V Radio-Interface in V2X Positioning
Role of LTE V2V Communication in V2X Positioning
  Distance measurements with proximate vehicle(s)/RSU(s)
  Broadcasting of coordinates or geo-location measurements to facilitate relative or absolute positioning
  Enabling cooperative geo-location protocols to perform positioning
Technical Advantages
  Increased estimation accuracy
    GNSS is complemented by radio-layer techniques
  Increased system reliability
    Additional sources of geo-location information
  Increased robustness
    Multiple links with favorable radio-conditions
  Integrated communication and positioning protocol

## Slide 7: V2X Positioning Performance Link Level Analysis
  Conclusion
  Advanced timing estimation techniques can provide accurate timing measurements that can outperform GNSS based distance measurement
Parameter | Value
Bandwidth | 20 MHz
SCS | 15 KHz
Number of RX antennas | 4
Timing estimation | Single shot
Channel model | V2V Channel Model (TR 36.875)
First path detection | Advanced timing estimation

## Slide 8: V2X Positioning Performance System Level Analysis
CDF of Absolute Positioning Error
Conclusion
  Combination of accurate radio-layer timing measurements and GNSS geo-location provides improved positioning accuracy
Parameter | Value
Bandwidth | 20 MHz
SCS | 15 KHz
Number of RX antennas | 4
Timing estimation | Advanced Timing Estimation
Channel model | V2V Channel Model (LTE-V2V TR 36.875)
Inter-vehicle distance distribution | LTE-V2V Evaluation Methodology (Freeway Scenario 70km/h)
Positioning | 1) GNSS only 2) GNSS + Distance

## Slide 9: Summary
Conclusions
  Presented analysis shows benefits of enabling range/distance measurements for vehicular services
  Accurate and reliable geo-location and proximity is a key enabler of future vehicular services
  LTE-V2X communication can play crucial role to improve V2X positioning (complementary solution)
  3GPP LTE-V2X and NR technologies can be used to enable new positioning accuracy bounds beyond current GNSS limits
Proposal
  Organize 3GPP V2X positioning study item to analyze V2X positioning enhancements that can be provided by 3GPP radio-interface(s) LTE or NR
  Start from LTE-V2X positioning given that NR air-interface is in active study/development stage

## Slide 10: LTE V2X Positioning Study Item Proposal Objectives
Definition of LTE-V2X positioning evaluation scenarios
  Identification of deployment scenarios for analysis of vehicle-to-vehicle or vehicle-to-RSU distance measurements and vehicle positioning protocols based on LTE communication technology including both LTE-Uu and LTE-PC5 air-interfaces [RAN1]
  Definition of necessary evaluation assumptions and performance metrics on top of the existing LTE-V2X communication methodology [TR 36.885] for LTE-V2X vehicle positioning [RAN1]
Study of physical layer enhancements to enable inter-vehicle distance measurements
  Study accuracy and feasibility of distance measurements using LTE-Uu and/or LTE-PC5 air-interfaces for vehicular positioning [RAN1, RAN4]
  Study LTE-Uu and/or LTE-PC5 enhancements beneficial for accurate vehicle-to-vehicle, vehicle-to-RSU, or vehicle-to-eNB distance measurements [RAN1]
  Study accuracy of advanced timing estimation algorithms, facilitating distance measurements [RAN1, RAN4 ]
Study positioning protocols to facilitate enhanced V2X positioning based on LTE technology
  Study LTE-Uu and/or Sidelink protocol enhancements to enable positioning protocols utilizing positioning technologies including but not limited to inter-vehicle distance measurement, GNSS information, etc. [RAN1, RAN2]
  Study of LTE positioning protocols enhancements beneficial for LTE-V2X positioning [RAN1, RAN2]
Identify specification impact to enable V2X positioning [RAN1, RAN2, RAN4]

## Slide 11: LTE V2X Positioning Study Item Proposal Tentative Work Plan and Timelines
WG Meetings | Date | RAN1 TUs | RAN2 TUs | RAN4 TUs | Work planning
RAN1#88 /RAN2#97 /RAN4#82 | Feb.’17 | 3 | 0 | 0 | RAN1: Define scenarios for LTE-V2X range and positioning based on evaluation assumptions of LTE-V2V methodology Identify design principles and protocols for range estimation and positioning
RAN1#88bis /RAN2#97bis /RAN4#82bis | Apr’17 | 3 | 1 | 0.5 | RAN1: Initial evaluation of identified design principles and analysis of different design options RAN2: L2 aspects of range estimation and positioning (based on RAN1 input) RAN4: Feasibility / accuracy analysis based on RAN1 input
RAN1#89 /RAN2#98 /RAN4#83 | May’17 | 3 | 1 | 0.5 | RAN1: System level evaluation of range estimation and positioning accuracy RAN2: Architectural consideration / LPP considerations RAN4: Feasibility / accuracy analysis based on RAN1 input
RAN1#90 /RAN2#99 /RAN4#84 | Aug’17 | 3 | 2 | 1 | RAN1: Finalization of evaluation results, summary of design principles for range and positioning estimation. Recommendations on L1 design enhancements. RAN2: Conclusions on L2/upper layer aspects of identified positioning protocols. RAN4: Summary of feasibility / accuracy analysis based on RAN1 input

## Slide 13: Backup
V2X Positioning System

## Slide 14: V2X Positioning Heterogeneous Solution
V2X positioning
  Multiple technical challenges to get accurate and reliable vehicle coordinate or inter-vehicle distance
    High mobility, GNSS signal blockage in Urban scenarios, LOS and NLOS multipath propagation, interference
  Primary technology is GNSS based positioning, which is not sufficient in all scenarios
    GNSS based positioning accuracy, availability and reliability in Urban scenarios is of concern
  Vehicular positioning systems (heterogeneous system)
  Combination of multiple technologies with pros and cons (camera / lidar / radar / sensor / radio)
  Strict requirements on accuracy, reliability and availability