## Slide 1: Motivation of Study on 5G Non-orthogonal Multiple Access
3GPP TSG RAN #74
Vienna, Austria
December 5-8, 2016
ZTE, ZTE Microelectronics
RP-162483

## Slide 2: Main Use Cases
URLLC
  UE is in RRC connected state or possibly inactive state
  The key metrics are low latency and high reliability
mMTC
  UE is in inactive state
  The key metrics are very low power consumption and good coverage
eMBB (infrequent small data)
  UE is in inactive state
  The key metrics are lower power consumption and less signaling overhead

## Slide 3: Orthogonal vs. Non-orthogonal Multiple Access
As in LTE, basic multiple access of NR is orthogonal for both DL and UL
  Orthogonal can deliver enough good performance system throughput for big data
  Less sophisticated receiver implementation
Non-orthogonal transmission can be complementary, to
  Improve the system load
  Reduce the latency
  Lower the UE power consumption
  Minimize the control signaling

## Slide 4: Grant-free Contention-based Non-orthogonal Transmission
Grant –free non-orthogonal transmission can significantly reduce the latency
    Control plane latency is reduced by skipping state transition procedures
    User plane latency is reduced by autonomous transmission without explicit dynamic grant
Resource is more efficiently utilized in grant-free, via non-orthogonal transmission
Small packet
state transition
Deep sleep
Grant / Transmit the small packet
Success
Fail
towards lighter connection

## Slide 5: Gain of System Load by Non-orthogonal Transmission
Non-orthogonal transmission can support higher system load
    More resilient to random arrival of large number of small packets
    Gracefully degrade as system load increases
Packet drop rate vs. system load

## Slide 6: Non-orthogonal is not a Simple Superposition
Simple superposition at power domain is not sufficient
  Very complicated receiver is needed
  Prone to various imperfections
Transmitter side processing is the key to
  Optimization of the system capacity or system load
  Reducing the receiver complexity
  Robustness to imperfections

## Slide 7: Example 1: Rel-13/14 MUST
Bit to symbol mapping to ensure Gray property in the composition constellation
Symbol level interference cancellation (IC) can be used, rather than much more complicated code-word level IC
Flipping:
where c and d depend on Tx power ratio P1: P2

## Slide 8: Example 2: Various Multiple Access Signatures
Short (i.e. <16) spreading sequence/code at symbol level
Long sequence at symbol level
Scrambling/interleaver at bit level
DMRS, preamble, etc.

## Slide 9: Proposal
To continue studying non-orthogonal multiple access, in particular grant-free transmission for small data/message
To study potential transmitter side schemes to enhance the performance and reduce the receiver complexity