## Slide 1
Source: Samsung
Motivation for Integrated Backhaul and Access
Agenda Item: 9.1, Document for: Discussion and Decision
RP-170168
3GPP TSG RAN Meeting #75
Dubrovnik, 6th - 9th Mar 2017

## Slide 2: Introduction
Wireless relay enables self-backhauling which can significantly reduce the cost of deploying NR networks by eliminating or reducing the need for fiber backhaul or other wired backhaul types
  Enables economical dense small cell deployments, providing capacity boost in dense urban area
  Enables low cost coverage extension for mmWave frequency and for rural area
To enable efficient spectrum utilization of backhaul and access, support for integrated backhaul and access functionality is essential

## Slide 3: NR requirement on wireless relay
The design of the 5G RAN and Radio Interface Technology shall aim at supporting wireless relay functions
  Scenarios and Requirements for Next Generation Access Technologies (TR 38.913 10.16 Relay requirements)
RAN1#85 agreements
  NR should allow for efficient same frequency operation between the access link and backhaul link
  NR should also allow for efficient operation when the backhaul link and access link are on different frequencies. This includes:
    Operation of backhaul link and access link on different frequencies in the same band
    Operation of backhaul link and access link in different bands
  Note: The term ‘backhaul link’ does not make any assumption on NR RAN architecture design options

## Slide 4: RAN1 conclusions during NR Study Item (RAN1#86)
Mechanisms for joint operation of backhaul link and access link should be studied by NR, including
  Study dynamic resource allocation among backhaul and access links, including TDM and FDM and SDM approaches under half-duplex constraint
  Study multi-hop backhauling and multi-site connectivity in backhauling
  Mechanism for integration of new TRPs/RNs carrying integrated backhaul and access functionalities
  Mechanisms for discovery and management of backhaul links for the connected TRP/relay nodes (if supported) with integrated backhaul and access links
  Other aspects/functionalities such as forward compatibility to study full duplex operation on backhaul and/or access links are FFS
RAN1 should strive for a common mobility handling and beam management framework for mobile TRP/relay nodes (if supported) carrying joint operation of backhaul and access functionalities and the usual UEs
Note: No assumption on particular RAN architecture

## Slide 5: Study Item on Integrated Backhaul and Access (IBA)
Proposal: Approve a RAN1-led study item on IBA. The study aims to develop technical solutions for supporting efficient in-band wireless relay for NR. Frequency ranges up to 100 GHz will be considered.
Based on the conclusion of the RAN1 study item, the following should be included in the study item scope
  Identify mechanisms for joint operation of backhaul link and access link, including
    Study dynamic resource allocation among backhaul and access links, including TDM and FDM and SDM approaches under half-duplex constraint [RAN1, RAN2]
    Study multi-hop backhauling and multi-site connectivity in backhauling [RAN1, RAN2, RAN3]
    Mechanism for integration of new TRPs/RNs carrying integrated backhaul and access functionalities
    Mechanisms for discovery and management of backhaul links for the connected TRP/relay nodes (if supported) with integrated backhaul and access links [RAN1, RAN2, RAN3]
    Other aspects/functionalities such as forward compatibility to study full duplex operation on backhaul and/or access links are FFS [RAN1]
  Strive for a common mobility handling and beam management framework for mobile TRP/relay nodes carrying joint operation of backhaul and access functionalities and the usual UEs [RAN1, RAN2]
  Identify physical layer solutions to support wireless backhaul links with high spectral efficiency [RAN1].