## Slide 1
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6 - 9, 2017
RP-170170
Source: Samsung
Title: Motivation for new WI: Further Enhancements on Full-Dimension (FD) MIMO for LTE
Document for: Discussion
Agenda Item: 10.1.1

## Slide 2: Motivation 1
Enhanced inter-operability between FD-MIMO and some other LTE-A features
  Key component: CSI reporting
Rel-14 periodic CSI reporting (P-CSI) for non-precoded CSI-RS (Class A) requires at least 3 UL subframes for one complete CSI report
  Intermittent (un)availability of UL subframes for LAA and eIMTA
  Limitation of PUCCH format 2/2a/2b (small maximum payload)
  Issues: complex priority rules, increased dropping of CSI reports, error propagation, stale CSI reports
  Solution: use PUCCH formats with larger maximum payload to design compact/self-contained P-CSI reporting which requires, e.g. at most 2 subframes for one complete report

## Slide 3: Motivation 1
Rel-14 aperiodic CSI reporting (A-CSI) only supports mode 1-1 for eCA
  Issue: with eCA, subband CQI and/or PMI is not applicable – performance limitation
  Solution: specify mechanism to support other modes, e.g. 1-2, 3-1, 3-2
CRS-based CSI reporting can be used for MTC in Rel-14
  FD-MIMO can improve DL multiplexing capacity (number of connections) for MTC
  Issue: FD-MIMO-related CSI reporting requires CSI-RS
  Solution: enable CSI-RS-based CSI reporting for MTC while maintaining low-payload principle

## Slide 4: Motivation 2
Enable concurrent usage of advanced CSI with other pertinent FD-MIMO features
  Beamformed CSI-RS, hybrid CSI, and semi-open-loop transmission
Currently advanced CSI codebook is only enabled for non-precoded CSI-RS (Class A)
  The W1 part of advanced CSI codebook can be beneficial for hybrid CSI mechanism 1 and semi-open-loop transmission
  The W2 part of advanced CSI codebook can be beneficial for beamformed CSI-RS

## Slide 5: Motivation 3
Enable efficient usage of IMR by extending aperiodic CSI-RS functionality to ZP CSI-RS
Rel-14 aperiodic CSI-RS is only enabled for NZP CSI-RS for {2, 4, 8} ports
  Aperiodic CSI-RS enables more efficient resource pooling across UEs
  Extension to ZP CSI-RS seems natural

## Slide 6: Objective: Core
Extend specification support for CSI reporting in the following areas [RAN1]
  [Motivation 1] Specify periodic CSI reporting using PUCCH format(s) other than format 2 to facilitate compact and self-contained PUCCH-based periodic CSI reports
  [Motivation 1] Specify aperiodic CSI reporting beyond PUSCH mode 1-1 when configured together with enhanced carrier aggregation
  [Motivation 1] Specify low-payload CSI reporting which takes advantage of FD-MIMO for the purpose of MTC-type applications
  [Motivation 2] Specify necessary components to enable concurrent usage of advanced CSI codebook with UE-specific beamformed CSI-RS (with 2, 4, or 8 ports), hybrid CSI, and semi-open-loop transmissions
  [Motivation 3] Specify aperiodic CSI-IM for interference measurement overhead reduction in high-load MU-MIMO scenario
Specify higher layer support of enhancements listed above [RAN2]