## Slide 1
On NR Forward Compatibility
RP-170208
3GPP RAN #75
Dubrovnik, March 2017
Qualcomm

## Slide 2: Outline
Migration scenarios for CN (from EPC to 5GC) while supporting different type of UEs (e.g. Option 3, Option 7, Option 2, etc.)
  Covered by SA2
SA/NSA high level view from RAN1/RAN2 perspective
Forward compatibility at RAN
Conclusions

## Slide 3: Migration from EPC based options to 5GC options
How can deployments based on different 3GPP architecture options (i.e. EPC based or 5GC based) and UEs with different capabilities (EPC NAS and 5GC NAS) may coexist at the same time within one PLMN?
Problem Statement
Figure 5.17.1.1-1: Architecture for migration scenario for EPC and 5G CN
Option 1 UE
Option 3 UE
Option 2 UE
Option 5 or 7 UE
Dotted lines indicating termination of NAS protocols.
Also indicative of network route for UE initial access.
Possibility of aggregation (via DC) of NR carrier not explicitly shown.
Figure taken from TS 23.501 v0.2.0 [text in blue added for presentation]

## Slide 4: NSA/SA – RAN1/RAN2 perspective
SYNC
PRACH
PDCCHPUCCH
PDSCH PUSCH
M-RS
NR
CONNECTED
mode mobility
LTE
IDLE + CONNECTED
Mode mobility
NSA RAN
PBCH
NR IDLE mobility
Common PHY ch
+ SA
Capability
+
Common PHY channels

## Slide 5: NSA/SA – RAN1/RAN2 perspective
NSA RAN/UEs do not support NR IDLE mode procedures
  No L1/L2/L3 functionalities for NR camping and paging
    NO SI delivery over NR carrier
  IDLE mode procedures are based on LTE
Forward compatibility and coexistence [when SA RAN/UEs introduced] is ensured by defining IDLE and CONNECTED mobility procedures based on common PHY channels
  Similar to the fact that one LTE carrier can be PCell for some UEs and SCell for some others
SA operation requires definition of additional functionalities
  e.g., L1/L2/L3 procedures in support of NR IDLE mode
  NSA devices will continue to be supported by using a subset of SA RAN functionalities
  SA devices will support additional functionality stemming from
    NR radio SA operation, as well as, possibly new 5GC
Cont’d

## Slide 6: A flexible framework with forward compatibility
Efficiently multiplex envisioned and future 5G services on the same frequency
Integrated framework
That can support diverse deployment scenarios and network topologies
Scalable transmission time interval (TTI)
For diverse latency requirements—capable of latencies an order of magnitude lower than LTE
Mission-critical transmissions
May occur at any time; design such that other traffic can sustain puncturing2
Forward compatibility
With support for ‘blank’ resources1
Scalable numerology
Blank subcarriers
Scalable TTI
MBB
D2D
Multicast
Self-contained integrated subframe
UL/DL scheduling info, data and acknowledgement in the same sub-frame
Dynamic uplink/downlink
Faster switching for more flexible capacity based on traffic conditions
DL
UL
DL
Blank subframes
UL
UL
Notes: 5G will deliver a flexible frame structure designed for efficient service/feature multiplexing on same frequency and is designed for forward compatibility for future 5G features/services; so 5G is not just being designed for wider bandwidths to enhance mobile broadband, but being designed at the PHY/MAC layer to support and multiplex a richer and more varied set of services with various levels of data rate, mobility, latency and reliability. The features of this flexible frame structure include:
    Scalable Time Transmission Intervals (TTIs) that can support diverse latency and QoS requirements all the way down to 1ms end-to-end latency; today’s LTE supports 1 ms TTI; 5G supports shorter TTI traffic (100s of us) for low latency and high reliability and longer TTI for low latency and higher spectral efficiency; 5G also supports service aware TTI multiplexing on the same frequency
    An integrated framework that can support diverse deployment scenarios and network topologies – such as supporting traditional macro WAN deployment/topology integrated with device-to-device or multi-hop communications
    Support blank sub-frames and blank frequency resources—designed for future features/services on same frequency; synchronous (time) or asynchronous (freq.)—Example; broadcast on frequency resources
    Support multiplexing ultra-reliable transmissions with nominal WAN traffic via puncturing that may occur at anytime; requires new PHY/MAC design for nominal traffic that can sustain this puncturing

## Slide 7: Forward Compatibility
R15 NR is expected to support
  eMBB at sub6 GHz + mmW
  Some level of URLLC
Long-term forward compatibility = Introducing major new features seamlessly
Current NR design meets following requirements
  Need for periodic always-on transmissions reduced to a bare minimum
  Scalability in time and frequency
  Compact self-containable waveforms
  Efficient and robust resource reservation/multiplexing
Hooks for future NR evolution

## Slide 8: Forward Compatibility
Envision applications may require
  100s kHz to multiple GHz bandwidth support
  Long range, ultra low latency, etc.
NR is defined with scalable numerology to meet these requirements
  Tone spacing = 15 kHz x 2n
  Slots of 14 symbols, 1 ms x 2-n
  Mini-slots of 2 symbols
  Aggregated bandwidth scaling up to > 1 GHz
Scalability in time and frequency

## Slide 9: Forward Compatibility
Compact legacy waveform enables efficient multiplexing of future waveforms
NR has compact time/frequency foot print  blank space for future
  No CRS
  Single slot SYNC waveform with < 10% duty cycle in time
  Narrow band SYNC waveform limited to < 5MHz for sub6GHz and <40 MHz for mmW
  New frame structure enables self-containable DL/UL traffic transactions
Legacy operation can be “contained” within some resources

## Slide 10: Forward Compatibility
When new waveforms are introduced, legacy devices should be able yield/multiplex time-frequency resources with the new waveform
Following items have been discussed/identified in RAN1 w.r.t. forward compatibility:
  Dynamic signaling for eMBB UEs to monitor for URLLC multiplexing
  Group common control signaling to indicate resource reservation for future services
  Error correction for eMBB UEs when resources are overridden by future services
Conclusion: Forward compatibility is an integral part of NR
  Sets the system for its very own evolution
  NR WID should address it explicitly in a way that ALL feel comfortable
  Subsequent normative work should consider the importance to adequately address forward compatibility
and Conclusion