## Slide 1: Motivation Paper: Study on Flexible and Full Duplex for NR
LG Electronics
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6 - 9, 2017
RP-170241
Agenda Item: 9.1

## Slide 2
Introduction
Trends in NR
  Explosive Increase in Demand for Data Traffic
    Traffic volume/burst and DL/UL traffic asymmetry
  Ultra Low Latency required
  Support Various Usage Scenarios by a single cell: eMBB, URLLC, mMTC
Enabling Technologies
  Dynamic and flexibility of frequency resource utilization
    Support flexible DL/UL resource allocation with FDM manner
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Full duplex functionality
    Support simultaneous DL/UL resource allocation for spectral efficiency enhancement and latency reduction
NR requires further enhanced solution with high spectral efficiency and low latency

## Slide 3
Motivation
Limitation in TDM between DL/UL
  TDM between DL and UL leads higher latency in both DL and UL due to time partitioning between DL and UL
  Symmetric DL/UL partitioning to address URLLC may not be effective from spectral efficiency perspective particularly when traffic patterns are either DL heavy or UL heavy
Further enhancements in spectral efficiency
  By allowing full duplex at one spectrum, enhanced spectral efficiency can be achieved (ideally by 2x)

## Slide 4
Flexible Duplex for NR
Flexible Duplex with FDM manner
  Handling Mixed Usage Scenarios
    - e.g., multiplexing between eMBB DL and URLLC UL with FDM manner
    - e.g., multiplexing between mMTC UL and eMBB/URLLC DL with FDM manner
  Sub-band wise DL/UL adaptation required
  Occurrence of DL’s OOB power in UL reception at gNB
  Occurrence of inter-cell cross-link Interference between gNBs and UEs
Potential gains from flexible duplex with FDM manner
  DL or UL resource availability at any time  possibly reduce latency for URLLC applications
  Multiplexing becomes easy for different usage scenarios
<Example of flexible duplex with FDM manner>
gNB
eMBB UE #1
URLLC UE #2
DL
Guard Band
UL

## Slide 5
Full Duplex for NR
<Example of full duplex operation at gNB>
Full Duplex gNB
UE #1
UE #2
Full Duplex at gNB
  Efficient adaptation for time variant DL/UL data traffic
    Spectral efficiency enhancement via fully utilized frequency resources
    Overall latency reduction via always on UL transmission opportunity
    Easier multiplexing among different usage scenarios with different DL/UL traffic patterns
  gNB with Full Duplex capability required
  Occurrence of self-Interference at gNB
  Occurrence of inter-cell cross-link interference between gNBs
  Occurrence inter/intra-cell cross-link interference among UEs
Potential gains from full duplex
  Expected spectral efficiency enhancement
Self-interference
UE-to-UE cross-link Interference
DL
Full Duplex (DL+UL)
UL
* N X M, where N, M are the number of transmit and receive antennas, respectively.

## Slide 6
Objectives
Identify deployment scenarios and use cases, and evaluate the benefits of various DL/UL resource adaptation operation (e.g., FDM between DL and UL, simultaneous DL and UL transmission) with or without interference mitigation/cancellation/coordination techniques in such scenarios [RAN1].
Study potential interference mitigation/cancelation/coordination techniques [RAN1]
  Interference mitigation/cancellation/coordination techniques to allow downlink and uplink at a band in FDM manner includes e.g., guard band configuration [RAN1, RAN4]
  Interference cancellation/mitigation techniques to allow full duplex capability at gNB, e.g., self interference cancellation, cross-link interference mitigation techniques among UEs in the same cell [RAN1, RAN4]
Identify the physical layer impacts (e.g., frame structure, HARQ procedure) to support various DL/UL resource adaptation operations [RAN1]
Study any necessary and relevant RF requirements to support various DL/UL resource adaptation operations [RAN4]

## Slide 7: Thank You