## Slide 1: Motivation for WI on Architecture Evolution for E-UTRAN
China Unciom, Orange, China Telecom, Huawei, HiSilicon
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, Mar 6 – 9, 2017
Document for: Discussion
Agenda Item: 10.1.3
RP-170265

## Slide 2: Motivation of higher layer split for LTE CU/DU
There would be only one high layer option for NR CU and DU function split, which should be standardized in stage 2 and stage 3 in normative phase.
To support tight interworking of LTE and NR, the higher layer functional split between LTE CU/DU is one of the most feasible solution.
    The higher layer split of LTE CU/DU could well support for tight interworking between LTE and NR.
    This architecture will utilize the transport network in an efficient way and minimize the impacts on legacy LTE transport network.
    It is easier for further network upgrading when LTE CU/DU deploy in operator’s network.
Fig.1 A simplified architecture for LTE CU/DU split

## Slide 3: Scope of new WI
To make the progress of standardization, a short-term study phase is started first and the detailed objectives of the study item are:
  Study and identify the potential scenarios and requirements of LTE CU/DU functional split;
  Study the architecture, and select one function split option of LTE central unit (CU) and distributed unit (DU) aligned with the option finally selected for NR considering option 2 i.e. PDCP/RLC split as the baseline;
  Study and evaluate the possible impacts on the existing features, including the functions and procedure required in the interface to support the higher layer functional split, i.e. the interface between LTE CU and DU ;
  Study the potential enhancements on the coordination between LTE-CU and NR-CU, if needed;
  Further investigate possible function improvements with the centralized architecture, including but not limited to
    Intra-system and inter-system mobility handling
    Positioning…
    ……

## Slide 4: Scope of new WI
After the short-term study item, the work item phase should work on specifications and detailed objectives of the work item are:
  Specify the higher layer function split architecture, functionalities, interface for LTE-CU and DU
    Specify the higher layer functions split for LTE CU and DU;
    Specify the interface and relative functionalities to support CP and UP between LTE CU and DU;
  To align with the NR CU/DU higher layer split progress, specify the enhancements on the coordination between LTE-CU and NR-CU
    Specify the interface and relative functionalities both CP and UP between LTE CU and NR-CU;
  Specify the possible function improvements according to the SI phase conclusion, including but not limited to
    Intra-system and inter-system mobility handling
    Positioning
    …

## Slide 5: WI time budget
leading WG | WI or SI | Title | latest WID/SID | rapporteur | REL | target | 75 March17 REL-14 freeze | 88bis | 97bis | 95bis | 82bis | 82bis | 89 | 98 | 96 | 83 | 83 | 4 | 76 June17 | 90 | 99 | 97 | 84 | 84 | 5 | 77 Sep.17 | 90bis | 99bis | 97bis | 84bis | 84bis | 91 | 100 | 98 | 85 | 85 | 6 | 78 Dec.17 | 92 | 101 | 99 | 86 | 86 | 7 | 79 March18 | 92bis | 101bis | 99bis | 86bis | 86bis | 93 | 102 | 100 | 87 | 87 | 8 | 80 June18 REL-15 freeze
RAN3 | SI | Architecture Evolution for E-UTRAN |  | China Unicom | R15 | Sep. 17 |  |  |  | 1 |  |  |  |  | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RAN3 | WI | Architecture Evolution for E-UTRAN |  | China Unicom | R15 | Jun. 18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1.5 |  |  |  |  |  | 1 | 1.5 |  |  |  | 1 | 1.5 |  |  |  |  |  | 1 | 1.5 |  |  |  |  |  | 1 | 1.5 |  |  |  | 1 | 1.5 |  |  |  |