## Slide 1: Motivation for new SI on Licensed-Downlink Assisted NB-IoT in Rel-15
3GPP TSG RAN Meeting #75 RP-170339
Dubrovnik, Croatia, March 6-9, 2017
Agenda Item: 10.1.1
Source: Huawei, HiSilicon
Document for: Information

## Slide 2: Justification
Enabling NB-IoT in unlicensed spectrum allows operators to build a unified IoT ecosystem across their licensed and unlicensed resources
Very-low cost spectrum to hold down IoT connection cost as device numbers grow
Gives the chance to compete with other unlicensed solutions in their own space
Re-use what NB-IoT already has as much as possible → chipset economies of scale
Keep eNB hardware impacts small → easier to deploy quickly and cheaply
RAN already has good understanding of unlicensed regimes from LAA/eLAA, so can look to previous study for methodologies and requirements where possible
Unlicensed spectrum is plentiful on the NB-IoT bandwidth scale (i.e. 1 PRB)
Support for massive numbers of connections → Uplink offloading onto unlicensed
High power cellular downlink enables high efficiency and reliable control channels
Unlicensed downlink is very power restricted, ~10 dB to 30 dB lower than cellular
Build on
what we
already have
Unified
IoT
Ecosystem
&
Solutions
Low Cost
Massive Connections
Offloading

## Slide 3: Spectrum bands
Cellular Technology
Frequency Hopping
Contention Based Access
Uplink
Sub 1 GHz
Downlink
700/800/900 MHz
1.8, 1.9 GHz
eNB
Transmitter
Licensed Cellular Carrier
eNB
Receiver
Unlicensed Spectrum

## Slide 4: Network deployment flexibility for operators
LDA-NB-IoT
Mode
Normal
NB-IoT Mode
Cellular
NB-IoT Tx
  Cost to upgrade eNB is low – needs a new filter
Unlicensed
Rx
Cellular
NB-IoT Rx
LDA-NB-IoT
Mode
Normal
NB-IoT Mode
Unlicensed
Rx(s)
Fiber/CPRI
eNB
eNB with additional Rx
Upgraded NB-IoT eNB
RRH in unlicensed spectrum
  Site engineering free
Cellular
NB-IoT Tx
Cellular
NB-IoT Rx

## Slide 5: Spectrum options
Prefer sub-GHz for IoT connections
  Propagation advantages
  MBB services moving to higher frequency bands gradually
Spectrum pairing between licensed spectrum and unlicensed spectrum
  Band 5 and Band 8 cellular bands (700/800/900 MHz) downlink, with
  Unlicensed sub-GHz bands uplink
High priority can be given to spectrum with global availability, but a study item should strive to be band-agnostic

## Slide 6: Transmit regulation options
Frequency hopping preferred
  No PSD restrictions for frequency hopping → max power allowed by regulations can be used
  UE does not always transmit at the maximum bandwidth in the regulations
  Frequency hopping helps interference avoidance in crowded spectrum
Duty-cycle based transmit control preferred
  Duty cycle is not a problem for UE because there are many channels for each UE
  Significantly simplify the designs
  Power consumption friendly
  LBT requires much lower Rx sensitivity for wide coverage (cost to UE)
Options
1. Frequency hopping
2. Digital modulation
Interference averaging
Options
1. LBT
2. Duty cycle transmit control
Fair
Coexistence

## Slide 7: Rel-15 Study Item: March – September 2017
Define an evaluation methodology and architecture suitable for this licensing regime. [RAN1]
Document the relevant requirements and design targets for this licensing regime, in particular:
  Document the relevant existing regulatory requirements for unlicensed UL spectrum deployment in sub-GHz and ISM 2.4 GHz bands [RAN4]
  Identify any differences in the design targets for this feasibility with respect to the LAA study (TR 36.889)
Identify and evaluate physical layer options and enhancements to NB-IoT to meet the requirements and targets for this licensing regime, including consideration of the methods to address the co-existence aspects on unlicensed bands with other LTE and NB-IoT operators and other typical use of the band, including: [RAN1]
  UL frequency hopping for NPUSCH
  Duty-cycle based UL transmit control for NPUSCH
  UL contention-based access without timing advance
Identify the need of and, if necessary, evaluate needed enhancements to the NB-IoT RAN protocols to support deployment in unlicensed spectrum for the scenarios and requirements described above [RAN2]
Assess the feasibility of base station and terminal operation of: [RAN4]
  Band 5 and Band 8 cellular bands downlink, with unlicensed sub-GHz bands uplink.
The study shall strive to be band-agnostic. The study shall assume re-use of the features of NB-IoT up to Rel-14 as much as possible.
→ After the SI, approve a WI Sep 2017 – Jun 2018

## Slide 9: Spectrum and regulations in sub-GHz and ISM 2.4 GHz bands
 | Modulations | <1 GHz (Different in Regions) |  |  | <2.4GHz (2400-2483.5, available globally) |  | 
 |  | EIRP Power (dBm) | PSD | Dwell Time, LBT or Duty Cycle Channel Number | EIRP Power (dBm) | PSD | Dwell Time, LBT Duty Cycle
US 902-928 | FHSS <500kHz | <30, or 36 (with 6dBi antenna) | No | <400ms/20s >50 Channel, if BW<250kHz | <27, or 36 (6dBi antenna) | No | Dwell Time: 1/Channels (s) >15 Channel
 | DSSS >=500kHz | 36 (with 6dBi antenna) | 8dBm/3kHz | No | 36 (6dBi antenna) | 8dBm/3kHz | No
EU 863-870 | FHSS | 14dBm CH BW<100kHz | No | <400ms/20s LBT, or Duty Cycle | 20 | No | <400ms/20s No LBT or Duty Cycle
 | DSSS | 14dBm | Yes | LBT or Duty Cycle | 20 | 10mW/MHz | No
 | Wide/Narrow | Band g1: 14 Band 1.3: 27 | No | LBT or Duty Cycle | 20 | No | No
China 470-510 630-787 | FHSS | No Requirements | No | No | 20 (<10dBi) 27(>=10dBi) | 20/MHz (<10dBi) 27/MHz(>=10dBi) | No
 | Others | 17 dBm | No | <200kHz, <4s | 20 (<10dBi) 27(>=10dBi) | 10/MHz (<10dBi) 17/MHz(>=10dBi) | No
Japan 920-923.5 Korea (TBC) | FHSS | (no FH/DSSS requirements) 24dBm+3dBi 200, 400, 600, 800, 1000 | No | LBT | 10dBm+12.14dBi/MHz | 10dBm+12.14dBi/MHz | <400ms
 | DSSS etc. |  |  |  | 10dBm+12.14dBi/MHz | 10dBm+12.14dBi/MHz | No
 | Others |  |  |  | 10dBm+12.14dBi | 10dBm+12.14dBi | No