## Slide 1: Motivation for New WI on Even further enhanced MTC for LTE
Ericsson, Qualcomm
RP-170466
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6-9, 2017
Agenda item 10.1.1

## Slide 2: Requirements from new use cases
Justification
  Earlier releases have focused on low-mobility cases such as metering devices in basements. As BL UEs are increasingly becoming interesting for other use cases such as wearables, it is relevant to consider improvements for scenarios with higher mobility and new device form factors with small batteries. Therefore, it is proposed to consider specifying support for higher UE velocities and lower UE power classes.
Objective
  Support higher UE velocity [RAN4 lead, RAN2]
    Specify support in CE mode A for higher velocities (e.g. [200] km/h).
  Lower UE power class [RAN4 lead, RAN2]
    Evaluate and, if appropriate, specify new UE power class(es) and signaling support without physical layer changes, to support lower maximum transmit power suitable for new use cases, e.g. wearables and logistics, with appropriate MCL relaxations.

## Slide 3: Next generation requirements
Justification
  3GPP have in TR 38.913 agreed a set of scenarios and requirements for the Next Generation Access Technologies among which a specific set of requirements associated with the massive MTC (mMTC) use case is found. It has also been agreed to include LTE and NB-IoT as part of the 3GPP IMT-2020 submission to ITU. It is therefore time to study the feasibility of LTE MTC to meet the mMTC requirements, and if necessary specify any improvements needed to secure the fulfilment of these requirements.
Objective
  Study the support for the mMTC requirements defined in TR 38.913 and, if needed, specify necessary enhancements to fulfill these requirements. [RAN1 lead, RAN2, RAN3, RAN4]
    Support latency of at most 10 seconds.
    Support coverage of 164 dB Maximum Coupling Loss (MCL).
    Support UE battery life beyond 10 years.
    Support connection density of 1,000,000 devices per square km.

## Slide 4: Improved latency
Justification
  In order to achieve a sufficiently short call setup time also in challenging coverage conditions where a lot of repetition may be required, it is critical to keep the system acquisition time as short as possible. Therefore, it is proposed to consider possible reduction of the and PSS/SSS, PBCH and SI acquisition time (cf. RAN4 LS R4-1610970)
  To further strengthen the support for new uses cases it is proposed to specify a set of latency improvement measures including connection setup improvements, e.g. Msg3 and Msg4 data transmission.
Objective
  Reduced system acquisition time [RAN1 lead, RAN2, RAN4]
    Improved cell search and/or system information acquisition performance
  Support early data transmission [RAN2 lead, RAN1, RAN3]
    Support DL/UL data transmission on a dedicated resource during the Random Access procedure (after Msg1PRACH transmission and before Msg5the RRC connection setup is completed) at least in the RRC Suspend/Resume case.

## Slide 5: Improved power consumption
Justification
  In idle mode in order to improve battery life for applications with low data activity, it is critical to keep the power consumption as low as possible. Therefore, is proposed to target reduced power consumption in particular related to paging and cell (re)selection.
  It should also be ensured that all UE categories can operate in the most optimal (CE or non-CE) mode from coverage and power consumption points of view and it is therefore proposed to identify and address any potential issues with switching between CE mode and non-CE.
Objective
  Power consumption reduction for idle mode paging and connected mode DRX [RAN1 lead, RAN2, RAN4]
    Specify physical signal(s) and/or channel(s) that can be efficiently decoded or detected prior to decoding the physical downlink control channel.
  Relaxed monitoring for cell reselection [RAN2 lead, RAN4]
    Enable relaxed UE monitoring for cell (re)selection e.g. by (re)configuration.
  Support efficient transition between CE mode and non-CE [RAN2 lead]
    Enable CE mode operation (i.e., narrowband) for power saving purposes.

## Slide 6: Improved spectral efficiency
Justification
  In Rel-13 it is assumed that BL UEs have no need for CRS transmissions outside their allocated narrowband but there is nothing precluding that BL UEs monitor CRS outside their allocated narrowband. In order to facilitate flexible deployment of eMTC by improving the possibility for CRS muting (for reduced inter-cell interference), it is proposed to allow the UE to indicate that it does not rely on CRS outside a certain bandwidth.
  It is also worth considering whether the starting PRACH CE level selection procedure can be optimized.
  Physical layer improvements for increased spectral efficiency especially in uplink may also be needed to cater for the envisioned increase in number of connected devices.
Objective
  Specify support for CRS muting [RAN1 lead, RAN2]
    Enable UE to indicate that it does not rely on CRS outside a certain bandwidth.
  Improved CE level selection [RAN4 lead, RAN2]
    E.g. changes to the starting PRACH CE level selection criteria
  Increased PUSCH spectral efficiency [RAN1 lead, RAN2, RAN4]
    E.g. sub-PRB resource allocation

## Slide 7: Improved load control
Justification
  As the number of devices that need to be managed efficiently increases, it is desired that the network has effective tools for access/load control of idle mode UEs.
Objective
  Improved access/load control of idle mode UEs [RAN2 lead]
    E.g. CE-level-based access class barring