## Slide 1
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6 - 9, 2017
RP-17xxxx
Source: Samsung
Title: Motivation for new WI: Further Enhancements on Full-Dimension (FD) MIMO for LTE
Document for: Discussion
Agenda Item: 10.1.1

## Slide 2: FD-MIMO(Rel-13) and eFD-MIMO(Rel-14)
Rel-13 work item on EBF/FD-MIMO was completed in Dec. 2015 with the following features
  Enhancement of non-precoded CSI-RS to support up to 16 ports and relevant CSI mechanism
  Introduction of beamformed CSI-RS and relevant CSI mechanism
  Enhancement of DL DMRS to support up to 4 orthogonal ports
  Enhancement of SRS to improve SRS capacity
Rel-14 work item on eFD-MIMO was finalized in Feb. 2017 with the following features
  Enhancement of non-precoded CSI-RS to support up to 32 ports and relevant CSI mechanism
    Rel-13 codebook extension + advanced CSI (combination) codebook
  Enhancement of beamformed CSI-RS for efficient resource utilization via aperiodic/multi-shot CSI-RS transmission
  Enhancement of UL DMRS for MU MIMO with partial overlapping BW
  Introduction of DMRS-based semi-open-loop transmission
  Introduction of hybrid CSI reporting
    e.g. ‘non-precoded’-’beamformed’, or ‘beamformed’-’beamformed’

## Slide 3: Rel-15 FeFD-MIMO [Motivation 1]
Rel-13/14 focused on definition of new CSI reports (up to 32 ports, adv-CSI) but did not address the limitation on payload size for periodic reports
  As a consequence, CSI reporting is severely constrained in actual utilization (payload size is larger than container)
Operational side effects due to limited payload size for periodic reports
  Complete set of CSI being spread over increased number of reporting instances (Rel-12: CSI is spread over 2 up to subframes, Rel-13: 3 up to subframes)
  Complex priority rules between reporting types
  Increased probability of dropping periodic CSI reports
Proposal: Support new periodic CSI reports with larger max payload
MTC only relies on CRS-based CSI reporting
  Extension of FD-MIMO/eFD-MIMO specification support to MTC can improve DL multiplexing capacity (number of connections)
  Current CSI-RS based CSI reporting requires large payload
Proposal: Introduce CSI-RS-based CSI report for MTC with low-payload

## Slide 4: Rel-15 FeFD-MIMO [Motivation 2]
In Rel-14 eFD-MIMO, advanced CSI is only enabled for non-precoded CSI-RS
  Enhanced resolution of CSI reporting can be beneficial for other FD-MIMO features such as beamformed CSI-RS, hybrid CSI, and semi-open-loop transmission
Proposal: Extend the usage of advanced CSI with other FD-MIMO features
Aperiodic transmission of CSI-RS enables more efficient resource pooling across UEs
  Rel-14 aperiodic transmission of CSI-RS is only enabled for desired channel measurements and rate matching for PDSCH transmission
  Extension to aperiodic interference measurements seems natural
Proposal: Enable efficient usage of CSI-IM by supporting aperiodic ZP CSI-RS for interference measurements

## Slide 5: Objective: Core
Extend specification support for CSI reporting in the following areas [RAN1]
  [Motivation 1] Specify periodic CSI reporting using PUCCH format(s) other than format 2 to facilitate compact and self-contained PUCCH-based periodic CSI reports
  [Motivation 1] Specify aperiodic CSI reporting beyond PUSCH mode 1-1 when configured together with enhanced carrier aggregation
  [Motivation 1] Specify low-payload CSI reporting which takes advantage of FD-MIMO for the purpose of MTC-type applications
  [Motivation 2] Specify necessary components to enable concurrent usage of advanced CSI codebook with UE-specific beamformed CSI-RS (with 2, 4, or 8 ports), hybrid CSI, and semi-open-loop transmissions
  [Motivation 2] Specify aperiodic CSI-IM for interference measurement overhead reduction in high-load MU-MIMO scenario
Specify higher layer support of enhancements listed above [RAN2]