## Slide 1
Source: Samsung
Motivation for new WI: Further enhancements
on NB-IoT
RP-170677
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6 - 9, 2017 Agenda item: 10.1.1 Document for: Discussion

## Slide 2: Justification
eMTC/NB-IoT align with mMTC requirements
  NB-IoT was specified in Rel-13 and further enhanced in Rel-14, targeting to IoT/MTC business, with extended coverage, longer battery life, and low complexity device.
  It was agreed that “3GPP’s IMT-2020 self-evaluations towards mMTC requirements will assess NB-IoT
  and/or LTE eMTC”.
IoT/MTC marketing is maturing
  Global operators start to launch cellular IoT/MTC service with NB-IoT.
  Massive connections of IoT/MTC device will be the challenge in the near future.
Further enhancement on NB-IoT in Rel-15
  Target to mMTC requirements:
    Coverage of 164dB MaxCL (with 9dB/5dB noise figure at UE and eNB side),
    Less than 10 seconds latency,
    More than 10 years battery life, and
    Support of massive connection of 1 000 000 device/km2 .
  Study the achievable performance of NB-IoT over TDD spectrum, and specify necessary changes.

## Slide 3: Gap of NB-IoT and eMTC for mMTC
NB-IoT to 5G mMTC
  Some gaps (MCL, Battery life, Latency) are expected to 5G mMTC requirement due to “noise figure” and some practical constraint (e.g., NPDCCH period).
  Connection density needs to be optimized.
KPI | 5G mMTC | NB-IoT
Coverage | 164dB with 160bps (with 5dB/9dB noise figure) | 144dB +20dB MCL with 160bps (with 3dB/5dB noise figure)
Battery life | Beyond 10 yrs with UL 200 bytes per day followed by 20bytes DL from MaxCL of 164dB | up to 10 yrs with 20dB coverage extension. (with 3dB/5dB noise figure)
Latency | <10s with 20 bytes application package @ 164dB MCL | 10s event trigger @164dB MCL theoretically. (with 3dB/5dB noise figure, NPDCCH period constraint )
Connection density | 1 000 000 device/km2 | 52547 device with ISD 1732m (i.e., ~600 00 device/km2 per 200kHz)
Low cost | Ultra-low cost devices | Significantly reduce complexity and hence cost.
Positioning and multi-cast | Supported positioning and multi-cast | Supported

## Slide 4: Massive connections
Motivation:
  To meet connection density (1e6 per sq km) requirement of mMTC with a high spectrum efficiency is desirable.
  Traffic model for mMTC is expected to be denser than traffic model used in TR 45.802, i.e., 11.2 sessions per device per day:
  Congestion control is needed to handle massive connections
Possible solutions:
  Larger capacity for uplink reference signals/preambles and random access preambles.
  Congestion control.
  UE group scheduling to reduce control overhead and UE power consumption.
  Support CSI feedback for no or small coverage enhancement.
  Enable operating NB-IoT in unlicensed spectrum to offload the connections.

## Slide 5: Latency reduction and 10 years battery life
Motivation:
  It is required to support less than 10 seconds latency for exception report in extreme coverage.
  With the constraint of NPDCCH period, it is barely can support less than 10 seconds latency in extreme coverage for NB-IoT system.
  Some gaps are expected to 10 years battery life with 5/9dB noise figure .
Possible solutions:
  SPS for both uplink and downlink.
  Early termination of uplink and downlink data transmissions.
  Mechanisms to enable data transmission/reception without RRC transition to connected state.
About 9 NPDCCH periods are needed to finish signaling flow in RRC
resume. Assuming Rmax = 512, it about 512*1.5*9 = 6912ms after
NPRACH without counting UL/DL data channel.

## Slide 6: Coverage
Motivation:
  NB-IoT can support 164dB MCL coverage with 3/5dB noise figure.
Possible solutions:
  Enhancement of DL common channels/signals.
  Specify more repetitions or other techniques (e.g., PSD boosting, channel estimation enhancements, link adaptation enhancements) to further improve coverage of unicast channels.

## Slide 7: NB-IoT over TDD spectrum
Motivation:
  TDD spectrum exists globally, and support NB-IoT in TDD spectrum can enlarge the NB-IoT ecosystem.
  Competing LWPA techniques use TDD spectrum.
  Similar performances can be expected (with two TDD carriers) compared with HD-FDD.
Possible solutions:
  Study the achievable performance of NB-IoT over TDD, and specify necessary specification change to support TDD for NB-IoT for in-band, guard-band and standalone operation, at least including :
    SIB-NB and MIB-NB/NSSS(if needed) on non-anchor PRB.
    Necessary changes on NPRACH transmissions to support discontinuous transmission.
    Special subframe with 3.75kHz subcarrier spacing for the uplink.