## Slide 1: Motivation of Sidelink Framework
CATT
RP-171110
3GPP TSG RAN Meeting #76
West Palm Beach, FL, USA, May 5 – 8, 2017

## Slide 2: NR Sidelink Use Cases
Sidelink is a direct link for communications between devices
  Sidelink has been used for everal applications, such as Proximity service (D2D), V2V, V2P, IoT, wearable.
Sidelink provides different operations for end-to-end communication
  Distributed control and managements among devices
  Direct communication with and without network coverage
  Extended range of communication through relay
Potential se cases for NR sidelinks
  SA1 V2X requirements
    Including V2V and V2P
  Public safety NR D2D for out of network and in-network
  IoT: including machine type communication and sensors
  Wearable devices: communication between devices

## Slide 3: Sidelink Framework
A generic sidelink framework for all use cases
  A single mode operation for communication between different use cases – e.g. V2P
    Avoid incompatible operation between different use cases
    Forward compatibility of any sidelink features in the future
      IoT would be one driving force of NR applications
  Co-existence and inter-working between different applications in the same spectrum – e.g. wearable devices, IoT devices, ProSe
  Flexible duplex – Dynamic resource allocation of DL/UL/SL
  Minimize mutual interference – joint interference management among DL/UL/SL with different sidelink applications
  Extended coverage through relay by same or different sidelink applications.

## Slide 4: Objectives of Sidelink Framework
Main objective – sidelink system design to support eV2X with forward compatibility to support ProSe, IoT, and wearable devices.
Sidelink system design to support broadcast, multi-cast, and unicast
  Unicast as the starting point with link adaptation and QoS control
  Multi-cast and broadcast are further optimized from sidelink system design for unicast
Sidelink architecture, interface, protocol
  Physical Layer structure and procedure for sidelink
  U-plane and C-plane sidelink functions
  Distributed control - QoS architecture, access control, priority control, mobility management
UE to UE relay - low latency, extended coverage, better reliability, UE power saving
UE positioning and tracking
Co-existence and Inter-working with applications provided by LTE sidelink and IEEE 802.11p-based V2X
Operation environment s – within NR network, within LTE network, OOC

## Slide 5: eV2X SA1 requirements summary
Use case group | Descriptions | KPI
Platooning operation | Enables the vehicles to dynamically form a platoon travelling together. | Broadcast, groupcast and unicast; Announcing/joining/leaving operation; 50-1200 bytes, 40Hz, 25ms, 90%, less than 100m; 50-1200 bytes, 100Hz, 10ms, [99.99%], less than 100m; [6500]bytes, [50]Hz, [20]ms, high reliability, [10] sec * max relative speed ; [65]Mbps, [50]Hz, [20]ms, high reliability, [5] sec * max relative speed ;
Advanced driving | Enables Limited/Full automated driving, vehicles share their own perception data with other vehicles in proximity, to synchronize and coordinate their driving trajectories. | Broadcast; [6500]bytes, [10]Hz, [100]ms, high reliability, [10] sec * max relative speed; [53]Mbps, [10]Hz, [100]ms, high reliability, [5] sec * max relative speed; [10]Mbps and message size range up to [2]M bytes, [100]Hz, [10]ms,[99.99%]; [30]Mbps, [3]ms, [99.999%], [500]m; DL broadcast: [0.5]Mbps, UL unicast:[50]Mbps, [50]Hz, [20]ms
Extended sensor | Enables exchange of raw or processed sensor data to build collective situational awareness. | Broadcast; [1600]bytes, [10]Hz, [100]ms, [99%], [1000]m; [10]Mbps, [20]Hz, [50]ms, [90%], [100]m; [25]Mbps, [100]Hz, [10]ms, [90%], [x]m [700]Mbps, [100]Hz, [10]ms, [99.99%], [500]m [x]-[1]Gbps, [3]-[50]ms, [99%-99.999%], [50]-[1000]m
Remote driving | Enables a remote driver or a V2X application to operate a remote vehicle. | Unicast; DL :1Mbps, UL: 20Mbps, 5ms, 99.999%; DL :[1]Mbps, UL: [25]Mbps, [20]ms, [99.999%];

## Slide 6: Proposed work plan for Rel-15 and future
Release
14
Sidelink
Release
12
-
13
Release
15
Release
16
Release
17
LTE D
2
D
,
eD
2
D
LTE
-
eV
2
X
NR sidelink SI after NR phase 1
NR V
2
X SI
/
WI
NR other sidelink
SI
/
WI
LTE
-
V
2
V
/
V
2
X
Further enhancements based
on LTE
Timeline
  NR sidelink framework SI starts in January 2018 release 15 to support eV2X and forward compatibility features, such as NR D2D, IoT, and wearable.
    NR V2X SI/WI starts after a completion of sidelink framework