## Slide 1
3GPP TSG-RAN #77 RP-171528
Sapporo, Japan, 11-14 September, 2017
RAN6 Chair: Juergen Hofmann (NOKIA)
RAN6 Secretary: Paolo Usai (ETSI MCC)
Status Report RAN WG6 to TSG-RAN #77

## Slide 2: Meetings
Meetings held since RAN#76 plenary
RAN6 #5 | 21 – 25 August, 2017 | Berlin, Germany | EF3
RAN #77 | 11 – 14 September, 2017 | Sapporo, Japan | ARIB, TTC

## Slide 3: RAN6 #5 Meeting Schedule
The meeting schedule for RAN6#5 was agreed.

## Slide 4: RAN6 #5 Statistics (1/3)
Incoming: 77
Total: 132

## Slide 5: RAN6 #5 Statistics (2/3)
Total CRs: 50

## Slide 6: RAN6 #5 Statistics (3/3)
Total number of participants attending: 20 (registered for the meeting: 35)

## Slide 7: Executive Summary
In total 50 CRs agreed: to UMTS specs (12), to GERAN specs (38).
Liaisons: 2 incoming LS (UMTS) and 3 outgoing LS (1 UMTS, 2 GERAN).
GERAN, Rel-12+: 18 CRs agreed on removal of references to GERAN Iu mode specs 44.118 and 44.160.
GERAN, Rel-13: agreed CRs for eDRX_GSM (2)
GERAN, Rel-14: agreed CRs on Positioning Enhancements for GERAN (9), Radio Interface Enhancements for EC-GSM-IoT (5), TEI-14 including GANSS Time model clarifications (3). LS sent to RAN5 on completion of two Rel-14 features.
GERAN, Rel-14: Discussion on restricted use of enhanced coverage. LS sent to CT1 to receive guidance for specifying the Access Stratum behaviour.
GERAN, Rel-15: 1 agreed CR on fast detection of EAB conditions. No work item or study item proposal contributed.
UMTS, Rel-12+: 3 CRs agreed on removal of references to GERAN Iu mode specs. UMTS, Rel-14: 3 CRs agreed on RRC corrections, GANSS Time model clarifications and DL Interference Mitigation.
UMTS, Rel-15: Simplified HS-SCCH type 1 operation introduced in specs
  Concept proposals and stage 2 / stage 3 descriptions (6 CRs) agreed, LS sent to RAN3
UMTS, Rel-15: Proposal on runtime QoE contributed, discussion started.
UMTS 25.xxx rapporteur responsibilities partially updated.
List of agreed CRs in RP-171529 which are for block approval at RAN#77.

## Slide 8: General Matters/RAN6 #5 Report Approval
Report of 3GPP TSG RAN WG6 meeting #4, R6-170405 approved.
Tdoc reservation and submission deadline was confirmed to be kept (Friday, 10 days before meeting start, 21.00 CEST).
Delegates were reminded to commemorate François Courau, the former Chairman of ETSI SMG12, ETSI SMG2 WPA, 3GPP TSG RAN and ETSI MSG who had passed away.

## Slide 9: Liaisons (1/2)
Two incoming LSs were received.
R6-170331 LS on the conclusions for the SI on a simplified HS-SCCH for UMTS (source: RAN1)
  RAN1 informs about the conclusion of the completed study item, the work being documented in TR 25.709, to be taken into account as background for the work on the successive Rel-15 work item. The LS was noted.
R6-170332 LS on enhanced scheduling for UMTS (source: RAN1)
  RAN1 informs about the conclusion of the completed study item, the work being documented in TR 25.708, to be taken into account. The LS was noted.

## Slide 10: Liaisons (2/2)
Three outgoing LSs were sent.
R6-170424 LS on the WI of a simplified HS-SCCH for UMTS (to: RAN3)
  RAN6 informs about the achieved progress for the work item at RAN6#5. In particular agreed concept proposals and agreed CRs are listed for the simplified HS-SCCH type 1 operation, applicable in CELL_DCH state. Higher layer signalling for this feature is needed to convey the network capability and UE capability and hence RAN3 is asked to update its relevant specs.
R6-170458 LS on completion of core parts of Rel-14 features Positioning Enhancements for GERAN and Radio Interface Enhancements for EC-GSM-IoT (to: RAN5 cc: ETSI MSG)
  RAN6 informs on the completion of Rel-14 features (Positioning enhancements for GERAN and Radio Interface Enhancements for EC-GSM-IoT), and asks RAN5 to provide feedback on their plan to specify MS conformance tests for these features.
R6-170460 LS on Restricted Use of Enhanced Coverage (to: CT1 cc: SA2, RAN2)
  RAN6 raises questions on the impact to radio link control and mobility management procedures for the Rel-14 feature and guidance from CT1 is requested for specifying the AS behaviour.

## Slide 11: Contributions to Rel-13 and Earlier Features (GERAN)

## Slide 12: eDRX_GSM (Rel-13)
Set of 2 essential corrections agreed related to clarification of MS behavior when the network discontinues support of Rel-13 features and rolls back to pre-Rel-13 feature support.
CR 44.018 Miscellaneous corrections for PEO_BCCH_CHANGE_MARK (Rel-13) agreed in R6-170437
  Rel-14 mirror in R6-170438
CRs for Approval
The agreed CRs are collected in RP-171598 for block approval at RAN#77.

## Slide 13: CIoT_EC_GSM, Core and Perf aspects (Rel-13)
No contributions.

## Slide 14: CS/PS Coordination for Shared GERAN Networks (Rel-13)
No contributions.

## Slide 15: Removal of references to TS 44.118 and TS 44.160 (GERAN Iu mode)
In accordance with the decision taken at RAN#76, references to GERAN Iu mode specifications TS 44.118 and TS 44.160 were removed in specifications under RAN6 responsibility from Rel-12.
A set of 21 CRs to GERAN and UTRAN specs was agreed under TEI12:
  In TS 25.331: R6-170359 (Rel-12), R6-170360 (Rel-13), R6-170361 (Rel-14)
  In TS 43.059: R6-170389 (Rel-12), R6-170390 (Rel-13), R6-170391 (Rel-14)
  In TS 43.129: R6-170392 (Rel-12), R6-170393 (Rel-13), R6-170394 (Rel-14)
  In TS 43.130: R6-170395 (Rel-12), R6-170396 (Rel-13), R6-170397 (Rel-14)
  In TS 44.004: R6-170398 (Rel-12), R6-170399 (Rel-13), R6-170400 (Rel-14)
  In TS 44.060: R6-170336 (Rel-12), R6-170335 (Rel-13), R6-170334 (Rel-14)
  In TS 45.008: R6-170347 (Rel-12), R6-170348 (Rel-13), R6-170349 (Rel-14)
CRs for Approval
The agreed CRs are collected in RP-171597 for block approval at RAN#77.

## Slide 16: Contributions to Rel-14 Features (GERAN)

## Slide 17: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (1/3)
One concept refinements of the Multilateration Timing Advance (MTA) positioning method at RAN6 #5 agreed:
On Definition of BTS Reception Accuracy Capability for Multilateration Positioning, R6-170441, with agreement on reporting up to two values to SMLC:
  BSS reports BTS Reception Accuracy Capability down to RACH sensitivity level if the BTS supports PEO and/or
  BSS reports BTS Reception Accuracy Capability down to EC-RACH (CC1) sensitivity level if the BTS supports EC-GSM-IoT.
Further agreements found:
Range for BTS Reception Accuracy Capability and BTS Reception Accuracy Level extended from 4 bits to 5 bits to include supported range by legacy BTS.
DL and UL Coverage Class are informed to SMLC in the Perform Location Request message to allow SMLC to distinguish the position estimate procedure between a PEO and EC-GSM-IoT device.

## Slide 18: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (2/3)
Normative Work
CR 44.060 Corrections to figures 10.3a.2.1.1 and 10.3a.2.2.1 agreed in R6-170410
  Correction of table formatting and note.
CR 49.031 Clarifying Use of Random ID Set IE and BTS Reception Accuracy Capability IE agreed in R6-170439
  Extension from 4 to 5 bit for latter IE.
CR 48.008 Clarifying References to BTS Reception Accuracy Level IE agreed in R6-170440
  Range for BTS Reception Accuracy Level extended to 5 bits.
CR 48.018 Correction of the BTS Reception Accuracy Level IE agreed in R6-170413
  Range for BTS Reception Accuracy Level extended to 5 bits.
CR 49.031 Corrections to BTS Reception Accuracy Capability for Multilateration Positioning, agreed in R6-170447
  Up to 2 BTS Reception Accuracy Capabilities added to Assistance Information message.
  UL and DL coverage class added to Perform Location Request.

## Slide 19: Positioning Enhancements in GERAN - ePOS_GERAN (Rel-14) (3/3)
Normative Work (cont’d)
CR 45.010 Corrections to BTS Reception Accuracy Capability for Multilateration Positioning agreed in R6-170448
  Introduces requirements for verifying BTS Reception Accuracy Capability for PEO and for EC operation.
CR 51.021 Corrections to BTS Reception Accuracy Capability for Multilateration Positioning agreed in R6-170444
  Adds corresponding changes to BTS conformance testing.
CR 45.005 Performance Requirements for Extended AB agreed in R6-170425
  Performance requirements for Extended Access Burst are finalized.
CR 51.021 Performance Requirements for Extended AB agreed in R6-170426
  Adds corresponding changes to BTS conformance testing.
CRs for Approval
The agreed CRs are collected in RP-171594 for block approval at RAN#77.

## Slide 20: Support of Dedicated Core Networks - DECOR_GERAN (Rel-14)
WI closed at RAN#73.
No contributions.

## Slide 21: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (1/3)
Alternative Mappings for Higher Coverage Classes with 2 PDCHs - Normative work
2 essential corrections agreed at RAN6#5.
CR 45.005 Performance requirements for uplink CC5 and for Alternative Coverage Class mapping method agreed in R6-170445
  Receiver performance requirements for sensitivity, ACI and CCI for higher coverage classes CC2 to CC5 (CC5 for UL only) based on 2 PDCHs finalized.
CR 51.021 Performance requirements for uplink CC5 and for Alternative Coverage Class mapping method agreed in R6-170446
  Adds corresponding changes to BTS conformance testing.

## Slide 22: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (2/3)
UL MCL Improvement for Low Power Devices in EC-GSM-IoT
Following concept refinements at RAN6#5 agreed:
Training Sequence Selection for CC5 EC-RACH using EDAB, R6-170456 with agreement:
  Use of training sequence TS5, TS6 or TS7 for EDAB in dependency of the EC-RACH configuration (1 TS or 2TS) and used training sequences in cell.
Normative Work
CR 44.018 Training Sequence selection for CC5 EC-RACH using EDAB, agreed in R6-170452
  Corrections to messages using ESAB and EDAB and training sequence usage for EDAB.
CR 45.002 Training Sequence selection for CC5 EC-RACH using EDAB, agreed in R6-170457
  Training sequence determination for EDAB.
CR 45.002 Remove brackets for TS8 for ESAB agreed in R6-170344
  Training sequence for ESAB finalized.

## Slide 23: Radio Interface Enhancements for EC-GSM-IoT (Rel-14) (3/3)
UL MCL Improvement for Low Power Devices in EC-GSM-IoT - Normative work (cont’d)
CR 45.005 Performance requirements for uplink CC5 and for Alternative Coverage Class mapping method agreed in R6-170445
  Receiver performance requirements for sensitivity, ACI and CCI for traffic channel EC-PDTCH and associated control channel EC-PACCH based on 4 PDCHs and for EC-RACH finalized, except for ESAB, which is foreseen to be finalized at RAN6#6.
CR 51.021 Performance requirements for uplink CC5 and for Alternative Coverage Class mapping method agreed in R6-170446
  Adds corresponding changes to BTS conformance testing for all CC5 related performance requirements finalized in TS 45.005.
CRs for Approval
The agreed CRs are collected in RP-171595 for block approval at RAN#77.

## Slide 24: Small technical enhancements and improvements (TEI14) (1/2)
CR 44.060 Handling of PCCN message including a 3G CCN Measurement Report with no available 3G neighbour cell report, R6-170330
  Inconsistency observed for reporting neighbor cells in the Packet Cell Change Notification message in CCN mode for the case that no 3G cells are reported by the MS.
  The corresponding late CR for Rel-14 was postponed at RAN6#4 to allow companies to check the proposed solution.
  It was agreed at RAN6#5.
CR 44.060 Clarification of DL PACCH DRX in Extended Uplink TBF Mode
  Clarification added that MS in PEO entering extended uplink TBF has to monitor DL PACCH only when there is no downlink TBF.
CRs for Approval
The agreed CRs are collected in RP-171593 for block approval at RAN#77.

## Slide 25: Small technical enhancements and improvements (TEI14) (2/2)
Impacts to RLC Procedures from Restriction on Use of Enhanced Coverage, R6-170381
  Considers impacts of the Rel-14 feature “Restricted use of enhanced coverage” as part of the WI CIoT_Ext (SA) to radio link control and mobility management procedures, such as cell reselection, coverage class selection, Routing Area update and the removal of enhanced coverage restriction via paging.
  The AS behaviour is not specified for GERAN in Rel-14 as RAN6 did not receive a reply LS from SA2 or CT1 informing us on the completion of stage 2 or stage 3 for NAS behavior for this joint work item.
  In particular network connectivity for devices in extended coverage receiving the enhanced coverage restriction command needs to be considered in more detail.
  Accompanying Rel-14 CRs to TS 43.064, 44.018, 45.008 and 48.018 in R6-170382 to R6-170385 to specify the AS behavior were postponed, since the AS behaviour of this feature needs further clarification from CN perspective.
LS sent to CT1 in R6-170460 to receive guidance on the raised matters (see outgoing LSs).

## Slide 26: Contributions to Rel-15 Features (GERAN)

## Slide 27: New work item proposals (GERAN)
No contributions.

## Slide 28: Small technical enhancements and improvements (TEI15) (2/2)
CR 44.018 Faster Detection of EAB Barring Conditions, R6-170454
  It is clarified that a change in the EAB Authorization mask and EAB Subcategory fields alone shall not be indicated using the BCCH_CHANGE_MARK and PEO_BCCH_CHANGE_MARK fields. Only when EAB is enabled / disabled or when the set of PLMNs affected by EAB is changed will these fields be used to indicate system information has changed.
  This identifies a change of the network’s broadcast behavior for Rel-15.
  The benefit is (1) a reduced power consumption for MS not using EAB since they will not perform SI acquisition due to EAB no longer triggering changes to BCCH_ CHANGE_MARK and PEO_BCCH_CHANGE_MARK fields when only the EAB Authorization mask and EAB Subcategory fields change, and (2) network can make changes to EAB Authorization mask and EAB Subcategory fields every 30 seconds instead of being limited by the maximum number of changes to BCCH_CHANGE_ MARK and PEO_BCCH_CHANGE_MARK fields allowed per 24 hour period.
CRs for Approval
The agreed CR is presented in RP-171596 for approval at RAN#77.

## Slide 29: Contributions to Rel-12 and earlier releases (UMTS)

## Slide 30: UMTS (Rel-12) and earlier releases
Contributions treated under removal of references to GERAN Iu mode specification 44.118 (i.e. CR 25.331 from Rel-12), see slide 15.

## Slide 31: Contributions to Rel-13 features (UMTS)

## Slide 32: Contributions to Rel-13 features (UMTS)
No contributions.

## Slide 33: Contributions to Rel-14 features (UMTS)

## Slide 34: DL interference mitigation for UMTS (UTRA_DL_IM-Core, Rel-14)
CR 25.300 Corrections for DL Interference Mitigation agreed in R6-170422
  Clarifies that signaling of the indication for adjacent interference is done in SIB5, SIB5bis and SIB6.
  Introduces editorial corrections to improve the functional description of the feature.
CRs for Approval
The agreed CR is presented in RP-171591 for approval at RAN#77.

## Slide 35: Small technical enhancements and improvements (TEI14)
CR 25.331 ASN.1 corrections for RRC 25.331, R6-170351
  Miscellaneous corrections related to tabular, ASN.1 non-critical extension ‘vexy’ replaced with ve30.
CRs for Approval
The agreed CR is presented in RP-171590 for block approval at RAN#77.

## Slide 36: Contributions to Rel-15 Features (UMTS)

## Slide 37: Simplified HS-SCCH for UMTS (1/3)
WI opened at RAN#76 (target completion RAN#78).
Set of discussion papers with proposals presented:
  On the simplified HS-SCCH type 1 operation, R6-170354, noted. It provides an overview of the SI conclusion.
  On the triggering mechanism for the simplified HS-SCCH based on legacy CQI reports, R6-170355, noted. Proposal 1 (definition of fixed timing (4 subframes) for receiving the simplified HS-SCCH Type 1 when the legacy CQI reports are used as triggering mechanism) agreed. Proposal 2 (agree CR 25.214 in R6-170356) not agreed.
  On the triggering mechanism for the simplified HS-SCCH based on HS-SCCH orders, R6-170408, agreed. Proposal 1 (use of triggering mechanism based on HS-SCCH orders as complementary trigger mechanism) and Proposal 2 (normative text proposals to be adopted for CR 25.214 and CR 25.212; fallback to CQI based triggering after deactivation of HS-SCCH orders based triggering) agreed.
  Impacts on layer 2 and 3 specifications, R6-170418, agreed. Proposal 1 (operation in CELL_DCH state, Proposal 2 (name of feature: Simplified HS-SCCH type 1 operation), Proposal 3 (network support for Simplified HS-SCCH in RRC messages) and Proposal 4 (UE capability support in UE radio access capability) agreed.

## Slide 38: Simplified HS-SCCH for UMTS (2/3)
Overall 6 CRs agreed on this feature.
Two Stage 2 CRs agreed:
  CR 25.300 Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170353, providing a reference to functional overview description in TS 25.308.
  CR 25.308 Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170419, agreed providing the functional overview description of the feature.
Four Stage 3 CRs agreed:
  CR 25.214 Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170436, specifying the interworking of both trigger mechanisms (CQI based, HS-SCCH order based).
  CR 25.212 Introduction of the HS-SCCH orders for the additional triggering mechanism based on HS-SCCH orders Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170409, specifying the HS-SCCH orders for this feature.
  CR 25.331 Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170420, specifying network support for the feature in Radio Bearer Reconfiguration, Radio Bearer Setup, Radio Bearer Release messages.
  CR 25.306 Introduction of Simplified HS-SCCH type 1 operation for UMTS, R6-170421, specifying UE feature support in the UE radio access capability IE.

## Slide 39: Simplified HS-SCCH for UMTS (3/3)
Work plan for the WI on a simplified HS-SCCH for UMTS , R6-170406, agreed.
  Completion level lifted to 85%.
LS sent to RAN3 in R6-170424 to inform on the progress (see outgoing LSs).
CRs for Approval
The agreed CRs are collected in RP-171592 for block approval at RAN#77.
WI Status Report to RAN#77
Status report of WI Simplified HS-SCCH for UMTS, RP-171903

## Slide 40: New work item proposals (UMTS)
Proposal for run-time QoE Management, R6-170386, noted.
  This describes a complementary solution approach, independent of the Rel-14 QMC framework which triggers run-time control actions to achieve superior QoE, while controlling the congestion at different levels in the Radio Network.
  Companies were invited to consider the proposal and discuss the need for standardizing this approach given there are no UE impacts; however considering the impact this approach has on the CN, the need to handle this through SA was raised, and more details about RAN impacts were asked to be provided.

## Slide 41: Other Rel-15 items (UMTS)
No contributions to “Small technical enhancements and improvements [TEI15]”
No contributions to “Study items for Rel-15”
No contributions to “Any other Rel-15 documents”

## Slide 42: Common GERAN / UMTS matters
Problems with GANSS Time Model Assistance Data, R6-170401, noted.
  discusses problems when determining the GNSS-GNSS system time offset for the case that the GANSS time model provides assistance data for two GNSS and proposes modifications affecting SMLC/location server and MS/UE.
  The SMLC and MS behaviour are proposed to be corrected for RRLP in TS 44.031 for GSM and for RRC in TS 25.331 for UMTS from Rel-14.
Accompanying CRs for GERAN and UMTS for Rel-14 (TEI-14) agreed:
  CR 44.031 Clarification to GANSS time model, R6-170402
  CR 25.331 Clarification to UE positioning GANSS time model, R6-170423
CRs for Approval
The first above CR is presented in RP-171593 for block approval at RAN#77.
The second above CR is presented in RP-171590 for block approval at RAN#77.

## Slide 43: Other technical work
Update of Rapporteur responsibilities for UMTS 25.xxx specifications
  Upon the move of UMTS specifications TS 25.xxx under RAN1/RAN2 responsibility to RAN6, responsibilities for these UMTS specs were partially updated at RAN6#5.
  Further work to complete the update as well as the update of rapporteur responsibilities for GERAN specs is needed.
  This will be progressed by RAN6 leadership prior to RAN#78.

## Slide 44: Work Plan
Presented in R6-170450 and approved.
Work / Study Item | Objective | Rel (Core Feature) | Completion
UTRA_simple_HSSCCH-Core | Simplified HS-SCCH type 1 operation (Stage 2 + Stage 3) | Rel-15 | 85%

## Slide 45: RAN WG6 Schedule (2016 – 2018)
Meeting | Date | Location | Host
RAN6#1 | 22 – 26 August 2016 | Gothenburg, Sweden | EF3
RAN#73 | 19 – 22 September 2016 | New Orleans, US | NAF3
RAN6#2 | 14 – 18 November 2016 | Reno, US | NAF3
RAN#74 | 5 – 8 December 2016 | Vienna, Austria | EF3
RAN6#3 | 13 – 17 February 2017 | Athens, Greece | EF3
RAN#75 | 6 – 9 March 2017 | Dubrovnik, Croatia | EF3
RAN6#4 | 15 – 19 May 2017 | Hangzhou, China | Huawei
RAN#76 | 5 – 8 June 2017 | West Palm Beach, US | NAF3
RAN6#5 | 21 – 25 August 2017 | Berlin, Germany | EF3
RAN#77 | 11 – 14 September 2017 | Sapporo, Japan | ARIB, TTC
RAN6#6 | 27 November – 1 December 2017 | Reno, US | NAF3
RAN#78 | 18 – 21 December 2017 | Lisbon, Portugal | EF3
RAN6#7 | 26 February – 2 March 2018 | Athens, Greece | EF3
RAN#79 | 19 - 22 March 2018 | India | 
RAN6#8 | 21 - 25 May 2018 | Korea | 
RAN#80 | 11 - 14 Jun 2018 | North America | NAF3
RAN6#9 | 20 - 24 Aug 2018 | Gothenburg, Sweden | EF3
RAN#81 | 10 - 13 Sep 2018 | Gold Coast, Australia | 
RAN6#10 | 12 - 16 Nov 2018 | TBD (US) | 
RAN#82 | 10 - 13 Dec 2018 | Sorrento, Italy | EF3

## Slide 46: Concluding Remarks
A special thanks to Paolo Usai (ETSI MCC) for his efficient secretary support.
Thanks to all delegates for their hard work.
Thanks to the host EF3 for the convenient meeting organization.