## Slide 1: Standardization of narrowband V2X in Rel-15
LG Electronics
3GPP TSG RAN Meeting #77 RP-171621 Sapporo, Japan, September 11 - 14, 2017
Agenda item: 10.6.5

## Slide 2: Narrowband V2X
“Narrowband V2X” means V2X operations using “bandwidth limited UEs” similar to the Cat-M1 UEs.
  Uplink and downlink for narrowband V2X can use the functionality specified via eMTC WI.
Focus is on sidelink transmissions where currently all the V2X UEs are required to support at least 10 MHz bandwidth transmissions.
  In many cases, only a subset of the system bandwidth is used for the actual transmission of each individual UE.
  If a UE needs to receive sidelink V2X, reception over the whole system bandwidth is necessary to receive FDMed transmissions from multiple UEs.

## Slide 3: Motivation of Narrowband V2X
It was concluded that reducing maximum transmission bandwidth can contributed to UE power and cost reduction [1].
  UEs in some V2P and V2I use cases do not need to perform reception but transmit only.
    Sidelink TX and RX are separated UE capability since Rel-14.
Motivation scenario #1: Power saving of pedestrian UE
  The pedestrian UE can reduce its transmission bandwidth to save power consumption.
    Up to 20% power saving can be achieved depending on the operation scenario [2].
Motivation scenario #2: Involvement of CAT-M1 UEs in V2X
  For example, a UE in a smartwatch can transmit V2P messages.
Motivation scenario #3: Low-cost deployment of UE-type RSUs
  RSU deployment cost can be reduced if such RSUs only transmit low-rate information such as traffic signals, road information, etc.

## Slide 4: Scope of standardization in Rel-15
Backward compatibility to Rel-14 needs to be kept.
  Rel-14 UEs should be able to receive sidelink transmissions from a narrowband V2X UE.
  Minor specification effort is expected mostly in RAN4.
    RF requirement needs to be specified for PSCCH/PSSCH transmissions of bandwidth limited UEs in Band 47 (i.e., 5.9 GHz band). The following changes are expected in TS36.101:
      Editorial addition of new V2X Channel BW w/ 1.4MHz to Band 47
      Analysis on MPR requirements for power class 3
      Further clarification on frequency error/In-band emission relaxation for narrow channel bandwidth
    But works for UL cases of CAT-M1 UEs can be reused much.
  We note that a similar work needs to be done if a follow-up WI of feD2D SI is approved.
  Small optimization can be considered in RAN1 in order to deal with frequency change between initial transmission and retransmission.
    E.g., UE behavior can be modified in order to avoid selecting two contiguous subframes.

## Slide 5: Proposal
It is proposed to standardize “narrowband V2X” in Rel-15.
  To support sidelink transmissions in Band 47 from a UE whose bandwidth is limited to 1.4 MHz.
  Such transmissions should be received by Rel-14 UEs.
This objective can be added to the WI on 3GPP V2X phase 2.
  Main work will be in RAN4 but small additional TU will be sufficient.
Alternatively, this objective can be handled as a part of a follow-up WI of feD2D SI.
  If such a WI is approved, SL RF requirement bandwidth limited UEs will be specified anyway.

## Slide 6: Reference
[1] 3GPP TR 36.888, Machine-Type Communications (MTC) User Equipments (UEs) based on LTE.
[2] R1-1713120/R2-1708452/ R4-1707910, “Discussion on standardization of narrowband V2X in Rel-15,” LG Electronics.