## Slide 1
Source: Samsung
Motivation to Study on MBMS for NR
Agenda Item: 9.1, Document for: Discussion and Decision
RP-171808
3GPP TSG RAN Meeting #77
Sapporo, Japan, September 11th - 14th, 2017

## Slide 2: Introduction
Dramatic growth for demand of immersive video to mobile devices
  UHD (4K/8K) contents rapidly replacing HD/FHD contents
  New form of immersive service (e.g., VR/AR, car infotainment) getting popular
  Heavy network traffic for popular live programming such as sports, news
Network traffic during England-Wales match
65% increase
Time
Mobile Network Traffic
Source: EE, UK, 2016
54 % CAGR 2016~2021 in mobile video

## Slide 3: MBMS Evolution and Motivation for New SI
TR 38.913 (MBMS requirements for NR)
  High Mobility of up to 250 km/h
  Large cell radii of up to 100 km
  Resource allocation for dedicated MBMS network
  Multicast/Broadcast network sharing between multiple MNOs
  Efficient multiplexing with unicast transmission in frequency and time domain
TR 22.261 (Service requirement for 5G system)
  UHD content delivery
Maintain forward compatibility
  NR Phase 1 and NR Phase 2
NR Requirement
Need to study the technical solutions for satisfying those requirements

## Slide 4: Study Item on MBMS for NR
NR MBMS Numerology
Advanced Tech for
Capacity Increase
Forward Compatibility
Numerology
  Extended CP
  Subcarrier spacing
Frame structure
Consideration of features of
LTE-based eMBMS/FeMBMS
Multiple antenna techniques
Advanced modulation techniques
Superposition transmission
Integrated system performance
evaluation
Flexible time and/or frequency
resource allocation
Up to
100km
Up to
250 km/h
HD
UHD
NR
Immersive
LTE
MBMS
NR
Phase 1
NR
Phase 2
eMBB
mMTC
URLLC

## Slide 5: Study Item on MBMS for NR (details)
The following should be included in the study item scope
  Study NR MBMS numerology to fulfill NR MBMS requirements specified in TR 38.913
    Subcarrier spacing to support high mobility of up to 250km/h
    Extended cyclic prefix to support cell radii of up to 100km
  Study the feasibility of the advanced technologies to improve NR MBMS capacity
    Multiple antenna techniques (e.g. MIMO) for Multicast/Broadcast traffic channel
    Advanced modulation techniques (e.g. Non-Uniform Constellation)
    Superposition transmission techniques for Multicast/Broadcast traffic channel
    Impact of advanced techniques above – but not limited to – in conjunction with techniques agreed in NR Phase 1 (e.g. LDPC codes)
  Study mechanisms to support dedicated MBMS network and network sharing between multiple MNOs
  Study the techniques to maintain forward compatibility of NR MBMS
    Flexible time and/or frequency resource allocation for NR MBMS