## Slide 1
3GPP TSG RAN Meeting #77
Sapporo, Japan, September 11 - 14, 2017
RP-171810
Source: Samsung, ZTE, CATT
Title: Motivation for new WI: Enhancements on
MIMO for NR
Document for: Discussion
Agenda Item: 9.1

## Slide 2: Background: Phase I NR MIMO
Expected key features
  DL and UL TX schemes: DMRS-based precoding and diversity, dynamic switching
  Limited support for multi-TRP/panel
  Modular CSI acquisition including Beam Management
  Type I (low resolution) and II (high resolution) CSI: 2 to 32 antenna ports
  Flexible RS: DMRS, CSI-RS, SRS, …
Key differentiation from LTE:
  Type II CSI: at least 30% average TP gain over LTE Rel.14 (eFD-MIMO)
  Modular CSI acquisition & flexible RS  scalable to, e.g. multi-TRP/panel
  Accommodate high-frequency (>6GHz) operation
Phase I will be finalized in Dec 2017 (basic MIMO functionalities)
  Unrealized/latent MIMO potentials in Phase I  Need to be unlocked in Phase II

## Slide 3: Timeline and items of interest
Approximately 21-month WI, including proposals to:
  Support: Specify proposed features
  Study: Evaluate/study and, if needed, specify proposed features
Phase II WI includes the following items:
  Enhanced Type II CSI
  Enhanced multi-TRP/panel support
  Enhanced high-frequency support
  Enhanced DL-UL channel reciprocity support (both DL and UL transmissions)
  Miscellaneous enhancement
2018-03
2018-06
2018-09
2018-12
2017-12
Phase II MIMO WI started in RAN1
Phase II MIMO WI endorsed
Planned RAN1 meetings
Planned RAN meetings
Phase II MIMO WI Core completed in RAN1/2/4
Phase II MIMO WI completed in RAN1
2019-03
2019-06
2019-09

## Slide 4: Enhanced Type II CSI
Type II CSI is the most promising feature of NR MIMO in terms of NW performance
  The only feature offering large TP gain over LTE under the same scenario
  “Long” term extension to achieve near-ideal CSI performance
Phase I most likely supports Cat1 with L=2, 3, 4 and rank 1-2
  Cat3 (hybrid) is naturally supported
  Facilitate explicit feedback: major TP gain over Rel.14 LTE (at least ~30%) …
  … but significant gap from near-ideal CSI
Possible enhancements:
  Support Cat1 L>4 with differential reporting (to distribute reporting payload)
  Support Cat1 with rank 3-4 support (for UE capable of 8RX and light NW loading)
  Study “Cat1+” utilizing spatial feedback compression scheme
  Study Cat2 (covariance matrix)

## Slide 5: Enhanced Type II CSI
Schemes
16 ports, (N1,N2) = (2,4), UMi, 50% RU, Rank 2
 | Scheme | #coefficients (9 SBs) | Per layer compression
Adv. CSI CB | L = 2 beams | 9*3 = 27 | 0.19
Type II, Cat 1 | L = 4 beams | 9*7 = 63 | 0.44
 | L = 8 beams | 9*15 = 135 | 0.94
Principal component analysis (PCA) | d = 2 principal components | (9+16)*2 = 50 | 0.35
 | d = 4 principal components | (9+16)*4 = 100 | 0.69
Ideal | Un-quantized eigenvectors | 9*16 = 144 | 1 (uncompressed)
Chart: 
| Avg. UPT | 5% UPT | Per layer compression
R14 Adv. CSI | 1 | 1 | 0.19
Type II, Cat 1, L = 4 | 1.4318 | 1.9227 | 0.44
Type II, Cat 1, L = 8 | 1.5688 | 2.2236 | 0.94
PCA, d = 2 | 1.64 | 2.43 | 0.35
PCA, d = 4 | 1.72 | 2.5 | 0.69
Ideal | 1.738 | 2.526 | 1
Gain w.r.t Rel. 14 Adv. CSI
Compression (#SB coefficients))
w.r.t to ideal
PCA, d=2, the best in terms of
performance gain and compression

## Slide 6: Enhanced multi-TRP/panel support
Requirement for enhanced multi-TRP/panel support
  Scalable: facilitate natural extension to >=2 transmit/receive points
  Flexible: applicable for various operations, e.g. coherent/non-coherent, UL/DL, indoor/outdoor, joint transmission/coordinated beamforming/point selection
Phase I most likely supports the following
  Type I multi-TRP/panel CSI (co-phase) for coherent JT
  Multi-assignment (multi-DCI) reception for non-coherent JT
Possible enhancements – transmission:
  Support DL/UL single-assignment for non-coherent JT using two-level DL control (e.g. “two-level DCI”)
  Study multi-TRP/panel operation for control channel(s)

## Slide 7: Enhanced multi-TRP/panel support
Possible enhancements – reporting:
  Support beam reporting (multi-TRP/panel context) schemes considering not only channel, but also interference measurement and/or transmission schemes
  Study enhanced codebooks for DL/UL multi-panel scenarios
    UL multi-panel codebooks: panel/port selection or combination
    Differential/multi-level DL codebooks (progressive refinement of spatial resolution)

## Slide 8: Enhanced high-frequency support
Phase I most likely supports the following
  Scenarios for up to 40GHz
  DL and UL beam management based on SS block and CSI-RS/SRS
  Context for >40 GHz:
    5G V2X may operate @63-64GHz and 76-81GHz
    Fully analog architecture (as opposed to hybrid) is more commonly used
Possible enhancements
  Study optimization for DL/UL beam management for >40GHz
    How Phase I UL/DL beam management can be extended/scaled to address this scenario
  Study SC-FDMA-based DL/UL transmission for >40GHz
    Single-layer or low-order DL/UL MIMO (e.g. 2-layer)

## Slide 9: Enhanced DL-UL channel reciprocity support
Phase I most likely supports the following
  Limited spec feature (if any) to facilitate SRS usage for DL CSI acquisition and CSI-RS usage for UL CSI acquisition
Possible enhancements [depending on Phase I outcome]
  Study interference feedback
  Study DL CSI acquisition based on SRS and UL CSI acquisition based on CSI-RS (e.g. DL control signaling, joint triggering)
  Study transmission scheme for partial reciprocity scenarios
  Study verification of channel reciprocity accuracy for beam correspondence

## Slide 10: Miscellaneous Enhancement
UL MIMO:
  Phase I most likely supports basic codebook-based UL SU-MIMO (cf. Rel.10 LTE) and max SRS ports per resource = 4
  Possible enhancements [depending on Phase I outcome]
    Support enhancement on UL frequency selective precoding based on, e.g. two-level DL control signaling
    Support larger number of SRS ports per resource, e.g. [8]
    Study UL Tx diversity scheme for DFT-S-OFDM
RS efficiency:
  Study CSI-RS and DMRS overhead reduction via, e.g. pattern sub-sampling, non-orthogonal multiplexing, resource sharing between DMRS and CSI-RS, time-domain bundling/aggregation