## Slide 1: On support of dual UL and single UL transmission Source: Orange
RP-171876
3GPP TSG RAN meeting #77
Sapporo, Japan, September 11 - 14, 2017
Agenda Item: 9.2.1

## Slide 2: Background scenarios
Three different deployment scenarios were presented in R1-1711817 for UL coverage extension of TDD @3.5GHz

## Slide 3: Need for support of both dual UL and single UL transmission
Need for Dual UL transmission
End use throughput and latency performance is critical, and will be better served with independent scheduling of LTE and NR.
For LTE – NR band combinations when no MSD degradation is experienced and UL power not restricted by cell edge, dual UL transmission gives better performance than single UL transmission
Need for Single UL transmission
For very specific frequency allocations within LTE – NR band combinations, REFSENS degradation may be experienced due to IMD issues when dual UL transmission is used
At cell edge, UL power restriction may lead to coverage limitation when dual UL transmission is used
For both above cases, single UL transmission can be a solution

## Slide 4: Proposal
Dual UL transmission is mandatory and supported by the UE for all LTE – NR band combinations
Single UL transmission is also mandatory and supported by the UE for all LTE – NR band combinations with the condition that a switch mechanism between Dual UL and Single UL is implemented, based on L3 messages and controlled by the network.
Triggers for the switch between dual UL and single UL transmission should be restricted to cases with severe MSD (to be advised by RAN4 analysis) for specific band combinations, and coverage extension to allow NR (or LTE) to use the full power for its uplink transmission